## Slide 1: Embedded Computer Architecture 5SAI0 Introduction
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2016-2017

## Slide 2: Lecture overview
Trends
  Performance increase
  Technology factors
Computing classes
Cost
Performance measurement
  Benchmarks
  Metrics
Dependability

## Slide 3: Trends
See the ITRS (International Technology Roadmap Semiconductors)
http://public.itrs.net/

## Slide 4: Performance of (single) processors

## Slide 5: Frequency development of processors

## Slide 6: Where has Performance Improvement come from?
Technology
  More transistors per chip
  Faster logic
Machine Organization/Implementation
  Deeper pipelines
  More instructions executed in parallel
Instruction Set Architecture
  Reduced Instruction Set Computers (RISC > 1985)
  Multimedia extensions
  Explicit parallelism
Compiler technology (lecture 5LIM0)
  Finding more parallelism in code
  Greater levels of optimization

## Slide 7: ENIAC: Electronic Numerical Integrator And Computer, 1946

## Slide 8: VLSI Developments: Technology Improvement
1946: ENIAC electronic numerical integrator and computer
Floor area
  140 m2
Performance
  multiplication of two 10-digit numbers in 2 ms
Power
  160 KWatt
2016: High Performance microprocessor
Chip area
  100-400 mm2 (for multi-core)
Board area
  200 cm2; improvement of 104
Performance:
  64-bit multiply in O(1 ns); improvement of 106
Power
  20 Watt; improvement 8000
On top
  architectural improvements, like ILP exploitation
  extreme cost reduction

## Slide 9
CMOS improvements:
Transistor density: 4x / 3 yrs
Die size: 10% / yr

## Slide 10: Evolution of memory granularity
From SSCS by Randall D. Isaac

## Slide 11: PC hard drive capacity

## Slide 12: Latency Lags Bandwidth (last ~20 years)
Performance Milestones
Processor: ‘286, ‘386, ‘486, Pentium, Pentium Pro, Pentium 4 (21x,2250x)
Ethernet: 10Mb, 100Mb, 1000Mb, 10000 Mb/s (16x,1000x)
Memory Module: 16bit plain DRAM, Page Mode DRAM, 32b, 64b, SDRAM, DDR SDRAM (4x,120x)
Disk : 3600, 5400, 7200, 10000, 15000 RPM (8x, 143x)
CPU high,
Memory low (“Memory Wall”)
Notes: Processor: 2250X, 22X Latency

## Slide 13: Technology Trends: Capacity vs Speed (Summary)
Capacity Speed (latency)
Logic 2x in 3 years 2x in 3 years
DRAM 4x in 3 years 2x in 10 years
Disk 4x in 3 years 2x in 10 years

## Slide 14: 8” MIPS64 R20K wafer (564 dies)
Drawing single-crystal Si ingot from furnace….
Then, slice into wafers and pattern it…

## Slide 15: What's the price of an IC ?
Die cost + Testing cost + Packaging cost
Final test yield
Final test yield = fraction of packaged dies which pass the final testing state
IC cost =

## Slide 16: Integrated Circuits Costs
IC cost = Die cost + Testing cost + Packaging cost
Final test yield
Die cost = Wafer cost
Dies per Wafer * Die yield
Final test yield: fraction of packaged dies which pass the final testing state
Die yield: fraction of good dies on a wafer

## Slide 17: What's the price of the final product ?
Component Costs
Direct Costs (add 25% to 40%)
  recurring costs: labor, purchasing, warranty
Gross Margin (add 82% to 186%)
  nonrecurring costs: R&D, marketing, sales, equipment maintenance, rental, financing cost, pretax profits, taxes
Average Discount to get List Price (add 33% to 66%):
  volume discounts and/or retailer markup
Component
Cost
Direct Cost
Gross
Margin
Average
Discount
Avg. Selling Price
List Price
15% to 33%
6% to 8%
34% to 39%
25% to 40%

## Slide 18: Quantitative Principles of Design
Take Advantage of Parallelism
Principle of Locality
Focus on the Common Case
  Amdahl’s Law, or
  Gustafson's Law
  E.g. common case supported by special hardware; uncommon cases in software
The Performance Equation

## Slide 19: 1. Parallelism
How to improve performance?
(Super)-pipelining
Powerful instructions
  MD-technique
    multiple data operands per operation
  MO-technique
    multiple operations per instruction
Multiple instruction issue
  single instruction-program stream
  multiple streams (or programs, or tasks)

## Slide 20: Pipelined Instruction Execution
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5

## Slide 21: Limits to pipelining
Hazards prevent next instruction from executing during its designated clock cycle
  Structural hazards: Use same hardware to do two different things at once
  Data hazards: Instruction depends on result of prior instruction still in the pipeline
  Control hazards: Caused by delay between the fetching of instructions and decisions about changes in control flow (branches and jumps).
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 22: 2. The Principle of Locality
Programs access a relatively small portion of the address space at any instant of time
Two Different Types of Locality:
  Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon (e.g., instruction loops, data reuse)
  Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon (e.g., straight-line code, array access)
Last 30 years, HW relied on locality for memory perf.
Proc.
Memory
$
Notes: The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
This is kind of like in real life, we all have a lot of friends. But at any given time most of us can only keep in touch with a small group of them.
There are two different types of locality: Temporal and Spatial. Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
This is like saying if you just talk to one of your friends, it is likely that you will talk to him or her again soon.
This makes sense. For example, if you just have lunch with a friend, you may say, let’s go to the ball game this Sunday. So you will talk to him again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon.
Once again, using our analogy. We can usually divide our friends into groups. Like friends from high school, friends from work, friends from home.
Let’s say you just talk to one of your friends from high school and she may say something like: “So did you hear so and so just won the lottery.”
You probably will say NO, I better give him a call and find out more.
So this is an example of spatial locality. You just talked to a friend from your high school days. As a result, you end up talking to another high school friend. Or at least in this case, you hope he still remember you are his friend.
+3 = 10 min. (X:50)

## Slide 23: Memory Hierarchy Levels
CPU Registers
100s Bytes
300 – 500 ps (0.3-0.5 ns)
L1 and L2 Cache
10s-100s K Bytes
~1 ns - ~10 ns
~ $100s/ GByte
Main Memory
many G Bytes
80ns- 200ns
~ $10/ GByte
Disk
10s T Bytes, 10 ms (10,000,000 ns)
~ $0.1 / GByte
Capacity
Access Time
Cost
Tape
infinite
sec-min
~$0.1 / GByte
Registers
L1 Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Xfer Unit
prog./compiler
1-32 bytes
cache cntl
32-64 bytes
OS
4K-8K bytes
user/operator
Gbytes
Upper Level
Lower Level
faster
Larger
L2 Cache
cache cntl
64-128 bytes
Blocks
still needed?

## Slide 24: 3. Focus on the Common Case
Favor the frequent case over the infrequent case
  E.g., Instruction fetch and decode unit used more frequently than multiplier, so optimize it first
  E.g., If database server has 50 disks / processor, storage dependability dominates system dependability, so optimize it first
Frequent case is often simpler and can be done faster than the infrequent case
  E.g., overflow is rare when adding 2 numbers, so improve performance by optimizing more common case of no overflow
  May slow down overflow, but overall performance improved by optimizing for the normal case
What is frequent case? How much performance improved by making case faster? => Amdahl’s Law

## Slide 25: Amdahl’s Law
Speedupoverall =
Texec,old
Texec,new
=
1
(1 - fparallel) + fparallel
Speedupparallel
exc. time
serial part
parallel part
serial part
fparallel= parallel fraction

## Slide 26: Amdahl’s Law: exercise
Floating point instructions improved to run 2 times faster, but only 10% of actual instructions are FP
Speedupoverall
=
Texec,new =

## Slide 27: Amdahl’s Law
Floating point instructions improved to run 2 times faster; but only 10% of actual instructions are FP
Speedupoverall
=
1
0.95
=
1.053
Texec,new = Texec,old x (0.9 + 0.1/2) = 0.95 x Texec,old

## Slide 28: Amdahl's law

## Slide 29: Gustafson's law
Gustafson proposed a change to Amdahl's law
He assumes the data (input) set for the parallel part scales (increases) linearly with the number of processors => much better scaling
Speedup = P - fseq(P-1) where P = # of processors (parallel speedup), fseq = sequential fraction of the original program

## Slide 30: Gustafson's law

## Slide 31: 4. The performance equation
Main performance metric:
Total Execution Time
Texec = Ncycles * Tcycle
= Ninstructions * CPI * Tcycle
  CPI = (Average number of) Cycles Per Instruction
  IPC = ....

## Slide 32: Example: Calculating CPI
Typical Mix
Base Machine (Reg / Reg)
Op Freq Cycles CPI(i) (% Time)
ALU 50% 1 .5 (33%)
Load 20% 2 .4 (27%)
Store 10% 2 .2 (13%)
Branch 20% 2 .4 (27%)
1.5

## Slide 33: Measurement Tools
Benchmarks, Traces, Mixes
Hardware: Cost, delay, area, power estimation
Simulation (many levels, see ch. 9)
  ISA, RT, Gate, Circuit level
Queuing Theory (analytic models)
Rules of Thumb
Fundamental “Laws”/Principles

## Slide 34: Aspects of CPU Performance what influences what?
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
Instr. Cnt CPI Clock Rate
Program
Compiler
Instr. Set
Organization
Technology

## Slide 35: Aspects of CPU Performance check the ‘x’
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
Inst Count CPI Clock Rate
Program X X
Compiler X X
Inst. Set. X X
Organization X X
Technology X

## Slide 36: Marketing Metrics
MIPS =Instruction Count / (Time * 10^6) = (Frequency / CPI) / 10^6
  Not effective for machines with different instruction sets
  Not effective for programs with different instruction mixes
  Uncorrelated with performance
MFLOPs = (FP Operations / Time) / 10^6
  Machine dependent
  Often not where time is spent
Peak - maximum able to achieve
Average - for a set of benchmarks
Relative - compared to another platform
Normalized MFLOPS:
  add,sub,compare,mult 1
  divide, sqrt 4
  exp, sin, . . . 8

## Slide 37: Programs to Evaluate Processor Performance
(Toy) Benchmarks
  10-100 line program
  e.g.: sieve, puzzle, quicksort
Synthetic Benchmarks
  Attempt to match average frequencies of real workloads
  e.g., Whetstone, Dhrystone
Kernels
  Time critical excerpts
Real Benchmarks

## Slide 38: Benchmarks
Benchmark mistakes
  Only average behavior represented in test workload
  Loading level controlled inappropriately
  Caching effects ignored
  Ignoring monitoring overhead
  Not ensuring same initial conditions
  Collecting too much data but doing too little analysis
Benchmark tricks
  Compiler (soft)wired to optimize the workload
  Very small benchmarks used
  Benchmarks manually translated to optimize performance

## Slide 39: SPEC benchmarks, since 1989
CPU: CPU2006
  CINT2006 and CFP2006
Graphics: SPECviewperf12 e.o.
HPC/OMP: HPC2002; OMP2001, MPI2006
Java Client/Server: jAppServer2004
Java runtime: SPECjvm2008
Mail Servers: MAIL2001
Network File System: SDS97_R1
Power: under development
Web Servers: WEB2005
Handheld: under development
Cloud: SPEC Cloud_laaS 2016
see for updates: www.spec.org

## Slide 40: SPEC benchmarks

## Slide 41: How to Summarize Performance?
Arithmetic mean (weighted arithmetic mean) tracks execution time: (Ti)/n or (Wi*Ti)
Normalized execution time is handy for scaling performance (e.g., X times faster than VAX-780)
But do not take the arithmetic mean of normalized execution time, but use the geometric mean: (i ratioi)1/n

## Slide 42: Summarize performance: example
Geometric means of speedups
    Mean speedup comparisons between two machines are independent of the reference machine
 | Program A | Program B | Arithmetic Mean | Speedup (ref 1) | Speedup (ref 2)
Machine 1 | 10 sec | 100 sec | 55 sec | 91.8 | 10
Machine 2 | 1 sec | 200 sec | 100.5 sec | 50.2 | 5.5
Reference 1 | 100 sec | 10000 sec | 5050 sec |  | 
Reference 2 | 100 sec | 1000 sec | 550 sec |  | 
 |  | Program A | Program B | Arithmetic | Harmonic | Geometric
Wrt Reference 1 | Machine 1 | 10 | 100 | 55 | 18.2 | 31.6
 | Machine 2 | 100 | 50 | 75 | 66.7 | 70.7
Wrt Reference 2 | Machine 1 | 10 | 10 | 10 | 10 | 10
 | Machine 2 | 100 | 5 | 52.5 | 9.5 | 22.4
Speedup

## Slide 43: Computer Architecture Topics
Instruction Set Architecture
Pipelining, Hazard Resolution,
Superscalar, Reordering,
Prediction, Speculation,
Vector, DSP
Addressing,
Protection,
Exception Handling
L1 Cache
L2 Cache
DRAM
Disks, WORM, Tape
Coherence,
Bandwidth,
Latency
Emerging Technologies
Interleaving
Bus protocols
RAID
VLSI
Input/Output and Storage
Memory
Hierarchy
Pipelining and Instruction
Level Parallelism

## Slide 44: Computer Architecture Topics
M
Interconnection Network
S
P
M
P
M
P
M
P
° ° °
Topologies,
Routing,
Bandwidth,
Latency,
Dependability /
Reliability
Network Interfaces
Programming model
Shared Memory,
Message Passing,
Data Parallelism
Processor-Memory-Switch
Multiprocessors
Networks and Interconnections

## Slide 45: Dependability
MTTF: mean time between failure (in hours)
MTTR: mean time to repair (in hours)
Availability = MTTF / (MTTF + MTTR)
FIT: failures in time (per 1 billion hours)
Example
  MTTF = 1,000,000 hours
  FIT = 109 / MTTF = 1000 failures per billion hours

## Slide 46: Dependability of a Disk subsystem
10 disks MTTF = 1,000,000 hours
1 Disk controller MTTF = 500,000
1 power-supply MTTF = 200,000
1 fan MTTF = 200,000
1 Disk cable MTTF = 1,000,000
What is MTTF of this subsystem?
  assuming lifetimes exp. distributed &
  independent failures
FIT = Σi FITi = 109 * {10 *1/106 + 1/(5.105) + .. } = 23000 failures / billion hours
MTTF = 1/FIT = 109 hours / 23000 = 43,500 hours

## Slide 47: Dependability: let's use redundancy
Two powersupplies, each MTTF = 200,000 hour and MTTR = 1 day
What is the MTTF of the combined power supply?
On average the first disk fails in MTTF/2 = 100,000 hours
During repair second failure with probability p = MTTR / MTTF = 24/200,000
MTTFpair = 100,000/p = 830,000,000 hours

## Slide 48: What is Ahead?
Bigger caches.
  More levels of cache? Software controlled caches / scratchpad
Greater instruction level parallelism?
Increased exploiting data level parallelism:
  Vector and Subword parallel processing, bigger GPUs
Exploiting task level parallelism: Multiple processor cores per chip; how many are needed?
  Bus based communication, or
  Networks-on-Chip (NoC)
Complete MP Systems on Chip: platforms
Compute servers & Cloud computing

## Slide 49: Intel Dunnington 6-core

## Slide 50: AMD Hydra 8 core
45 nm
L2: 1MByte/core
L3: shared 6MByte

## Slide 51: Intel Xeon Phi
latest version (2015): Knights Landing
build on Silvermont (Atom) x86 cores
with 512-bit (SIMD) AVX units
up to 72 cores / chip => 3 TeraFlops
14 nm
using Micron’s DRAM 3D techn. (hybrid memory cube)

## Slide 52: Tianhe-2: nr 2 in 2016 (top500.org)
3.120.000 cores
33.86 PetaFlop (on Linpack benchmark)
17.8 MegaWatt

## Slide 53
summarize what you learned