## Slide 1: Embedded Computer Architecture 5SAI0 Multi-Processor Systems
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2016-2017

## Slide 2: Welcome back
Multi-Processors
Shared memory architectures
  symmetric
  distributed
Message passing architectures
Programming model
Material:
  Book Chapter 5-5.4.1

## Slide 3: Should we go Multi-Processing?
Diminishing returns for exploiting ILP
  limited Instruction Level Parallelism costly to exploit
Power issues
Wiring issues (faster transistors do not help that much)
More vector and task-level parallel applications
Multi-core architectures hit all markets (even embedded)
  lower energy (due to same performance with lower Vdd)
  silicon technology still scales => abundance of transistors

## Slide 4
Trends:
#transistors follows Moore
but not freq. and performance/core
Core i7
3GHz
100W
5
Next?

## Slide 5: Intel’s 72-core ‘Knight’s Landing’ XEON Phi
- 14 nm
3D Tri-gate transistors
3 TFlops double / 6 TFlops single precision
512-bit SIMD/Vector processing per core

## Slide 6: Intel’s 72-core ‘Knight’s Landing’ XEON Phi

## Slide 7: Multi-core Architecture
Parallel / Multi-core Architecture extends traditional computer architecture with a communication network
  abstractions (HW/SW interface)
  organizational structure to realize abstraction efficiently
Communication Network
Processing
node
Processing
node
Processing
node
Processing
node
Processing
node
Memory
I/O

## Slide 8: Parallel programming models
How parallel computations can be expressed in a high-level language?
  Simple extensions through an API (application-programming interface) of common programming languages such as C/C++ or FORTRAN:
    Shared-memory: OpenMP or Pthreads
    Message-passing: MPI (message-passing interface)
  Parallelizing compilers translate a sequential program into parallel threads
Threads or processes must communicate and coordinate their activity (synchronization)

## Slide 9: Data vs function parallelism
Data parallelism:
  Partition the data set
  Apply the same function to each partition
  SPMD (= single program multiple data)
    SPMD ≠ SIMD; what's the difference?
  Massive parallelism
Function (Task-level) parallelism
  Independent functions are executed on different processors
  E.G.: Streaming--software pipeline
  More complex, limited parallelism
Combine both: function + data parallelism

## Slide 10: Communication models: Shared Memory
Process P1
Process P2
Shared
Memory
Coherence problem
Memory consistency issue
Synchronization problem
(read, write)
(read, write)

## Slide 11: Shared memory multiprocessors: Types
Shared memory multi-processors
  all memory addresses visible by every processor
  communication by loads and stores
2 Types:
a. Symmetric multiprocessors (SMP)
  Small number of cores
  Share single memory with uniform memory latency

## Slide 12: Shared memory multiprocessors: Types
b. Distributed shared memory (DSM)
  Memory distributed among processors
  Non-uniform memory access/latency (NUMA)
  Processors connected via direct (switched) and non-direct (multi-hop) interconnection networks

## Slide 13: 4 Cache organizations for SMPs
Rest of discussion considers organization (c) and (d)

## Slide 14: Example: matrix multiply + sum
Sequential program:
1 sum = 0;
2 for (i=0,i<n, i++)
3 for (j=0,j<n, j++){
4 C[i,j] = 0;
5 for (k=0,k<n, k++)
6 C[i,j] = C[i,j] + A[i,k]*A[k,j];
7 sum += C[i,j];
8 }
- Multiply A[n,n] by B[n,n] and store result in C[n,n]
- Add all elements of matrix C

## Slide 15: Shared mem: matrix multiply + sum
/* A, B, C, bar, lv and sum are shared, all others are private
*/
1a low = pid*n/nproc; /pid=0...Nproc-1
1b hi = low + n/nproc; /each proc sums rows
1c mysum = 0; sum = 0; /low to hi
2 for (i=low,i<hi, i++)
3 for (j=0,j<n, j++){
4 C[i,j] = 0;
5 for (k=0,k<n, k++)
6 C[i,j] = C[i,j] + A[i,k]*B[k,j];
7 mysum +=C[i,j]; /C summed in shared memory
8 }
9 barrier(bar);
10 lock(lv);
sum += mysum;
unlock(lv);

## Slide 16: Why Mutual Exclusion?
Assume the following statements are executed by 2 threads, T1 and T2, on sum
T1 T2
sum<- sum+1 sum<- sum+1
Compiled code on a RISC machine includes several instructions
A possible interleaving of execution is:
T1 T2
r1 <- sum
R1 <- sum
r1 <- r1 + 1
r1 <- r1 + 1
sum <- r1
sum <- r1
At the end the result is that sum is incremented by 1 (not 2)

## Slide 17: Communication models: Message Passing
Communication primitives
  e.g., send, receive library calls
  standard MPI: Message Passing Interface
    www.mpi-forum.org
Note that MP can be build on top of SM and vice versa !
Process P1
Process P2
receive
receive
send
send
FiFO

## Slide 18: Message Passing Model
Explicit message send and receive operations:
  Send specifies local buffer + receiving process on remote computer
  Receive specifies sending process on remote computer + local buffer to place data
Typically blocking communication, but may use DMA
  DMA = Direct Memory Access (check this out!)
Header
Data
Trailer
Message structure

## Slide 19: Message passing communication
Interconnection Network
Network
interface
Network
interface
Network
interface
Network
interface
Cache
Processor
Memory
DMA
Cache
Processor
Memory
DMA
Cache
Processor
Memory
DMA
Cache
Processor
Memory
DMA

## Slide 20: Synchronous message-passing
Thread T1: Thread T2:
a = 10; b = 5;
send(&a,sizeof(a),t2,send_a); recv(&b,sizeof(b),t1,send_a);
a = a+1; b=b+1;
recv(&a,sizeof(c),t2,send_b); send(&b,sizeof(b),t1,send_b);
printf(a);
Each send/recv has 4 operands:
  Starting address in memory
  Size of message
  Destination/source thread id
  Tag connecting sends and receives
Synchronous communication = sender blocks until recv is completed and receiver blocks until message has been sent
What is the value printed under synchronous MP?
Tag, not really
needed; why not?

## Slide 21: Message-passing: matrix multiply + sum

## Slide 22: Synchronous message-passing
Advantage:
  Communication protocol enforces synchronization
Disadvantages:
  Prone to deadlock
  Block threads: no overlap of communication with computation
Deadlock example:
thread T1: thread T2:
a = 10; b = 5;
send(&a,sizeof(a),t2,send_a); send(&b,sizeof(b),t1,send_b)
recv(&c,sizeof(c),t2,send_b); recv(&d,sizeof(d),t1,send_a);
To eliminate the deadlock: swap the send/recv pair in T2
Or employ asynchronous message-passing

## Slide 23: (A)Synchronous message-passing
thread T1: thread T2:
a = 10; b = 5;
asend(&a,sizeof(a),t2,send_a); asend(&b,sizeof(b),t1,send_b);
<unrelated computation;> <unrelated computation;>
srecv(&b,sizeof(b),t2,send_b); srecv(&a,sizeof(b),t1,send_a);

## Slide 24: (A)Synchronous message-passing
In general multiple threads are running on a core
This handshake is for synchronous message passing
Can also be applied to blocking or non-blocking asynchronous
  Sender continues after send (a) and receiver after recv (b)
    If blocking, sender must make a copy of message first

## Slide 25: Support for message passing protocols
Data must be copied from/to memory to/from NI (NW interf.)
  Processor could do it
  DMA (direct memory access) can speed up message transfers and off-load the processor
  DMA is programmed by the processor;
    Start address and size
Dedicated message processors
  Use a special processor to process messages on both ends
  Thus relieving the compute O/S from doing it
Support for user-level messages
  Basic message passing systems drive DMA engine from OS
    This is needed for protection between users
  Message is first copied into system space and then into user space (receive)
  Message is copied from user space to system space (send)
  Tag user messages so that they are picked up and delivered directly in user memory space (zero copy)

## Slide 26: Message-passing support

## Slide 27: Communication Models: Comparison
Shared-Memory (used by e.g. OpenMP)
  Compatibility with well-understood (language) mechanisms
  Ease of programming for complex or dynamic communications patterns
  Shared-memory applications; sharing of large data structures
  Efficient for small items
  Supports hardware caching
Messaging Passing (used by e.g. MPI)
  Simpler hardware
  Explicit communication
  Implicit synchronization (with any communication)
What do you prefer?

## Slide 28: Next: 3 fundamental issues for shared memory multiprocessors
Coherence, about: Do I see the most recent data?
Consistency, about: When do I see a written value?
  e.g. do different processors see writes at the same time (w.r.t. other memory accesses)?
Synchronization How to synchronize processes?
  how to protect access to shared data?

## Slide 29: Concluding remarks
Number of transistors still scales well
However power/energy limits reached
Frequency not further increased
Therefore: After 2005 going Multi-Core
  exploiting task / thread level parallelism (TLP)
  can be combined with exploiting DLP (SIMD / Sub-word parallelism)
2 types of systems and programming models
  Shared memory
  Message passing
  What are the pros and cons of both systems?