Accelerators and reconfigurable architectures
Mark Wijtvliet
m.wijtvliet@tue.nl

---
General purpose processors
- Run mixed application types
  - Operating system
  - Webserver
  - Games
  - Office applications

---
General purpose processors
- Cheap
  - E.g. Raspberry Pi's Broadcom processor
  - Many others

---
General purpose processors
- They work great
- So why this accelerator talk?
[XKCD.com]

---
Example: mobile phones
- Typically a power budget of 1 Watt (1 J/Sec).
- Modern communication systems (4G) require 1000 GOPS
- That requires a compute efficiency of 1 pJ/OP
[Multicore for Mobile Phones, Kees van Berkel]

---
Example: mobile phones
- (Older) ARM11: 200 pJ/OP (65nm)
- A modern ARM, in 28nm
  - Scaling is 1/(S^2)
  - Should be around 37 pJ/OP
  - Numbers not public

---
General purpose processors
Why are general purpose processors not powerful and efficient enough?
[XKCD.com]

---
Inefficiencies in processors
[Understanding sources of inefficiency in General-Purpose Chips, Hameed et al.]

---
Inefficiencies in processors
- Factor 500 difference to ASIC in energy.
  - For H.264 encoding
  - For a 2.8 GHz Pentium 4 and a Tensilica Micro-processor.

---
Inefficiencies in processors
- Instruction fetching and decoding
- Communication (register file, caches, etc.)
- Hardware reconfiguration (in processor pipeline)

---
Instruction fetching and decoding
- Where does the overhead come from?
  - Addressing and loading the instruction word from memory.
  - Instruction caches.
  - Decoding the instruction to decoded instruction bits that control the processing pipeline.

---
Data transport
- Where does the overhead come from?
  - Register file access
    - How do processors reduce this?
  - Data caches
Multiply
Accumulate
[Speaker Notes: Meaning: bypassing and hazard introduction by doing so.]

---
Hardware reconfiguration
Mostly multiplexers in the datapath

---
General purpose processors
- Lessons learned:
  - Reduce instruction fetching and decoding
  - Reduce cycle-based hardware reconfiguration.
  - Reduce data transport to and from memories and RF.
  - Still needs to be programmable

---
Hardware acceleration

---
Static control
- Loops are the best candidate for static control
  - Do the same thing many times
A[0...N]
for i = 0 to N
A
B
C
B[0...N]
C[0...N]
CF

---
Static control
- Loops are the best candidate for static control
  - Do the same thing many times
- Software pipelining
A0
for i = 0 to N
A
B
C
A1
B0
A[2...N]
B[1...N-1]
C[0...N-2]
CF
B2
C1
C2

---
Static control
- However, this does not work on a general purpose processor...
  - Control is never static
A[0...N]
for i = 0 to N
A
CF

---
Static control
Not even for multi-cores
Core 1 Core 2 Core 3
A0
for i = 0 to N
A
B
C
A1
B0
A[2...N]
B[1...N-1]
C[0...N-2]
CF
CF
CF
B2
C1
C2

---
Static control
What type of processor would you use?
PE 1 PE 2 PE 3 PE 4
A0
for i = 0 to N
A
B
C
A1
B0
A[2...N]
B[1...N-1]
C[0...N-2]
CF
B2
C1
C2

---
Very Long Instruction Word processors (VLIW)
- Processor with multiple issue-slots
- One long instruction controlling them all

---
Very Long Instruction Word processors (VLIW)
If we have a 4-issue VLIW we can do our loop in a single cycle.
Slot 1 Slot 2 Slot 3 Slot 4
A0
for i = 0 to N
A
B
C
A1
B0
A[2...N]
B[1...N-1]
C[0...N-2]
CF
B2
C1
C2

---
Very Long Instruction Word processors (VLIW)
- But once the VLIW is manufactured the number (and functionality) of the issue slots is fixed.
- Problem ...
for i = 0 to N
A
B
C
D

---
Very Long Instruction Word processors (VLIW)
- The good:
  - Can achieve single-cycle loops
  - Programmability is OK.
- The bad:
  - Needs to have enough issue slots.
  - Too many issue slots result in wasted energy
  - Does little against data transport reduction
    - multiple multi-ported register files

---
ASICs
- The application is completely software pipelined and implemented ('hard coded') in hardware.
    - No more instruction fetching and decoding
    - But cannot be changed anymore after production
- But ASICs can do something about RF and memory accesses...

---
Spatial layout
Compute: (A+B) * 2
General purpose
VLIW
Spatial layout
RF
+
2
RF
*
Cycle N
Cycle N+1

---
Spatial layout
Compute: (A+B) * 2
General purpose
VLIW
Spatial layout
2
RF
RF
+
+
*
2
2
RF
RF
*
+
*
2 times the throughput!
Cycle N
Cycle N+1

---
Spatial layout
Compute: (A+B) * 2
General purpose
VLIW
Spatial layout
2
2
RF
RF
RF
+
+
+
*
*
2
2
2
RF
RF
RF
*
+
*
+
*
2 times the throughput!
2 times the throughput!
Cycle N
Cycle N+1

---
ASICs
- Very efficient
  - (Almost) no control
    - Some configuration registers
    - Fully software-pipelined hardware implementation
  - Reduce memory accesses
    - With spatial layout many register file (and memory) accesses can be avoided
- Very inflexible
  - Highly optimized for a very small application set

---
Reconfigurable hardware

---
Field Programmable Gate Arrays
What are FPGAs?

---
Field Programmable Gate Arrays
Chip full of configurable logic blocks/cells
[fpgacentral.com]

---
Field Programmable Gate Arrays
- What is in a logic block
  - Look-up tables
  - Full adder
  - Flip-Flop
  - Some multiplexers
[fpgacentral.com]

---
Field Programmable Gate Arrays
- Other blocks you find in FPGAs:
  - DSP blocks
  - Memory blocks (BRAMs)
  - Complete processor cores
[Intechopen.com]

---
Field Programmable Gate Arrays
- With the exception of specialized blocks most FPGAs contain one-bit blocks.
- Allows you to build arbitrary hardware
  - Like a box full of logic gates to build circuits.
- These blocks can be connected together via the interconnect.
[chipsetc.com]

---
Field Programmable Gate Arrays
- The interconnect on a FPGA is static:
  - Configured at application level (typically when you power-up the FPGA).
  - Connections are fixed after that
Switchbox

---
Field Programmable Gate Arrays
- Switch-boxes
  - As the name implies ...

---
Field Programmable Gate Arrays
- By configuring the interconnect and the logic blocks arbitrary (digital) circuits are possible.
- This allows for building specialized circuits that implement your algorithm with:
  - Spatial layout
  - Static control
  - Or a processor that runs software if you like to...

---
Field Programmable Gate Arrays
- Spatial mapping and static control
- Reconfigurable
- … no such thing as a free lunch ...

---
Spatial Layout in FPGA
FPGA Configures at gate level, which incurs large overheads:
  - Large configuration memory (SRAM leakage: high static power)
  - Complex routing network (many long wires: high dynamic power)
Image Source: www.ni.com

---
Field Programmable Gate Arrays
- Each configurable item has some configuration memory cells attached that configure it.
- Often several megabits
- Memory cells have leakage
- … Many cells have more leakage …
- Not trivial to program
[xkcd.com]

---
What have we learned so far?
Very efficient
Not flexible
ASIC
SIMD
VLIW
GPU
DSP
FPGA
CPU
Flexibility
Energy Efficiency

---
What have we learned so far?
Very efficient
Not flexible
ASIC
SIMD
Quite flexible
Low efficiency
Often lack performance.
VLIW
GPU
DSP
FPGA
CPU
Flexibility
Energy Efficiency

---
What have we learned so far?
Very efficient
Not flexible
ASIC
SIMD
Quite flexible
Low efficiency
Often lack performance.
VLIW
GPU
DSP
FPGA
CPU
Improve efficiency by giving up
some flexibility
More application specific
Flexibility
Energy Efficiency

---
What have we learned so far?
Very efficient
Not flexible
ASIC
SIMD
Quite flexible
Low efficiency
Often lack performance.
VLIW
GPU
DSP
FPGA
CPU
Improve efficiency by giving up
some flexibility
More application specific
More efficient due to spatial
layout
High static control cost
Flexibility
Energy Efficiency

---
Coarse Grained Reconfigurable Architecture

---
Signal processing domain
Signal conditioning
Feature extraction
Classification
FIR
IIR
Convolution (Windowing, 2D stencils)
Peak-suppression (Clipping)
Amplitude squaring
Sensor fusion, motion artifact reduction.
...
Support Vector Machine
(Convolutional) Neural Network
Linear Discriminant Analysis
Bayesian classifiers (Markov)
Nearest Neighbors
Combined (Boosting, Voting, Stacking)
Independent Component Analysis
...
Mean and Variance
FFT / DFT
Continuous Wavelet Transform
Discrete Wavelet Transform
Line length
Root Mean Square
Number of Maxima and Minima
Power Spectrum Density
Band Power
Derivative
Edge detection
...

---
Signal processing domain
Signal conditioning
Feature extraction
Classification
FIR
IIR
Convolution (Windowing, 2D stencils)
Peak-suppression (Clipping)
Amplitude squaring
Sensor fusion, motion artifact reduction.
...
Support Vector Machine
(Convolutional) Neural Network
Linear Discriminant Analysis
Bayesian classifiers (Markov)
Nearest Neighbors
Combined (Boosting, Voting, Stacking)
Independent Component Analysis
...
Mean and Variance
FFT / DFT
Continuous Wavelet Transform
Discrete Wavelet Transform
Line length
Root Mean Square
Number of Maxima and Minima
Power Spectrum Density
Band Power
Derivative
Edge detection
...
Wide range of algorithms!

---
Spatial Layout on the Cheap
Gate-level granularity is not required for the application domain.
What our architecture does:
  - Configure at functional unit level
  - Statically route data-path and control-path (spatial layout) but allow instructions.
A specialized FPGA to build processors

---
CGRA
Global data memory
Host
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Instruction
memory
IF
ID
LS
LS
LS
LS
LS
LS
IF
ID
FU
FU
FU
RF
FU
FU
IF
ID
FU
FU
FU
FU
RF
FU
IF
ID
FU
FU
FU
FU
RF
FU
IF
ID
FU
FU
FU
FU
RF
FU

---
SIMD construction
Global data memory
Host
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Instruction
memory
IF
ID
LS
LS
LS
LS
LS
LS
IF
ID
FU
FU
FU
RF
FU
FU
IF
ID
FU
FU
FU
FU
RF
FU
IF
ID
FU
FU
FU
FU
RF
FU
IF
ID
FU
FU
FU
FU
RF
FU

---
VLIW construction
Global data memory
Host
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Instruction
memory
IF
ID
LS
LS
LS
LS
LS
LS
IF
ID
FU
FU
FU
RF
FU
FU
IF
ID
FU
FU
FU
FU
RF
FU
IF
ID
FU
FU
FU
FU
RF
FU
IF
ID
FU
FU
FU
FU
RF
FU

---
Reconfigurable architectures
- Lower static control power than FPGA
  - Higher granularity means less control bits
  - Reconfiguration will be faster
- Can adapt better to the application than VLIW
  - Only use the number of issue slots really required
  - Support spatial mapping and single-cycle loops
  - Unused units can be switched off.
- High number of operations per cycle
  - But as much as possible: the same instruction

---
Switch-boxes
- Why do we save power compared to a FPGA?
- Routing a single wire through a FPGA switch-box:
= configuration memory

---
Switch-boxes
- Why do we save power compared to a FPGA?
- Routing a 4-wire bus through FPGA switch-boxes:
= configuration memory

---
Switch-boxes
- Why do we save power compared to a FPGA?
- Routing a 4-wire bus through a CGRA switch-box:
= configuration memory

---
Switch-boxes
- Why do we save power compared to a FPGA?
- CGRAs have fewer switch-boxes than FPGAs:
  - Coarse granularity means bigger building blocks, less interconnect required and buses only.
  - Coarser blocks also means that fewer blocks are required.
= configuration memory

---
Some results
- “So, how good is this CGRA?” I hear you say…
- Well, let’s compare it with
  - A VLIW: 8-issue slots
  - A SIMD: 8-lanes + scalar processor
  - ARM Cortex M0+, low-power microcontroller
  - CGRA without switch-boxes. Direct connections, essentially an application specific processor.
  - CGRA with switch-boxes, same design for all benchmarks. Contains worst-case resources of all benchmarks.

---
Execution time

---
Power

---
Energy

---
Some results
- What does this mean?
  - It is not bad if your design uses more power…
  - As long as the cycles get reduced more
    - (e.g. 50% more power, 33% less cycles → same energy)
  - Area is not shown here, experiments still ongoing
- You will get a energy/area prediction tool to use for your experiments
  - Less accurate but MUCH faster (minutes versus hours)
  - Performance is measured, and is accurate

---
How to build a processor
- The CGRA can be used to construct application specific processors at run-time.
- Several building blocks are available within the CGRA architecture.
- The building blocks can be interconnected using two networks:
  - Data network (between functional units)
  - Control network (between instruction decoders and functional units).

---
How to build a processor
Reconfigurable section

---
How to build a processor
IF
ID
- Instruction Fetch/Decode (IF/ID)
- Load Store Units (LSU)
- Register Files (RF)
- Memories (MEM)
- Functional Units (FU)
  - Add, subtract, bitlevel operations
  - Multiplication
  - Accumulator
  - …
- Switchboxes
LS
RF
MEM
FU

---
How to build a processor
Instruction
memory
IF
ID

---
How to build a processor
Instruction
memory
IF
ID
ABU

---
How to build a processor
Instruction
memory
IF
ID
ABU
Instruction
memory
IF
ID

---
How to build a processor
Instruction
memory
IF
ID
ABU
Instruction
memory
IF
ID
ALU

---
How to build a processor
Instruction
memory
IF
ID
ABU
Instruction
memory
IF
ID
ALU
ALU
ALU
ALU

---
How to build a processor
Instruction
memory
IF
ID
ABU
Instruction
memory
IF
ID
ALU
ALU
ALU
ALU
Instruction
memory
IF
ID
LSU
LSU
LSU
LSU

---
How to build a processor
Instruction
memory
IF
ID
ABU
Instruction
memory
IF
ID
ALU
ALU
ALU
ALU
Instruction
memory
IF
ID
LSU
LSU
LSU
LSU
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Global data memory

---
How to build a processor
Instruction
memory
IF
ID
ABU
Instruction
memory
IF
ID
ALU
ALU
ALU
ALU
Instruction
memory
IF
ID
LSU
LSU
LSU
LSU
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Global data memory

---
How to build a processor
- Architecture is specified with XML file
- Two versions:
  - Static: all connections are fixed at design time
  - Dynamic: connections can be configured at runtime
- The assignment will use the static version

---
Dynamic CGRA
- Connections can be changed at run-time
  - Very similar to FPGA
LS
LS
FU
FU
FU
FU

---
Dynamic CGRA
Green = data network
Blue = control network
Instruction
memory
IF
ID
ABU
Instruction
memory
IF
ID
ALU
ALU
ALU
ALU
Instruction
memory
IF
ID
LSU
LSU
LSU
LSU
Local
Mem.
Local
Mem.
Local
Mem.
Local
Mem.
Global data memory

---
Functional units
- As mentioned before, we have several:
  - ALU	Arithmetic Logic Unit
  - RF	Register File
  - LSU	Load-Store Unit
  - ABU	Accumulate Branch Unit
  - MUL	Multiplier
  - IU	Immediate Unit

---
Functional units
Most units have 4 inputs and 2 outputs
sourceA
sourceB
Output register(s)
destination
A
in0
in1
in2
in3
B
in0
in1
in2
in3

---
Functional units
- Source inputs and destination outputs specified in instruction.
- Instruction usually in the form:
  opcode dest, inA, inB
- Each output register is a source on the network.

---
Functional units
- Two highlighted Fus:
  - ABU, this unit can be used for both program counter generation and as an accumulator.
  - IU, the immediate unit can be used to generate constants on the data network.

---
Memory
- There are two memory ‘levels’
  - Global memory
  - Local memory

---
Memory
- The local memories are private to each LSU (meaning that one LSU can not read the local memory of another LSU)
- The data-bus is 32-bit wide and can perform a read AND write operation in a single cycle.
- Three data sizes are supported:
  - Byte
  - Half-word
  - Word

---
Memory
- The global memory is shared among all LSUs
- The data-bus is 32-bit wide and can perform a read OR a write. There is a few cycles latency on this bus (processor will stall).
- Any simultaneous reads and writes will be sequentialized, writes first.
- If multiple read or write requests can be coalesced they will be performed as one memory operation.

---
Memory
Coalesced read:
LSU
req: byte 0
LSU
req: byte 1
LSU
req: byte 2
LSU
req: byte 3
Arbiter
t=0	Req [0:3]

---
Memory
(Partially) un-coalesced read:
LSU
req: byte 0
LSU
req: byte 0
LSU
req: byte 4
LSU
req: byte 8
Arbiter
Note!
Requests to same
memory address are
 broadcast to all
 requesters
t=0	Req [0]
t=1	Req [4]
t=2	Req [8]

---
Memory
Similar for writes
LSU
write: byte 0
LSU
write: byte 0
LSU
req: byte 4
LSU
req: byte 5
Arbiter
Note!
Arbitrary order!
t=0	Write [0]
t=1	Write [0]
t=2	Write [4:5]

---
Using the CGRA
- Two things are required:
  - Architecture description
  - Program

---
Architecture description

---
Architecture description

---
Application
- We would liked to give you a compiler...
  - Still in development.
  - Works, but results not (yet) so efficient.
  - If you are interested in helping out with the compiler follow the 5LIM0 (Parallelism, Compilers, and Platforms) course and contact us!
- Programming is done in an assembler dialect
  - We call it PASM: Parallel Assembler

---
Application

---
Your assignment
- You will get a naive implementation for an edge detection algorithm.
- Your job is to make a trade-off between energy, area and performance

---
Your assignment
- You can:
  - Modify the architecture:
    - Implement data-level parallelism
    - Implement instruction-level parallelism
    - Use bypassing
    - Use other nice hardware features
  - Modify the application:
    - There are algorithm level optimizations possible
    - To make use of the architecture changes

---
Your assignment
- The assignment document will describe everything in more detail.
  - Additional documentation and files can be found on the Oncourse page for this course.
- Tools are available to make energy, area and performance estimates.

---
Your assignment
- You can either work on our servers
- Or work at your own laptop
  - Virtual machine with Linux and required tools
    - Be aware that the VM is (much) slower than the servers, not only because of ‘hardware’, but also because of the simulator license restricting speed.
  - Directly on your laptop, but Linux only
    - If you want to port it to Windows be our guest!

---
One more thing...
- This is a research architecture…
  - Bugs will be present.
  - You will be among the very first users.
  - We will reward the best bug with a Walhalla beer card.
    - Bugs should be reproducible.
    - Report bugs on the bugs section on the forum

---
Interested?
- We are always looking for good master students for:
  - Internships
  - Master projects
- In the fields of:
  - Silicon level optimizations (gates, transistors, ...)
  - Hardware development (Verilog, functional units, …)
  - Toolflow development (Compilers, place & route, …)
- Look at:
  - www.cgra.nl for some student projects
  - Welcome to discuss your own ideas!