## Slide 1: Embedded Computer Architecture 5SAI0 Technology
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2019-2020

## Slide 2: Impact of Technology (slides based on book: Parallel Computer Organization and Design)
Transistor basics
Power issues
  Dynamic
  Static
Reliability
  AVF
  ACE
  NBTI
  EM
  TDDB
  ... what is all of this?

## Slide 3: Transistor basics
Operation
Scaling issues
Inverter
Symbols for transistors
nMOS transistor

## Slide 4: pMOS and nMOS transistors
n+
n+
p
Body Si
Drain
Source
Gate
PolySilicon
SiO2
nMOS transistor
p+
p+
n
Body Si
Drain
Source
Gate
PolySilicon
SiO2
pMOS transistor
Symbols n/pMOS transistors
Combining nMos and pMOS transistor
- inverter with input A, output Y

## Slide 5: nMOS transistor operation
VG (gate voltage) controls current by changing the thickness of conduction channel:
  VGS < 0 then holes populate between source and drain
  VGS > Vth minority carriers (electrons) are attracted to the gate forming a conductive channel
  VDS > 0 leaves positive potential between drain and source and electrons move from source to drain
  VDS > Vth then IDS increases but VGD decreases; when VGD< Vth channel is pinched off

## Slide 6: Three regions of operation
Cut-off
VDS
VGS-Vth=VDS

## Slide 7: Three regions of operation
Cut-off/sub-threshold region
  VGS< Vth when no current flows
Linear region (acts as resistor)
  VGS> Vth & VGS > VDS + Vth
  IDS ~ β*(VGS - Vth)*VDS
    β is transistor gain factor = μ*Cox*(W/L), so β ~ W/L
Saturation region
  VGS> Vth & VGS > VDS + Vth
  IDS = (β/2)*(VGS - Vth)2
Cut-off

## Slide 8: Technology Scaling
Feature/Voltage | Variable
Channel Length | L
Channel Width | W
Oxide Thickness | tox
Junction Depth | X
Supply Voltage | Vdd
Threshold Voltage | Vth
Wire width Wire spacing Wire height | w s h
Dennard (ideal) scaling (till about 2006):
    All these features scale by 1/S
Gordon Moore’s Law (scaling factor S)
  S= every 2-3 years

## Slide 9: Impact of scaling on characteristics
Device Characteristics | Feature Dependence | Scaling
Transistor Gain (β) | W/(L. tox) | S
Current (Ids) | β(Vdd-Vth)2 | S
Resistance | Vdd/Ids | 1
Gate Capacitance | (W.L)/tox | 1/S
Gate delay | R.C | 1/S
Clock Frequency | 1/(R.C) | S
Circuit Area | W.L | 1/S2
Wire Resistance (per unit length) | 1/(w.h) | S2
Wire Capacitance (per unit length) | h/s | 1

## Slide 10: Benefits of scaling
Scaling dimensions with S= doubles device density
Frequency increases by 41%
Scaling (reducing) voltage simultaneously keeps the power constant
  P = α.f.C.V2 => scaling = S.S-1.S-2 = S-2 per transistor
  N transistors/area ~ S2
If voltage is not scaled then clock frequency can scale even faster but dynamic power grows!
Threshold voltage (down)scaling causes gate leakage power growth!
Note, for more details on MOSFET see: https://en.wikipedia.org/wiki/MOSFET

## Slide 11: CMOS inverter
pMOS
nMOS
Vin
Vout = Vin
Vdd
Vss = ground
Inverter Symbol
Vin
Vout

## Slide 12: CMOS inverter
Dynamic power is consumed when device changes ON->OFF and OFF->ON
  1->0 current flows to move charge to the capacitance
  0->1 current flows from capacitance to ground
Charging and discharging of capacitance causes power dissipation:
  C*Vdd per charge + discharge
  see https://en.wikipedia.org/wiki/CMOS

## Slide 13: Impact of Technology
Transistor basics
Power issues
  Dynamic
  Static
Reliability
  MTTF
  AVF
  ACE
  NBTI
  EM
  TDDB
  ... what is all of this?

## Slide 14: Scaling dynamic power
Pdynamic = α.f.C.Vdd2
  α = fraction of clock cycles when gate switches (at most ½) = activity factor
  C and Vdd ~1/S and f ~S => Pdynamic scales like 1/S2
  Number of transistor in unit area ~ S2
Hence power density (power/area) = constant with ideal scaling
If Vdd does not scale (down with factor S) then power density grows
  Serious issue since voltage can not reduce very much beyond current levels
  If chip size grows then total power grows
Power dissipation leads to heat generation
  When heat is not removed at the same rate it causes thermal emergencies

## Slide 15: Reducing dynamic power: Pdynamic = α.f.C.Vdd2
Reduce α (switching activity)
  Power gating cuts off power from idle units
  Clock gating cuts off power-hungry clock

## Slide 16: Reducing dynamic power: Pdynamic = α.f.C.Vdd2
Reduce Vdd – most effective approach
  Voltage scaling
  For correct circuit operation it also requires simultaneous reduction in frequency since transistor becomes slower at lower voltage
Reducing both Vdd and f reduces power cubically
  Reduction comes at the cost of performance
Smart Scaling is the key to preserve performance

## Slide 17: Other scaling approaches: adapting Vth
Reduce Vdd and Vth simultaneously so frequency does not need to reduce
  Reducing Vth increases leakage !!
Use multiple threshold CMOS devices (MTCMOS)
  Use high leakage, i.e. lower Vth but faster, devices when speed is critical
  Use low leakage devices, i.e. higher Vth but slower, on non critical paths
  Or use (dynamic) Body Biasing, i.e. changing body voltage
    Forward Body Biasing (FBB): reduces Vth, increases performance and leakage
    Backward Body Biasing (BBB): increases Vth, reduces performance and leakage

## Slide 18: Other scaling approaches: power islands
Use multiple power (adaptive voltage & frequency) domains
  Eg. when caches run at a different voltage than logic

## Slide 19: Parallelism impact on Energy
Two choices for the same design:
  Pipeline the design so each of the two stages runs at the same frequency but does half the work
  Divide the work into two parallel units each running at half the frequency
  What happens to Pdynamic = α.f.C.Vdd2 ?
  And to E = Pdynamic * t ?
Notes: Use Pdynamic = αCVdd2f
Example has logic with delay of 16 FO4 (the delay of an inverter with fan-out of 4)
Pipelining
C and V do not change, f doubles, P doubles, t halves, E same;
however, if we keep f the same (as in picture, i.e. same performance), than we can reduce V and therefore P and E
Parallel units
C doubles, f same, V same, P doubles, t halves, E same
however, if we halve f (as in picture, i.e. same performance), than we can reduce V and therefore P and E

## Slide 20: Static power
Pstatic = V.Isub ~ V.e-kVth/T
When VGS drops below Vth, IDS still exists, leading to static power dissipation
The current in sub-threshold region is exponentially dependent on Vth as well as the operating temperature.
  Hence as Vth decreases static power increases exponentially
Techniques to reduce static power are similar to dynamic power
  HOWEVER, from a static power point of view, pipelining is better than parallelism (why?)
Higher Vth and lower T are better

## Slide 21: Metrics
Power is good metric for deciding on the thermal envelope of the processor
Energy is good metric in battery constrained environments
  E.g., app executed at ½ speed but ¼ power means: ½ the energy (2T * ¼ P = ½ E) =>
  2X battery life!
Energy*Delay (ED) metric gives higher weight to performance
  Same example above, ED ((2T)2 * ¼ P) stays same
Energy*Delay2 gives even more weight to performance
  Same example above shows that ½ speed is 2X worse on ED2 metric

## Slide 22: Impact of Technology
Transistor basics
Power issues
Reliability
  MTTF
  SDC
  SER
  AVF
  ACE
  NBTI
  EM
  TDDB
  ... what is all of this?

## Slide 23: Scaling problems
Smaller dimensions leads to:
  Increased magnitude of within-die parameter variations
  Greater susceptibility to soft errors
  More rapid wear-out
Shekhar Borkar
Notes: Simply stated, variations occur when we have too few dopant atoms. In a 65 NM technology roughly 100 dopant toms are present per transistor. If we loose a couple of those dopant atoms that is essentially 2% variability in the electrical characteristics of that device.

## Slide 24: Definitions
SDC = Silent Data Corruption (= not detected)
DUE = Detected and Unrecoverable Error
SER = Soft Error Rate = SDC + DUE
Failure is measured as
  MTTF = Mean Time to Failure
  FIT = Failure in Time ; 1 FIT = 1 failure in billion hours
    MTTF = 1 => 1 failure in 24*365 hours => 1 billion/(24*365)= 114,155 FIT
  FIT is commonly used because FIT is additive

## Slide 25: Fault => Error => Failure
Source: Shubhu Mukherjee, INTEL
A fault (e.g. cause by alpha particle) can give an error (bit toggle in memory or flip-flop)
When an error affect correct execution it becomes a failure
Vulnerability Factor = fraction of faults that become errors
Bit
Read?
Bit has error protection?
yes
no
detection &
correction
no
no error
benign fault
no error
detection only
affects program
outcome?
True DUE
False DUE
no
yes
yes
no
affects program
outcome?
benign fault
no error
SDC
yes
no
Silent Data Corruption
Detected and unrecoverable error
Notes: Parity will convert SDC into True DUE, but also convert “benign fault no error” into False DUE
EXAMPLE of False DUE: strike on wrong-path instruction in instruction queue, show the similarity with other branch of tree

## Slide 26: Error detection & correction
adding redundancy bits to the data
e.g. even parity: add a parity bit to every byte
  0 0 1 1 0 1 0 0 + 1 makes even parity
  detects single bit errors
  no correction possible
SECDED: single error correction, double error detection
Many codes:
  hash function / signature;
  checksum (like the 1-bit parity)
  CRC (cyclic redundancy check)
  Hamming codes: 2 valid codes have a minimum hamming distance > 1
    parity is a code with Hamming Distance = 2
    SECDED has Hamming Distance = 3

## Slide 27: Fault Containment
An SDC or a DUE becomes a failure if it affects program execution
SECDED = Single Error Correction, Double Error Detection

## Slide 28: Lifetime failure rates
Failure rate follows bathtub curve:
  Higher failure rates at the initial stage of the manufacturing and operation
  Long useful life
  Finally ageing-related wear-out errors
Burn-in testing removes early failure components

## Slide 29: SEUs: Single Event Upsets
p substrate
n+
n+
Body
+ -
+ -
+ -
+ -
Insulation
Neutron Strike
Single Event Upset
Electron-Hole Tunneling
Gate
High energy neutron strike:
  Creates electron-hole pairs by splitting silicon nucleus
  The charge from the pairs travels toward gate diffusion region
  Causes the transistor charge to flip
  Causes a bit to flip
  Both 0 or 1 stored can be flipped (depending on holes or electron interactions)

## Slide 30: BIT Soft Error Rates
SER: λ ~ flux * bit_area * eQcritical/Qcollect
  Particle Flux depends on altitude
  Bit_area is silicon area required to implement 1 bit
  Qcollect is charge collection efficiency also technology dependent
  Charge needed to flip a bit Qcritical
    Qcritical ~ Cnode * Vdd
    According to scaling rules both C and V decrease and hence Q decreases rapidly
Probability of a soft error in a clock cycle PSE
  PSE = Σe-λ Tc(λTc)k/k! for all odd k (only odd number of bit-flips gives an error)
  Tc and bit_area decrease, but λ depends exponentially on Qcritical
  Hence probability of soft error is largely dependent on Qcritical

## Slide 31: AVF (Architectural Vulnerability Factor)
AVFbit = Probability that bit matters
  = # of Errors visible to user / Total # of possible Bit Flips
  If we assume AVF = 100% then we will be over-designing the system
  Need to estimate AVF to optimize the system design for reliability
Example: timeline of events cache bit (in a cache block):

## Slide 32: ACE/unACE BITS IN microARCHITECTURE
Computing AVF requires identifying ACE bits (required for Architecturally Correct Execution) and unACE bits
Microarchitectural unACE bits (i.e. bits that do not change behavior):
  Idle/Invalid State: instructions where the opcode bits do not matter or reserved opcode bits
  Mis-Speculated State: instructions that are being executed speculatively and are not going to retire due to mis-speculation (or exceptions)
  All forms of predictors: Branch predictor, RAS
  Dead bits: Physical registers that have been read by the last consumer but are not deallocated

## Slide 33: ARCHITECTURAL unACE BITS
More unACE cases:
  NOP instructions: Plenty of them around (particularly in VLIW style processors)
    Only opcode must be protected; everything else is a don’t care
  Performance-enhancing instructions: Prefetch, Hint bits
  Predicated-false instructions: Itanium ISA supports predication to remove branch prediction (only predicate is ACE)
  Dynamically dead instructions: due to compiler inefficiencies
  Logical masking: Bit masking operations

## Slide 34: Electromigration (EM)
Wire width decreases with scaling
  But current density increases
  Nearly 1000 amps can move through a wire
Metal atoms in wire gather momentum and move with the electron flow
Leads to shorts and opens in the wires
Metal Atom Flow
Metal Layer 1
Metal Layer 2
Electron Flow
Hillock Deposition
Void Creation

## Slide 35: EM in SRAM cells
Both the BL and BL-bar have unidirectional current causing EM effects
Precharge
WL
BL
BL
Sense Amp
Unidirectional
Current Flow
P1
P2

## Slide 36: NBTI (Negative Bias Temperature Instability)
+ : interface trap
H : hydrogen
: electric field
VD = VDD
Stress Phase
n substrate
p+
p+
Body
+ + + + + + + + + +
H H H H H H H H
VS = VDD
VG = 0
Recovery Phase
n substrate
p+
p+
Body
+ + +
H H H H
VS = VDD or 0
VG = VDD
VD = VDD

## Slide 37: NBTI Impact
NBTI affects when a negative bias is applied on PMOS
The effect goes away when the bias is removed
  Partially recovers
Potential to fully recover if the bias is flipped to positive
  Yet, only partially recovery is possible
Threshold Voltage Increase (|Vth|)
Time
Stress Time
Recovery Time
T0
T1
T2

## Slide 38: TDDB (Time Dependent Dielectric Breakdown)
Wearout process breaking the gate dielectric material, creating a conductive path in the gate oxide
p+ substrate
n+
n+
Body
Gate Insulation
Traps
+
+
+
p+ substrate
n+
n+
Body
Trap Accumulation
Leading to Conducting
Path
+
+
+
+
+
+
Gate Insulation

## Slide 39: What did you learn?
nMOS transistor characteristics
Inverter: structure, operation
Dennard Scaling impact, and Moore's law
Faults – Errors – Failure
Error classification
  SEUs, Soft Errors, Silent data corruption, Permanent errors
FIT, MTTF
AVF: Architectural Vulnerability Factor
  ACE & unACE bits