## Slide 1: Embedded Computer Architecture 5SAI0 Simulation (ch9)
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2019-2020

## Slide 2: Processors Processing Processors
The meta-lecture

## Slide 3: Why Simulators?
Your Friend Harm

## Slide 4: Why Simulators?
Harm
Harm Loves Tractors

## Slide 5: Why Simulators?
Harm
The outside world
Unfortunately for Harm you need to go outside to drive tractors

## Slide 6: Why Simulators?
Harm
The outside world
And the outside world is filled with dangers

## Slide 7: Why Simulators?
Harm
The outside world
And the outside world is filled with dangers
Rain!

## Slide 8: Why Simulators?
Harm
The outside world
And the outside world is filled with dangers
Rain!
Scary Animals!

## Slide 9: Why Simulators?
Harm

## Slide 10: Why Simulators?
So Harm uses his PC
Harm

## Slide 11: Why Simulators?
Harm

## Slide 12: Why Simulators?
Harm
Oh No! My PC is too slow to run Farming Simulator

## Slide 13: Why Simulators?
Harm
Oh No! My PC is too slow to run Farming Simulator
You

## Slide 14: Why Simulators?
Harm
Oh No! My PC is too slow to run Farming Simulator
Stand back!
I’m a computer architect!
You
Obligatory cape

## Slide 15: How to help Harm?
You
Of course you have many ideas on how to speed-up Harms computer.
But which ones should you apply?

## Slide 16: Design Space Exploration Options

## Slide 17: Design Space Exploration Options
Buy (or build) all hardware options

## Slide 18: Design Space Exploration Options
Buy (or build) all hardware options
Gee that sounds expensive...

## Slide 19: Design Space Exploration Options
Buy (or build) all hardware options
Use analytical models

## Slide 20: Design Space Exploration Options
Buy (or build) all hardware options
Use analytical models
How reliable
is that?

## Slide 21: Design Space Exploration Options
Buy (or build) all hardware options
Use analytical models
Simulate the design points!

## Slide 22: Design Space Exploration Options
Buy (or build) all hardware options
Use analytical models
Simulate the design points!
Hey, I like simulators, That sounds promising :)

## Slide 23: What to simulate for?

## Slide 24: What to simulate for?
Performance
Energy
Power (!=Energy)
Thermal

## Slide 25: What to simulate for? What details to simulate?
Performance
Energy
Power (!=Energy)
Thermal

## Slide 26: What to simulate for? What details to simulate?
Cycle accurate vs Functionality
Caches
Full operating system
Disk accesses
Background tasks
...
Performance
Energy
Power (!=Energy)
Thermal

## Slide 27: What to simulate for? What details to simulate?
Cycle accurate vs Functionality
Caches
Full operating system
Disk accesses
Background tasks
...
Performance
Energy
Power (!=Energy)
Thermal

## Slide 28: All the details: RTL Simulation

## Slide 29: All the details: RTL Simulation
Simulate at gate level:

## Slide 30: All the details: RTL Simulation
Simulate at gate level:
modelsim/questasim (Mentor)
ncsim (Cadence)
VCS (Synopsys)
Icarus Verilog (Open Source!)
...

## Slide 31: All the details: RTL Simulation
Simulate at gate level:
modelsim/questasim (Mentor)
ncsim (Cadence)
VCS (Synopsys)
Icarus Verilog (Open Source!)
...
Advantages:
No need to build a custom simulator if you need RTL to build hardware anyway
Highest level of precision and detail

## Slide 32: All the details: RTL Simulation
Simulate at gate level:
modelsim/questasim (Mentor)
ncsim (Cadence)
VCS (Synopsys)
Icarus Verilog (Open Source!)
...
Advantages:
No need to build a custom simulator if you need RTL to build hardware anyway
Highest level of precision and detail
Disadvantage:
Horribly slow for realistic designs

## Slide 33: All the details: RTL Simulation
Simulate at gate level:
modelsim/questasim (Mentor)
ncsim (Cadence)
VCS (Synopsys)
Icarus Verilog (Open Source!)
...
Advantages:
No need to build a custom simulator if you need RTL to build hardware anyway
Highest level of precision and detail
Disadvantage:
Horribly slow for realistic designs
Nvidia GPU with > 1 Billion transistors
Small tests take over 8 hours! [1]
[1] http://www.deepchip.com/items/0523-04.html

## Slide 34
modified from http://xkcd.com/303/
Simulating!
Simulating
Computer Architect

## Slide 35: Slightly less horribly slow: Hardware Emulation
RTL description
of Target Architecture

## Slide 36: Slightly less horribly slow: Hardware Emulation
RTL description
of Target Architecture
Synthesize for
FPGA (slow)

## Slide 37: Slightly less horribly slow: Hardware Emulation
RTL description
of Target Architecture
Synthesize for
FPGA (slow)
Emulate on FPGA (fast!)
Note: instrumentation required to get detailed information out!

## Slide 38: Levels of detail in Simulation
Full-System versus User-level
Cycle Accurate versus Functional
Execution- versus Trace-driven

## Slide 39: Full-system versus User-Level
To OS or not to OS?

## Slide 40: Full-system versus User-Level
To OS or not to OS?
Full-System

## Slide 41: Full-system versus User-Level
To OS or not to OS?
Full-System

## Slide 42: Full-system versus User-Level
User-Level
To OS or not to OS?
Full-System

## Slide 43: User-Level
Famous example: Simple Scalar [1]
Advantages
Fast to develop and update to new architectures
Usually ‘accurate enough’
Disadvantages
Any time spent in the OS is not modelled accurately. Can have severe impact, database applications spent 20-30% of their time in OS mode.
[1] http://www.simplescalar.com/

## Slide 44: Cycle Accurate versus Functional
Notes: orthogonal classification to full-system vs user-level

## Slide 45: Cycle Accurate versus Functional
Cycle Accurate
Notes: orthogonal classification to full-system vs user-level

## Slide 46: Cycle Accurate versus Functional
Cycle Accurate
Notes: orthogonal classification to full-system vs user-level

## Slide 47: Cycle Accurate versus Functional
Cycle Accurate
Functional
Notes: orthogonal classification to full-system vs user-level

## Slide 48: Cycle Accurate versus Functional
Functional - no/limited model of the micro architecture
An (add) instruction of the target can be translated to an (add) instruction on the host, and be simulated that way.
Example 1: Simple Scalar sim-fast
Example 2: QEMU, Full-system emulator using dynamic translation
Cycle Accurate - includes model of the micro architecture
Block resources in the pipeline when instruction executes
Use target branch predictor scheme
Out-of-order execution
Example: Simple Scalar sim-outorder

## Slide 49: Intermezzo - Internals of dynamic translation
Target
Binary
Native
Instructions
Magic
Translate

## Slide 50: Intermezzo - Internals of dynamic translation
Target
Binary
Native
Instructions
Magic
Translate
int32_t instructions[]={
0x3FE9,
0xA701,
0xEF02,
0x8FF0
};
execute(instructions);

## Slide 51: Intermezzo - Internals of dynamic translation
Target
Binary
Native
Instructions
Magic
Translate
Question
Implement the execute function in regular C
int32_t instructions[]={
0x3FE9,
0xA701,
0xEF02,
0x8FF0
};
execute(instructions);

## Slide 52: Intermezzo - Internals of dynamic translation
int32_t instructions[]={
0x3FE9,
0xA701,
0xEF02,
0x8FF0
};
execute(instructions);
void execute(int32_t* instructions){
//declare a pointer to a function that returns void
// and has no arguments
void (fp*)(void);
//set the function pointer to the first instruction
fp=instructions;
//call the function
//Note: make sure the last instruction in the list returns
fp();
}

## Slide 53: Execution- versus Trace-driven

## Slide 54: Execution- versus Trace-driven
Application Binary
Execution-Driven
Simulator
Metrics
Execution Driven: Application executes on simulator

## Slide 55: Execution- versus Trace-driven
Application Binary
Execution-Driven
Simulator
Metrics
Instruction
Trace
Trace-Driven
Simulator
Application Binary
Execution-Driven
Simulator
Metrics
Execution Driven: Application executes on simulator
Trace Driven: simulator uses trace as input

## Slide 56: Execution- versus Trace-driven
Application Binary
Execution-Driven
Simulator
Metrics
Instruction
Trace
Trace-Driven
Simulator
Application Binary
Execution-Driven
Simulator
Metrics
Execution Driven: Application executes on simulator
Trace Driven: simulator uses trace as input
mov edx,len
mov ecx,msg
mov ebx,1
mov eax,4 int 0x80

## Slide 57: Execution- versus Trace-driven
Application Binary
Execution-Driven
Simulator
Metrics
Instruction
Trace
Trace-Driven
Simulator
Application Binary
Execution-Driven
Simulator
Metrics
Execution Driven: Application executes on simulator
Trace Driven: simulator uses trace as input
mov edx,len
mov ecx,msg
mov ebx,1
mov eax,4 int 0x80
Why would a sane person do this?

## Slide 58: Execution- versus Trace-driven
Application Binary
Execution-Driven
Simulator
Metrics
Instruction
Trace
Trace-Driven
Simulator
Application Binary
Execution-Driven
Simulator
Metrics
Execution Driven: Application executes on simulator
Trace Driven: simulator uses trace as input
mov edx,len
mov ecx,msg
mov ebx,1
mov eax,4 int 0x80
ISA compatible
Processor
OR

## Slide 59: Trace-driven Simulation
Advantages
Trace collection only required once
Trace collection can be done with ISA compatible processor
Trace simulator does not need to simulate all instructions, can skip ahead in trace if not implemented

## Slide 60: Trace-driven Simulation
Advantages
Trace collection only required once
Trace collection can be done with ISA compatible processor
Trace simulator does not need to simulate all instructions, can skip ahead in trace if not implemented
Disadvantages
Cannot speculatively execute code (trace is fixed)
Trace file can become huge for large applications (hundreds of GBs)

## Slide 61: Mixing Simulation Strategies
Direct-execution
Parts execute directly on the host (e.g. using dynamic translation such as QEMU)
Other parts are executed on cycle accurate simulation
Use case:
Interested in memory accesses and memory behavior. Execute only loads and
stores on the simulator, emulate the rest directly on the host machine

## Slide 62: Simulation in the Multiprocessor Era

## Slide 63: Simulation in the Multiprocessor Era

## Slide 64: Parallelisation in all levels of the simulation stack
Benchmark
Target Processor
Simulator
Host Platform

## Slide 65: Parallelisation in all levels of the simulation stack
Benchmark
Target Processor
Simulator
Host Platform
0
1
N
...
Multi-threaded application

## Slide 66: Parallelisation in all levels of the simulation stack
Benchmark
Target Processor
Simulator
Host Platform
0
1
N
...
Multi-threaded application
A multi-threaded application running on a single core target processor.
Question: Does this make sense?

## Slide 67: Parallelisation in all levels of the simulation stack
Benchmark
Target Processor
Simulator
Host Platform
0
1
N
...
Multi-threaded application
Multi-core target processor
A
B
?
...

## Slide 68: Parallelisation in all levels of the simulation stack
Benchmark
Target Processor
Simulator
Host Platform
0
1
N
...
Multi-threaded application
Multi-core target processor
A
B
?
...
A multi-core processor running on a single threaded simulator.
Question: Does this make sense?

## Slide 69: Parallelisation in all levels of the simulation stack
Benchmark
Target Processor
Simulator
Host Platform
0
1
N
...
Multi-threaded application
Multi-core target processor
A
B
?
...
Multi-threaded simulator
0
1
N
...

## Slide 70: Parallelisation in all levels of the simulation stack
Benchmark
Target Processor
Simulator
Host Platform
0
1
N
...
Multi-threaded application
Multi-core target processor
A
B
?
...
A multi-threaded simulator running on a single-core host.
Question: Does this make sense?
Multi-threaded simulator
0
1
N
...

## Slide 71: Parallelisation in all levels of the simulation stack
Benchmark
Target Processor
Simulator
Host Platform
0
1
N
...
Multi-threaded application
Multi-core target processor
A
B
?
...
Multi-threaded simulator
0
1
N
...
Multi-core host platform
A
B
?
...

## Slide 72: Parallelisation at all levels of the simulation stack
Benchmark
Target Processor
Simulator
Host Platform
0
1
N
...
Multi-threaded application
Multi-core target processor
A
B
?
...
Multi-threaded simulator
0
1
N
...
Multi-core host platform
A
B
?
...
But how to build a fast, multi-threaded simulator?

## Slide 73: Parallelisation in all levels of the simulation stack
Simulator
Multi-threaded simulator
0
1
N
...
But how to build a fast, multi-threaded simulator?

## Slide 74: Parallel Simulation Techniques
Discrete event simulation
Quantum simulation
Slack simulation

## Slide 75: Parallel Simulation Techniques
Discrete event simulation
Quantum simulation
Slack simulation
Not schrödinger's cat ‘quantum’ though

## Slide 76: Space Granularity
The textbook implicitly assumes the smallest hardware block that can be mapped to a simulator thread is a full target core.
Holds for almost all real-world simulators, which severely limits the parallelism

## Slide 77: Space Granularity
The textbook implicitly assumes the smallest hardware block that can be mapped to a simulator thread is a full target core.
Holds for almost all real-world simulators, which severely limits the parallelism
Exception is RTL simulation, there the blocks can be smaller.
The Rocketick simulator even appears to use GPUs! [1]
[1] http://www.deepchip.com/items/0523-04.html

## Slide 78: Discrete-Event Simulation
A logical choice for a simulator “time step” is one cycle for the fastest core.

## Slide 79: Discrete-Event Simulation
Disadvantage

## Slide 80: Discrete-Event Simulation
Disadvantage
Under utilisation of the host platform if threads are idle for synchronisation

## Slide 81: Discrete-Event Simulation
Disadvantage
Under utilisation of the host platform if threads are idle for synchronisation
Is it really this bad? What assumption did the author of the book make here?

## Slide 82: Discrete-Event Simulation
Disadvantage
Under utilisation of the host platform if threads are idle for synchronisation
Is it really this bad? What assumption did the author of the book make here?
Every target processor Pn is mapped to a separate host core

## Slide 83: Target vs Host Cores
There is no relation between the number of target cores and the number of host cores!!!

## Slide 84: Target vs Host Cores
There is no relation between the number of target cores and the number of host cores!!!

## Slide 85
Benchmark
Target Processor
Simulator
Host Platform
0
1
N
...
Multi-threaded application
Multi-core target processor
A
B
?
...
Multi-threaded simulator
0
1
N
...
Multi-core host platform
A
B
?
...

## Slide 86: Discrete-Event Simulation

## Slide 87: Discrete-Event Simulation
Utilisation of host depends on variation in processing time of a cycle, but also on the amount of host cores!
P4
P3
P2
P1
1
Host core 1

## Slide 88: Quantum Simulation
Synchronize threads at larger time-steps, e.g. 3 cycles

## Slide 89: Quantum Simulation
Advantage
Utilisation improves, because the variation of processing is amortized over longer sections of simulation
Disadvantage
No longer cycle accurate
Synchronize threads at larger time-steps, e.g. 3 cycles

## Slide 90: Slack Simulation
Start with discrete-event simulation schedule

## Slide 91: Slack Simulation
Instead of waiting in the red areas, use slack to process ahead

## Slide 92: Slack Simulation
Instead of waiting in the red areas, use slack to process ahead

## Slide 93: Slack Simulation
Side-effect: Drift
The cores might be simulating different points in time, and could drift apart
Mitigation
Allow a maximum drift (or slack), and synchronize when this value is exceeded

## Slide 94: Slack Simulation
Side-effect: Drift
The cores might be simulating different points in time, and could drift apart
Mitigation
Allow a maximum drift (or slack), and synchronize when this value is exceeded
Max slack of 2

## Slide 95: Slack versus Quantum simulation
In quantum simulation, the core simulation times always stay within a cycle window, which is fixed in global time.
Also in slack simulation the simulation times stay within a window, but with the key difference that this is a sliding window.

## Slide 96: Slack versus Quantum simulation
In quantum simulation, the core simulation times always stay within a cycle window, which is fixed in global time.
Also in slack simulation the simulation times stay within a window, but with the key difference that this is a sliding window.
Typically much less synchronisation!

## Slide 97: Still not good enough
[1] Graphite: A Distributed Parallel Simulator for Multicores - Jason E. Miller et al.
From the paper Graphite: a Distributed Parallel Simulator for Multicores
“Simulation slowdown is as low as 41× versus native execution”

## Slide 98: Still not good enough
[1] Graphite: A Distributed Parallel Simulator for Multicores - Jason E. Miller et al.
From the paper Graphite: a Distributed Parallel Simulator for Multicores
“Simulation slowdown is as low as 41× versus native execution”
That still sounds slow

## Slide 99: Still not good enough
[1] Graphite: A Distributed Parallel Simulator for Multicores - Jason E. Miller et al.
From the paper Graphite: a Distributed Parallel Simulator for Multicores
“Simulation slowdown is as low as 41× versus native execution”
That still sounds slow
Well...

## Slide 100: Still not good enough
[1] Graphite: A Distributed Parallel Simulator for Multicores - Jason E. Miller et al.
From the paper Graphite: a Distributed Parallel Simulator for Multicores
“Simulation slowdown is as low as 41× versus native execution”
That still sounds slow
Yes :(

## Slide 101
cycles
0
1e16
Question
What can we do if it still takes weeks or months to simulate a full benchmark?

## Slide 102: Workload Sampling
cycles
0
1e12
fixed length
Naive Approach
Only simulate first X cycles

## Slide 103: Workload Sampling
cycles
0
1e12
fixed length
Often benchmarks start with reading settings and initialisation. Most likely not representative of workload!

## Slide 104: Workload Sampling
cycles
0
1e12
init
fixed length
Fix
Use functional simulation to skip over the initial section
skip init with
functional sim

## Slide 105: Workload Sampling
cycles
0
1e12
init
fixed length
Question
Is the window always a good representation of the benchmark?
Why/why not?
skip init with
functional sim

## Slide 106: Program Modes
Real world programs spend time in different modes,
which can have very different characteristics

## Slide 107: Workload Sampling
cycles
0
1e12
init
fixed length
skip init with
functional sim
uniform sampling
Sample uniformly over the program, hopefully capturing the dominant modes

## Slide 108: Workload Sampling
cycles
0
1e12
init
fixed length
skip init with
functional sim
uniform sampling
However, if the window size is very small, the micro-architecture is not initialized correctly!
E.g.: the branch predictor and caches
Sample uniformly over the program, hopefully capturing the dominant modes

## Slide 109: Workload Sampling
cycles
0
1e12
init
fixed length
skip init with
functional sim
uniform sampling
Solution: add warm up period before every window

## Slide 110: Workload Sampling
cycles
0
1e12
init
fixed length
skip init with
functional sim
uniform sampling
Solution: add warm up period before every window
Question
How long should we warm-up?

## Slide 111: Workload Sampling
cycles
0
1e12
init
fixed length
skip init with
functional sim
uniform sampling
Solution: add warm up period before every window
Some numbers suggested by SMARTS [1] to get a feeling for the scale:
Initializing caches 500.000 cycles
Initializing branch prediction, reorder buffers, etc (micro architectural structures.) 4000 cycles
window size 1000 cycles
[1] SMARTS: accelerating microarchitecture simulation via rigorous statistical sampling - Roland E. Wunderlich et al.

## Slide 112: Workload Sampling
cycles
0
1e12
init
fixed length
skip init with
functional sim
uniform sampling

## Slide 113: Workload Sampling
cycles
0
1e12
init
fixed length
skip init with
functional sim
uniform sampling
“mode
sampling”

## Slide 114: Workload Sampling
cycles
0
1e12
init
fixed length
skip init with
functional sim
uniform sampling
“mode
sampling”
Profile for modes in the application,
and select representative windows.
Typically the window size can be larger,
so less windows + warm-up is required

## Slide 115: Summary
Why Simulators
  More accurate than models
  Cheaper than building hardware
Simulation detail
  Full-System vs User-level
  Functional vs Cycle Accurate (micro-arch.) vs Gate-Level
  Execution- vs Trace-driven
(Fast) Multiprocessor Simulation
  Discrete event
  Quantum
  slack
Workload Sampling
Summary (the meta lecture)

## Slide 116: Summary
You can read about all of this in your
textbook, chapter 9
Why Simulators
  More accurate than models
  Cheaper than building hardware
Simulation detail
  Full-System vs User-level
  Functional vs Cycle Accurate (micro-arch.) vs Gate-Level
  Execution- vs Trace-driven
(Fast) Multiprocessor Simulation
  Discrete event
  Quantum
  slack
Workload Sampling
Summary (the meta lecture)