## Slide 1: Neuromorphic Sensors and Processors
Amirreza Yousefzadeh (Amirreza.Yousefzadeh@imec.nl)
March 2021

## Slide 2: Sensing by Periodic sampling
Videos are made by continues capturing of static pictures
  Sampling rates -> fixed (24fps, 60fps, 120fps)
Same for Audio (and other sensors)
https://en.wikipedia.org/wiki/Stop_motion

## Slide 3: Fixed sampling rate is not optimal for machine vision
Low rate  motion blur
High rate  Redundancy
Optimum rate changes with time and location of pixels (background vs moving object)
The processing of recorded data happens on every sample individually
  Processing of high amount of redundant data

## Slide 4: Bio-inspired sensors
Adaptive spatio-temporal sampling rate (Asynchronous sampling)
  Every photo-receptor in the eye only fires when there is a change in the light intensity
Processing of compressed samples (events) is energy efficient
  When nothing happens, nothing is sent or processed (event-based processing)
"What is Neuromorphic Event-based Computer Vision? Sensors, Theory and Applications," a Presentation from Ryad B. Benosman

## Slide 5: Neuromorphic Sensors
Only produce output events (spikes) when detect a change in the scene
(Event-Driven)
Dynamic Vision Sensor
(DVS)
Dynamic Audio Sensor
(DAS)
Neuromorphic tactile sensor

## Slide 6: Dynamic Vision Sensor (DVS)
"E. Mueggler, B. Huber, D. Scaramuzza, Event-based, 6-DOF Pose Tracking for High-Speed Maneuvers", IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS), Chicago, 2014.
https://youtu.be/LauQ6LWTkxM
https://www.frontiersin.org/articles/10.3389/fnins.2013.00223/full

## Slide 7: Dynamic Vision Sensor
Many companies started building their own silicon retinas!
  March 2020: Prophesee built 1280x720 event-based vision sensor (link)

## Slide 8: Dynamic Vision Sensor
Many companies started building their own silicon retinas!
  March 2020: Prophesee built 1280x720 event-based vision sensor (link)

## Slide 9: Neuromorphic processors
Conventional signal processing algorithms and processors are designed to process time-sampled signals
Neuromorphic processors (inspired by the brain) are design to optimally process events from these sensors.
Artificial Neural Networks  Spiking Neural Networks (SNN)

## Slide 10: Von-Neumann processors
Separated Memory and processor
  High power consumption on data transfer
  Memory bottleneck issue for scalability
Centralized processing
  Not scalable anymore!
Static and fully synchronous programing
  Always executing something! even NOP
Conventional processors:
Biological Brain:
In-memory processing
  Memory and processor are the same
Fully distributed memory/processing
  Highly scalable
Sparse event-driven processing/communication
  Only process relevant data
Biological
processing
We are halfway!
Designed to perform exact calculation
Not good for signal processing!
Human Brain*
86B neurons, 150T Synapses (20 Watt)
Visual Processing -> 30%
Auditory Processing -> 3%
*Provided numbers are estimations and averaged
area

## Slide 11: Towards Biological Processing
Parallel Processing
  Going towards higher number of small processors
Distributed Memory
  Having more tightly coupled data memory, cache, ...
  Bring more memory closer to the processor
Sparse Event-Driven processing
  Skipping redundant operations
Data-flow Communication
  Data moves toward the place it is consumed
  Direct communication between processors

## Slide 12: Communications between Processors
Learning from biology 
Direct communication of neurons with spikes!
  Spikes can be a packet of data containing the address of the source neuron or it can be a pulse for a short time
EPIPHANY 1024-RISC Processors
SpiNNaker 16-ARM Processors
http://www.adapteva.com/announcements/epiphany-v-a-1024-core-64-bit-risc-processor/

## Slide 13: Asynchronous Processing and Communication
Learning from Biology  Asynchrony is the key feature for scalability
  Not possible with off the shelf processors
10K
250K
960K
310M
1.5B
28B
Similar architecture, scaling up 106 times!!!

## Slide 14: Event driven ...vs... vector processing
0 | 0 | 7 | 0 | 0 | 0 | 5 | 0 | 0 | 0
Sparse Vector
(2,7), (6,5)
Sparse vector representation
Event-based processing only process relevant input data (here it is non-zero)
 |  | 2 |  |  |  | 6 |  |  | 

## Slide 15: Typical Large scale Neuromorphic Architectures
RAM
ROM
ED-Proc
GALS Architecture :
Extremely Scalable to many core and many chip connectivity
Event-Driven Processing:
Extremely low power for sparse activity
High density Memory Technology:
Near memory low power computation
Scalable connectivity:
network on chip

## Slide 16: Event Driven Processor
Synapse Memory:
Synaptic parameters (weights)
State Memory:
Neurons’ state
Axon Memory:
Destination core address (to store the graph of DNN)
Synapse Memory
Neuron State Memory
Axon Memory
Event Driven Processor
One processing core updates the state of many neurons, based on the input events

## Slide 17: Some Neuromorphic Processors
4096 cores (digital 28nm, GALS)
256 Neurons/Core (time-multiplex)
1 axon per neuron
256 Synapses/N (Binary) no learning
Resources per neuron and 256 synapses:
  426b of SRAM
  5k Transistors
  26pJ per synaptic operation
Many-core Parallel Processors – Near/Inside Memory Processing – Event-driven Communication
IBM TrueNorth 2014
Intel LOIHI 2018
128 cores (digital 14nm, fully asynchronous)
1024 Neurons/C (time-multiplex)
4096 axons per core (shared)
1M Synapses/core (shared, Binary) With Learning
Resources per neuron and its synapses:
  2000b per neuron
  15k Transistors
  80pJ per synaptic operation
196 cores (digital 28nm, fully synchronous)
1024 Neurons/C (time-multiplex)
1024 axons per core (shared)
1024 Synapses/core (8b weights, shared)
Resources per neuron and its synapses:
  120b per neuron
  20pJ per synaptic operation
GML GrAI-One

## Slide 18: Some Neuromorphic Processors
Honeybees
1M Neurons
1B Synapses (non-binary) With plasticity
Total size of 1mm3
Resources per neuron and 1024 synapses:
Human brain
80B Neurons
150T Synapses (nonbinary) With plasticity
Total size of 1274cm3
Total power consumption of 20W
Resources per neuron and 2000 synapses:
  25
Learning from Biology  3D construction is needed!
DYNAPs 2017
4 cores (analog 180nm, fully asynchronous)
256 Neurons/C (physically implemented)
65 Synapses/N (4b) With plasticity
Resources per neuron and 65K synapses:
  0.13pJ per synaptic operation

## Slide 19: SpiNNakeR
18 ARM cores per chip
GALS packet-switched network
3D mounted HBM memory
1Watt per chip
Scaled-up to 1M cores
SpiNNaker2 will be released soon
https://en.wikipedia.org/wiki/SpiNNaker

## Slide 20: IBM True-North
Each neuron can only connect to one core (All 256 neurons inside one core)
1M neurons
256M synapses

## Slide 21: IBM True-North

## Slide 22: IBM TN
Power consumption
  Leak: 42mW (0.70 V, 0 Hz firing rate)
  323mW (1.05 V, 200 Hz firing rate, 256 synapses/neuron)

## Slide 23: Intel loihi
More flexible connectivity than True-North
Variable precision for synaptic weights
Weight Sharing (for CNN)
Fully asynchronous
Online learning
128 cores
1024 neurons/core
1M synapses/core

## Slide 24: Intel Loihi
1,024 spiking neural units per core
1Mb of synaptic memory per core
Ten architectural memories per core
  total of 2 Mb (including ECC)  2Kb per neuron

## Slide 25: Prominent neuromorphic enterprises
Intel (Munich)
IBM (Zurich)
Imec (Eindhoven, Leuven)
BrainChip (Toulouse)
GraiMatterLabs (Eindhoven, Paris)
Innatera (Delft)
Prophesee (Paris)
Inilab (Zurich)
SynSense (Zurich)
....

## Slide 26: Challenges
Limited On-Chip memory (synaptic parameters, topology of the graph, Neuron’s state)
 | Add int32 | Add FP16 | Mult int32 | Mult FP16 | SRAM SP 4096x32b (R&W) | SRAM SP 4096x16b (R&W)
Area (um2) | 200 | 500 | 2000 | 700 | 15000 | 9000
Energy (pJ) | 0.3 | 0.3 | 1.2 | 0.4 | 3.5 | 2.1

## Slide 27: Challenges
Idle power consumption (power consumption when no event is being processed)
Dynamic (related to Clock)
  Dynamic clock gating
  Globally Asynchronous (GALS) or fully asynchronous design
  Sleeping modes for memory peripherals
Static (related to Leakage)
  Low leak memory  Non-Volatile Memory for configuration (no leakage)
  Power-down strategy for not used circuits

## Slide 28: Challenges
Communication and Network-on-Chip
Overhead of Address Event Representation (Computation/communication load)
  Multi-casting
  Relative addressing
  Hyperthreading (increasing the size of a core)
NoC congestion
  Smart routing + Event dropping mechanism
  Multiple independent NoC
I/O bandwidth limitation for tiling
  Efficient event-driven LVDS communication links
Core Addr
Neuron Addr
Data
Event :

## Slide 29: Challenges
Programmability and Flexibility
Flexible neuron models
Heterogeneous processing cores (allows efficient mapping)

## Slide 30: Challenges
On-Chip Learning
Application!
Scalable HW efficient Algorithm (Local learning)

## Slide 31: References
Asynchronous Spiking Neurons, the natural key to exploit temporal sparsity, IEEE Journal on Emerging and Selected Topics in Circuits and Systems, 2019
Stochastic Spike Timing Dependent Plasticity with Binary Weights, Frontiers in Neuroscience, 2018
NeuronFlow: a neuromorphic processor architecture for Live AI applications, DATE 2020
BrainChip AKIDA is a fast learner, Spiking-Neural-Network Processor Identifies Patterns in Unlabeled Data, The Linley Group 2019
GrAI Matter Labs exploits Sparse Video, Neuromorphic Chip implements Convolutional Neural Networks, The Linley Group 2019

## Slide 32: Topics to discuss further
Sparsity types and how to exploit them
Advantages and Disadvantages of having stateful neurons
Asynchronous design challenges
Challenges in SNN trainings

## Slide 33: Temporal sparsity in human vision
Microsaccades (MS)
Rapid ballistic jumps of amplitude up to 1°, which occur at irregular intervals, only once or twice per second. They carry the retinal image over dozens of photoreceptor width or more, in only 20-30 ms.
Speed: 30 deg/s
Each Micro-saccade captures one frame!
One full frames per second is enough
Between micro-saccades, our vision system relies on the deltas (or motion events)
http://bbs.fmuser.com/t/what-is-gop-in-hdmi-sdi-h-264-iptv-streaming-video-encoder/139
http://bbs.fmuser.com/t/what-is-gop-in-hdmi-sdi-h-264-iptv-streaming-video-encoder/139
Conventional video compression techniques seem to have similar features as the human eye.
bigger

## Slide 34: Dynamic Vision Sensor
DVS : only send events when there is a change in log(light intensity)
  1us temporal resolution
  No grey scale information (only )
DAVIS (Dynamic and Active-pixel Vision Sensor)
  Events (1us resolution) + Grey scaled frames (30fps)
ATIS (Asynchronous Time-based Image)
  Two events per change (encode the grey level in time interval)
Compressed sensing
Temporally sparse
High temporal resolution (1us)
High dynamic range (140dB)
DVS with sunglasses
https://youtu.be/5NNoq1Gq4sc
Quadcopter localization with DVS
https://youtu.be/RFcjUBN3pw0