## Slide 1: Optimizing neural networks for deployment and execution
Quantization: from float32 to int8 and beyond
Floran de Putter
Electrical Engineering – Electronic Systems group

## Slide 2: AI is everywhere!
Object detection
Speech recognition
Autonomous driving

## Slide 3: DNN challenge: model size and compute power
2012
2015

## Slide 4: DNN challenge: energy efficiency
Main energy consumers are the memory accesses, not the actual computation itself.
Why is the RF dominant in conv layers and DRAM in FC layers?
INT16 AlexNet on 65nm Eyeriss architecture

## Slide 5: How to reduce energy consumption?
Previous lecture: pruning
    Eliminating as many neurons/connections as possible while preserving accuracy
Today: quantization
    Transforming a real-valued number to a finite number of distinct values
      Example: each pixel in a grayscale image is represented by 8 bits (256-levels)
    Advantage:
      Reducing the size of the weights and activations to save energy
    Disadvantage:
      Quantization is an irreversible process and causes information loss
Next lecture: data reuse
    Preventing costly data movements as much as possible
    Does not influence the accuracy

## Slide 6: Quantized grayscale image example
4 bits/pixel
8 bits/pixel
2 bits/pixel

## Slide 7: Relative energy cost of memory access and computation for various bitwidths
We see that:
DRAM access is expensive (~100x times more than SRAM)
SRAM access energy is linear
MAC energy is superlinear
Chart: 
| 2 bits | 4 bits | 8 bits | 16 bits | 32 bits
MAC | 0.37163 | 0.88388 | 2.1022 | 5 | 11.8921
SRAM | 1.25 | 2.5 | 5 | 10 | 20
DRAM | 80 | 160 | 320 | 640 | 1280
units and technology to be checked

## Slide 8: Overview of today’s lecture
Motivation
Data formats
    Common data types
    Fixed-point number format
Quantization schemes
Quantization heuristics
Quantization procedures
Assignment 1 internals
Conclusion

## Slide 9: Typical data formats used in DNNs
Number formats |  |  |  | Absolute range | Precision
 |  | 8 bits | 23 bits |  | 
float32 |  |  |  |  | 
 |  | 5 bits | 10 bits |  | 
float16 |  |  |  |  | 
 |  | 8 bits | 7 bits |  | 
bfloat16 |  |  |  |  | 
 |  | 15 bits |  |  | 
int16 |  |  |  |  | 0.5
 |  | 7 bits |  |  | 
int8 |  |  |  |  | 0.5
Number formats |  |  |  | Absolute range | Precision
 |  | 8 bits | 23 bits |  | 
float32 |  |  |  |  | 
 |  | 5 bits | 10 bits |  | 
float16 |  |  |  |  | 
 |  | 8 bits | 7 bits |  | 
bfloat16 |  |  |  |  | 
 |  | 15 bits |  |  | 
int16 |  |  |  |  | 0.5
 |  | 7 bits |  |  | 
int8 |  |  |  |  | 0.5
Notes: The higher dynamic range of bfloat16 is useful for gradients. Float16 typically requires loss scaling, whereas bfloat16 can represent such gradients directly

## Slide 10: Typical data formats used in DNNs
Number formats |  |  |  | Absolute range | Precision
 |  | 8 bits | 23 bits |  | 
float32 |  |  |  |  | 
 |  | 5 bits | 10 bits |  | 
float16 |  |  |  |  | 
Number formats |  |  |  | Absolute range | Precision
 |  | 8 bits | 23 bits |  | 
float32 |  |  |  |  | 
 |  | 5 bits | 10 bits |  | 
float16 |  |  |  |  | 
Floating-point numbers have (roughly) constant relative precision
Float32 can represent a very wide range of numbers!
Notes: The higher dynamic range of bfloat16 is useful for gradients. Float16 typically requires loss scaling, whereas bfloat16 can represent such gradients directly

## Slide 11: Typical data formats used in DNNs
Number formats |  |  |  | Absolute range | Precision
 |  | 8 bits | 23 bits |  | 
float32 |  |  |  |  | 
 |  | 5 bits | 10 bits |  | 
float16 |  |  |  |  | 
 |  | 8 bits | 7 bits |  | 
bfloat16 |  |  |  |  | 
Number formats |  |  |  | Absolute range | Precision
 |  | 8 bits | 23 bits |  | 
float32 |  |  |  |  | 
 |  | 5 bits | 10 bits |  | 
float16 |  |  |  |  | 
 |  | 8 bits | 7 bits |  | 
bfloat16 |  |  |  |  | 
Google introduced bfloat16 on the observation that “neural networks are far more sensitive to the size of the exponent than that of the mantissa”
Moreover: the physical size of a bfloat16 multiplier is roughly two times smaller than that of float16
Notes: The higher dynamic range of bfloat16 is useful for gradients. Float16 typically requires loss scaling, whereas bfloat16 can represent such gradients directly

## Slide 12: Typical data formats used in DNNs
Number formats |  |  |  | Absolute range | Precision
 |  | 8 bits | 23 bits |  | 
float32 |  |  |  |  | 
 |  | 5 bits | 10 bits |  | 
float16 |  |  |  |  | 
 |  | 8 bits | 7 bits |  | 
bfloat16 |  |  |  |  | 
 |  | 15 bits |  |  | 
int16 |  |  |  |  | 0.5
 |  | 7 bits |  |  | 
int8 |  |  |  |  | 0.5
Number formats |  |  |  | Absolute range | Precision
 |  | 8 bits | 23 bits |  | 
float32 |  |  |  |  | 
 |  | 5 bits | 10 bits |  | 
float16 |  |  |  |  | 
 |  | 8 bits | 7 bits |  | 
bfloat16 |  |  |  |  | 
 |  | 15 bits |  |  | 
int16 |  |  |  |  | 0.5
 |  | 7 bits |  |  | 
int8 |  |  |  |  | 0.5
Notes: The higher dynamic range of bfloat16 is useful for gradients. Float16 typically requires loss scaling, whereas bfloat16 can represent such gradients directly

## Slide 13: Data format summary
Integers are cheap, but their relative precision fluctuates
Floats are expensive, but their relative precision is constant
Other interesting data format is posit (https://posithub.org/docs/Posits4.pdf)
Range problem of integers can be solved by the fixed-point number format

## Slide 14: Fixed-point number format
Bit Width = Fractional (Word) Length + Integer (Word) Length + 1 (Sign)
Approximate real value by computing
Representable range: with precision/step size
0
0
1
0
1
0
1
0
Bit Width (8)
Fractional Length (4)
Integer
Length (3)
0
1
0
1
1
BW = 5
FL = 5
IL = -1

## Slide 15: Dynamic Fixed-point 16-bit multiplication example
0
0
1
0
1
0
1
0
BW = 8
FL = 4
0
1
0
1
1
BW = 5
FL = 5
1
1
0
0
1
1
1
0
1
0
0
0
FL = 5 + 4
BW = 8 + 5 – 1*

## Slide 16: Example: integer-based MAC data path
Inputs I
Weights W
X
+
Accumulator
K times
Operands width are or
Products width are
Accumulation width =
Scale
Input/output precision between layers is aligned using scale

## Slide 17: Overview of today’s lecture
Motivation
Data formats
Quantization schemes
    Linear (uniform) quantization
    Non-linear (non-uniform) quantization
    Codebook quantization
Quantization heuristics
Quantization procedures
Assignment 1 internals
Conclusion

## Slide 18: Linear (uniform) quantization
Linear implies constant step size
Step size is determined by the range of the tensor
    Symmetric mode
    Asymmetric mode
the quantized version of :
3 bits quantization example

## Slide 19: Symmetric mode
  Conventional fixed-point format
  Quantization range is symmetric around 0
  Step size given by:

## Slide 20: Asymmetric mode
  Useful when the distribution of values is not symmetric around 0
  Step size given by:
  Use a zero-point to shift the distribution:
  In practice, which means that zero is exactly representable by an integer in the quantized range

## Slide 21: Non-linear (non-uniform) quantization
Non-linear implies variable step size
    Variability follows a regular pattern:
      Example: power-of-two step
Concept:
    More likely (smaller) values should be more accurately quantized
    Less likely (larger) values should be coarsely quantized

## Slide 22: Codebook quantization
Useful when distribution of values is not normally distributed
Quantized values (codewords) are represented by a codebook
Codewords are selected using a clustering algorithm or training process
    E.g., values acquired by K-means clustering
Index | Value | Interval
0 | -0.07 | [-0.08, -0.04]
1 | 0 | [-0.04, 0.05]
2 | 0.01 | [0.05, 0.011]
3 | 0.012 | [0.011, 0,013]
Codebook example

## Slide 23: Quantization schemes summary
Scheme | Step size | Step size pattern
Linear | Fixed | Regular
Non-linear | Variable | Regular
Codebook | Variable | Irregular

## Slide 24: Overview of today’s lecture
Motivation
Data formats
Quantization schemes
Quantization heuristics
Quantization procedures
Assignment 1 internals
Conclusion

## Slide 25: Bit width selection
  Which data format do we use for weights/activations in each layer?
  Brute forcing the solution space is too costly…
  One bit width influences other choices
  We need to employ heuristics:
  Second derivative
  Learned quantization
  Something else?

## Slide 26: Second derivative as quantization heuristic
  The loss function can be expanded by a Taylor series for a single weight w:
  Assume a fully-trained network: weight w has converged into its (local) minimum ().
  Then, we approximate this minima with a parabola.
  The second derivative is a scalar that indicates the stability of the minima: the higher the scalar, the more the loss changes, when you introduce a quantization error ().
Loss
W*

## Slide 27: Second derivative heuristic for a
  In 1D calculus, our heuristic was simple.
  What about our many-dimensional network?
  The Hessian matrix is a square matrix of second-order partial derivatives of a scalar-valued function. It describes the local curvature of a function of many variables.
  How to compute and analyze the Hessian?

## Slide 28: Computing the Hessian
  Computing the Hessian (n by n matrix) is quite intensive and not feasible for networks with many parameters.
  For simplicity we ignore the off-diagonal elements, then our Hessian is a diagonal matrix. This implies its eigenvalues are on the diagonal.
  To calculate the diagonal, we now have two options:
  Directly calculate the 2nd derivatives
  Using RandNLA we can find the trace of the matrix (sum of the diagonal elements)

## Slide 29: Second derivative as quantization heuristic
  Using the Taylor expansion of the loss function and an approximated Hessian:
  We can directly calculate the effects of selecting a certain quantization bit width for weights and therefore try many possible solutions quickly.
  Note that this approach is also valid for activations.
Loss
W*

## Slide 30: Learned mixed-precision quantization
Concept: use a separate, reinforcement learning, (RL) neural network (RL agent) that has learned how select the bit width of each layer based on measurements on real hardware
Observation of the authors: Latency of quantized DNNs is highly dependent on the hardware platform
Full precision DNN
RL agent
Quantization policy
Predict
Hardware resource constraints
Fine-tune and map on hardware

## Slide 31: Training the RL agent
Full precision DNNs
RL agent
Quantization policy
Hardware evaluations
Resources < constraints?
No
Decrease bit width
Yes
DNN Accuracy as reward,
Update RL agent
Predict

## Slide 32: Quantization vs Pruning
  In previous lecture you have seen pruning, which removes a specific set of neurons. Or, in other words pruning sets weights to 0.
  Is this not identical to heavy quantization?
  No.. In quantization we are deviating a value slightly from its optimum.
  In pruning we typically deviate so much, the parabola approximation of a minimum is no longer valid.
  Note that the loss can stabilize even though a minimum is very sharp.
Loss
W*

## Slide 33: Overview of today’s lecture
Motivation
Data formats
Quantization schemes
Quantization heuristics
Quantization procedures
    Post-training quantization of a pretrained high-precision model
    Quantization-aware training
    Quantization of training procedure (not covered in this lecture)
Assignment 1 internals
Conclusion

## Slide 34: Post-training quantization
Typical procedure for an accumulator-constraint data path:
Range Analysis to determine minimum integer length
    Granularity: weights and/or activations within network, layer, or even channel?
Determine optimal bit width of fixed-point granularity group
    Using exhaustive testing (with heuristics) on validation set or analytical model?
Check if quality of final solution is sufficient. If not, do some fine-tuning

## Slide 35: 1. Determine Integer Length with Range Analysis
Forward small data set and monitor ranges.
Key observations:
    Weights and activations are clustered.
    Weights are small, activations are large.

## Slide 36: 1. Determine Integer Length with Range Analysis (2)
Determine integer length using heuristic:
    Problem: many bits wasted!

## Slide 37: 1. Determine Integer Length with Range Analysis (3)
Solution for dynamic range problem:
    Multiple fixed-point groups in layers → wide dynamic range!
    Only rescaling between layers → negligible overhead!

## Slide 38: Fixed-point group granularity
Figure 5.3. Top-1 accuracy for CaffeNet on ILSVRC 2014 validation dataset. Integer length refers to the number of bits assigned to the integer part of fixed point numbers.
Multiple fixed-point groups result in superior accuracy:

## Slide 39: Fixed-point group granularity (2)
Figure 10: Comparison of quantization-aware training schemes: Mobilenet-v1
Fine-grained per kernel quantization results in slightly better results:

## Slide 40: 2. Find fixed-point solution for every layer
Difficult problem: find the best bit width for every fixed-point group.
  Often boils down to testing many solutions on a small validation data set
  Valid combinations are platform-dependent, for example:
    Only 8-bit or 16-bit integer data types supported
    Accumulator is only 16-bit wide
Solution space for 4-layer DNN

## Slide 41: 3. Impact of post-quantization fine-tuning
Fig. 4. Top-1 accuracy drop of 8-bit networks. We show the accuracy difference between the approximated and the 32-bit FP network. Fine-tuned networks are denoted with FT. Our dynamic fixed point networks achieve best performance and are within 1% of the original network.
Fixed-point fine-tuning recovers some of the quantization precision loss.

## Slide 42: Quantization-aware training
Forward pass: simulated quantization to compute loss function
Backward pass: how to back propagate through the quantizers?

## Slide 43: Backpropagation: recap
Forward pass: for each training example. Compute the outputs for all layers
Backwards pass: compute cost derivatives iteratively from top to bottom:
Compute gradients and update weights
F1(x0, W1)
F2(x1, W2)
Fi(xi-1, Wi)
Fn(xn-1, Wn)
x0
x1
x2
xi-1
xi
xn-1
…
…
xn
(output)
(input)
E
C(Xn,Y)
y

## Slide 44: Quantizers: how to backpropagate?
quantize
quantize
Forward pass
Backward pass
4-bits
?
output
input

## Slide 45: Quantizers: how to backpropagate?
quantize
quantize
Forward pass
Backward pass
4-bits
Straight-through
estimator
output
input

## Slide 46: Quantization procedures – Summary
Approach | Training time | Quantization time | Quality of results
Quantization of pre-trained model | +++ | ++ | +
Quantization of pre-trained model with fine-tuning | ++ | + | ++ / +++
Quantization-aware training | + | +++ | +++
Quantized training procedure | ++* | +++ | +++
* on platforms that are specialized for high-throughput integer computations (e.g. FPGAs).

## Slide 47: Overview of today’s lecture
Motivation
Data formats
Quantization schemes
Quantization heuristics
Quantization procedures
Assignment 1 internals
Conclusion

## Slide 48: Quantizer implementation in PyTorch (IA assignment 1)
import math
import torch
pow2 = lambda x: math.pow(2,x)
def quantize(input, bits, frac_len, inplace=False):
# reduce precision
y = input if inplace else input.clone()
y.mul_(pow2(frac_len))
y.round_() # policy: Round half away from zero (ex: 23.5 becomes 24, -23.5 becomes -24)
y.mul_(pow2(-frac_len))
# clamp range
y_min = -pow2(bits-1) * pow2(-frac_len)
y_max = (pow2(bits-1)-1) * pow2(-frac_len)
y.clamp_(y_min, y_max)
return y
...
y = round(x)
Notes: Two interesting functions:
Round(): has derivative of zero everywhere (and infinite at tie-breaking point (in theory))
Clamp(): has derivative of 1 inside range and 0 outside

## Slide 49: Quantizer implementation in PyTorch (IA assignment 1)
...
# Create the graph and forward x
x = torch.tensor(2.0, requires_grad=True)
y = x ** 3
y.retain_grad()
z = quantize(y, bits=16, frac_len=8)
z.retain_grad()
# Backward pass: compute gradient of the output with respect to
# model parameters (all Tensors with requires_grad=True).
z.backward()
print(y.grad) # should print '1' which is dz/dy
print(x.grad) # should print '12' which is dz/dx
Actual console output:
>> tensor(0.)
>> tensor(0.)
Round() has derivative of zero almost everywhere. Result is actually correct, but not very useful!
Notes: The values that we get are correct, but not what we want.

## Slide 50: Quantizer implementation in PyTorch (IA assignment 1)
class Quantize(torch.autograd.Function):
"""
Symmetric Linear Quantizer. The forward pass reduces the precision and clamps the range.
The backward pass computes the unclipped Straight-Through Estimator (STE) i.e. the gradients
are not affected by this node.
"""
@staticmethod
def forward(ctx, input, bits, frac_len, inplace):
# reduce precision
y = input if inplace else input.clone()
y.mul_(pow2(frac_len))
y.round_() # policy: Round half away from zero (ex: 23.5 becomes 24, -23.5 becomes -24)
y.mul_(pow2(-frac_len))
# clamp range
y_min = -pow2(bits-1) * pow2(-frac_len)
y_max = (pow2(bits-1)-1) * pow2(-frac_len)
y.clamp_(y_min, y_max)
return y
@staticmethod
def backward(ctx, grad_output):
return grad_output, None, None, None # Straight-through estimator (unclipped). Only input needs gradient.
def quantize(input, bits, frac_len, inplace=False):
return Quantize.apply(input, bits, frac_len, inplace)

## Slide 51: Quantizer implementation in PyTorch (IA assignment 1)
...
# Create the graph and forward x
x = torch.tensor(2.0, requires_grad=True)
y = x ** 3
y.retain_grad()
z = quantize(y, bits=16, frac_len=8)
z.retain_grad()
# Backward pass: compute gradient of the output with respect to
# model parameters (all Tensors with requires_grad=True).
z.backward()
print(y.grad) # should print '1' which is dz/dy
print(x.grad) # should print '12' which is dz/dx
Actual console output:
>> tensor(1.)
>> tensor(12.)
Notes: The values that we get are correct, but not what we want.

## Slide 52: Summary – quantization for off-the-shelf platforms
For efficient deployment on embedded or mobile devices models are converted to integer-only arithmetic. We can either convert a pre-trained model to reduced-precision or train a quantized model from scratch.
A symmetric linear quantizer is a conventional fixed-point format. Asymmetric linear quantizers are used if the value distribution is not symmetric. Non-linear quantizers are sometimes used in the literature, but difficult to efficiently use on general-purpose platforms.
Multiple fixed-point groups are used to capture the different distributions within layers of the network more efficiently.
Typically, a number of quantization solutions will be tested, depending on the platform characteristics (supported data types and accumulator size).
Model fine-tuning or retraining is essential to recover some of the lost accuracy. Some measures needs to be taken to enable simulated quantized fine-tuning.

## Slide 53: Conclusions
Quantization is an essential tool for efficient model deployment
These techniques can be combined with other compression methods, such as pruning
8-bit data and weights with 32-bit accumulators is sufficient for recent DNNs
  Next up: extreme quantization (bitwise networks)
  For custom accelerators there is a huge shift from fixed-point to binary/ternary networks, which can potentially replace MACs by XNOR and POPCOUNT instructions
  Next lecture we will investigate the training and deployment of a bitwise networks