## Slide 1: Intelligent Architectures 5LIL0 Exploiting Data Reuse: From Loop Transformations to Halide
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/IA
h.corporaal@tue.nl
TUEindhoven
2021

## Slide 2: Application Excecution Time & Energy
High performance computing
Embedded computing
Small portions of the code dominate execution time
  Hot spots
  Loops
Apply Loop Transformations
for(i=0; i<N; i++){
for(j=0; j<N; j++){
for(k=0; k<N; k++)
c[i][j] += a[i][k] * b[k][j];
}}

## Slide 3: Loop Transformations
Can help you in many compute domains
CPU Code
Parallelism
Memory Hierarchy (multi-level caches)
Convert Loops to
GPU Threads
Embedded Devices
Fine-tune for architecture
ASICs & FPGAs
HDL, HW Description Languages

## Slide 4: Overview
RECAP: Constructing a DNN / CNN
  Neuron & Single layer
  Network: multiple layers
Energy
Loop transformations
  data flow
  reordering
  restructuring: tiling
Buffer management
  Store and Compute level

## Slide 5
Background: Artificial Neural Networks

## Slide 6: Artificial Neuron Model
Activation function:
Non Linear
Transformation
Dot Product

## Slide 7: Neuron Applied to Image Region
Neuron detects features in region
Convolution: Same neuron applied to all regions in the image yields an output feature map

## Slide 8: Input from multiple input (feature) maps
Input can be taken from multiple input feature maps

## Slide 9: Multiple neurons / convolutions
Multiple neurons generate multiple output feature maps

## Slide 10: Overview
RECAP: Constructing a DNN / CNN
  Neuron & Single layer
    Computational model of a single layer
  Network: multiple layers
Energy
Loop transformations
  data flow
  reordering
  restructuring: tiling
Buffer management
  Store and Compute level

## Slide 11: Convolution layer: Overview + Notation
N = batch size
C input feature maps of size HxW
M output feature maps of size ExF
M filters of size RxS
Note: for fully connected layer filter size is input size, RS = HW

## Slide 12: Convolution equations
U = stride
B = bias vector
Note: W has 4-dimensions
  i,j for kernel
  k for input feature maps
  u for output feature maps

## Slide 13: Convolution code, for 1 layer

## Slide 14: Several recent activation functions

## Slide 15: Computation Model of a CNN Layer
Input fmap
2
weights
X
Output fmap
1
=
Number of MACs = R x S x (H – R + 1) x (W - S + 1) x C
R
S
C
H
W
C
E
F
E
F

## Slide 16: Computation Model of a CNN Layer
Input fmap
X
Output fmap
=
M
weights
Number of MACs = R x S x (H – R + 1) x (W - S + 1) x C x M
M
Adding multiple (M) output Feature maps (fmap / output channels)
separate weights per output channel

## Slide 17: Overview
RECAP: Constructing a DNN / CNN
  Neuron & Single layer
  Network: multiple layers
Energy
Loop transformations
  data flow
  reordering
  restructuring: tiling
Buffer management
  Store and Compute level

## Slide 18: Sequence of feature maps forms the network

## Slide 19: How does it suffer from the memory wall?
CNN Accelerator
On Chip Memory
Data Path
MAC
MAC
MAC
MAC

## Slide 20: How does it suffer from the memory wall?
CNN Accelerator
On Chip Memory
Data Path
MAC
MAC
MAC
MAC

## Slide 21: How does it suffer from the memory wall?
CNN Accelerator
On Chip Memory
Data Path
MAC
MAC
MAC
MAC
A lot of data!
Weights
Intermediate data
Input data

## Slide 22: How does it suffer from the memory wall?
CNN Accelerator
On Chip Memory
External
Memory
Data Path
MAC
MAC
MAC
MAC
External memory needed to store all data

## Slide 23: How does it suffer from the memory wall?
CNN Accelerator
On Chip Memory
External
Memory
Data Path
MAC
MAC
MAC
MAC
Huge amount of traffic between external memory and the processor!*
* Note: Off-chip requires about 200x more energy than on-chip memory - Jonathan Ragan-Kelley, Decoupling Algorithms from the Organization of Computation for High Performance Image Processing

## Slide 24: Data Reuse – Ordering your computations
Data elements are used multiple times
Objective: Keep those uses close in time, and store data in on chip storage
All about ordering/scheduling
computations

## Slide 25: Overview
RECAP: Constructing a DNN / CNN
  Neuron & Single layer
  Network: multiple layers
Energy
Loop transformations
  data flow
  reordering
  restructuring: tiling
Buffer management
  Store and Compute level

## Slide 26: Where is the energy going

## Slide 27
Deep Convolutional Neural Networks
Contributes more than 90% of
overall computation and memory access,
dominating runtime and energy consumption
Source: ICIP Tutorial, 2019

## Slide 28: GoogLeNet: Energy
Yang.e.a CVPR'17
CNN layers: 21 depth, 57 in total
FC layer: 1
Weights: 7.0 M
MACs: 1.43 G per input

## Slide 29: Recap: what did we treat so far?
S
E (8)
M (23)
fp32
S
E(5)
M(10)
fp16
Quantization
Inference and Learning principles: Designing and Simulating a DNN
Improving Network Efficiency: Pruning, Quantization
Loop Optimizations - Software tricks to effectively use the Memory hierarchy

## Slide 30: VGG16 example
Conv layers: 13
FC Layers: 3
Weights: 138 M
MACs: 15.5 G per input
Simonyan, ICLR 2015

## Slide 31: Reducing external memory accesses: VGG16
Original code
Rescheduled code
Conclusion: we need advanced loop transformation to exploit data locality (in local buffers),
reducing external accesses

## Slide 32: Overview
RECAP: Constructing a DNN / CNN
  Neuron & Single layer
  Network: multiple layers
Energy
Loop transformations
  data flow transformations
  reordering
  restructuring: tiling
Buffer management
  Store and Compute level

## Slide 33: Data-Flow-Based Transformations
Can be very useful in case of a:
  Simple compiler
  Simple architecture
    No Hardware Multiplier
    No Out-Of-Order Superscalar
    No Speculative Branch Prediction
  If you are in a hurry and missing a few percent
These are the easy tricks
To get ready for the more difficult ones 
* Examples are from: D.F. Bacon, S.L. Graham, and O.J. Sharp, Compiler transformations for high-performance computing. ACM Comput. Surv. 26, (1994)

## Slide 34: Loop-Based Strength Reduction
Replace an expensive operation
Can be multiplication, especially for embedded cores
No HW multiplier, e.g. MicroBlaze
An optimizing compiler can help
c=3;
for(i=0; i<N; i++){
a[i] = a[i] + i*c;
}
c=3;
T=0;
for(i=0; i<N; i++){
a[i] = a[i] + T;
T = T + c;
}

## Slide 35: Induction Variable Elimination
Induction variable?
  Compute loop exit conditions
  Compute memory addresses
Given a known final value and relation to addresses
  Possible to eliminate index calculations
Again an optimizing compiler can help
A = &a[0];
T = &a[0] + N;
while(A<T){
*A = *A + c;
A++;
}
for(i=0; i<N; i++){
a[i] = a[i] + c;
}
Notes: Performing the control of a loop is basically overhead. I refer to the increment of i and the compare of i<N to check if the exit condition is not met.
With induction variable elimination we can reduce this overhead.

## Slide 36: Loop-Invariant Code Motion
Index of c[] does not change
Move one loop up and store in register
Reuse it over iterations of inner loop
Most compilers can perform this
Example is similar to Scalar Replacement Transformation
for(i=0; i<N; i++){
for(j=0; j<N; j++){
a[i][j]=b[j][i]+c[i];
}
}
for(i=0; i<N; i++){
T=c[i];
for(j=0; j<N; j++){
a[i][j]=b[j][i]+T;
}
}

## Slide 37: Loop Unswitching
Conditional execution inside a loop-body
  Move it outside the loop
  Each execution path independent loops
Increases code size
for(i=0; i<N; i++){
a[i] = b[i];
if(x<7){a[i]+=5;}
}
if(x<7){
for(i=0; i<N; i++){
a[i]=b[i];
a[i]+=5;
}
}
else{
for(i=0; i<N; i++){
a[i]=b[i];
}
}

## Slide 38: Overview
RECAP: Constructing a DNN / CNN
  Neuron & Single layer
  Network: multiple layers
Energy
Loop transformations
  data flow
  reordering
  restructuring: tiling
Buffer management
  Store and Compute level

## Slide 39: Iteration Reordering Transformations
Change the relative ordering
  Expose parallelism by altering iteration dependencies
  Improve locality by matching with a memory hierarchy
Normal compilers often don’t help you with this
Only state-of-the-art compilers can help
  Often research compilers ;)
*Based on:
M. Wolf, M. Lam, A Data Locality Optimizing Algorithm. ACM SIGPLAN, PLDI (1991)

## Slide 40: Loop representation as Iteration Space
for(i=0; i<N; i++){
for(j=0; j<N; j++){
A[i][j] = B[j+3][i+2];
Each position represents an iteration
  At each position 1 or more array elements are accessed

## Slide 41: Visitation order in Iteration Space
for(i=0; i<N; i++){
for(j=0; j<N; j++){
A[i][j] = B[j+3][i+2];
Iteration space is not data space

## Slide 42: But we don’t have to be regular
A[j][j] = B[j+3][i+2];
But order can have huge impact on:
  Memory Hierarchy
    E.g. Reuse of data
  Parallelism
  Loop or control overhead

## Slide 43: Can loop transformations reduce the memory wall?
CNN Accelerator
On Chip Memory
External
Memory
Data Path
MAC
MAC
MAC
MAC
Huge amount of traffic between external memory and the processor!*
* Note: Off-chip can require 200x more energy than on-chip memory

## Slide 44: Data Reuse – Ordering your computations
Data elements are used multiple times
Objective: Keep those uses close in time, and store data in on chip storage
All about ordering/scheduling
computations

## Slide 45: CNN: Just a Deep Loopnest
for l in layers:
for z in output_maps[l]:
for i in input_maps[l]:
for y in rows[l]:
for x in columns[l]:
for ky in kernel_height[l]:
for kx in kernel_widht[l]:
Y[l][z][x][y]+= X[l][i][x+kx][y+ky]* \
W[l][i][z][kx][ky]
Note: notation a little different; no Batch input, but Multiple layers in this code

## Slide 46: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];

## Slide 47: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];
j
0
0
N-1
M-1
i

## Slide 48: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];
j
0
0
i
j=0
i=0
N-1
M-1

## Slide 49: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];
j
0
0
i
j=0
i=1
N-1
M-1

## Slide 50: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];
j
0
0
i
j=0
i=2
N-1
M-1

## Slide 51: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];
j
0
0
i
j=0
i=M
N-1
M-1

## Slide 52: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];
j
0
0
i
j=1
i=0
N-1
M-1

## Slide 53: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];
j
0
0
i
j=2
i=0
N-1
M-1

## Slide 54: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];
j
0
0
i
Let’s have a look at the uses of
A[0]
N-1
M-1

## Slide 55: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];
j
0
0
i
Let’s have a look at the uses of
A[0]
Reuse distance of (M-1)
N-1
M-1

## Slide 56: Loop Interchange
for(j=0; j<N; j++)
for(i=0; i<M; i++) B[j][i]+=A[i];
j
0
0
i
Let’s have a look at the uses of
A[0]
N-1
M-1

## Slide 57: Loop Interchange
for(i=0; i<M; i++)
for(j=0; j<N; j++) B[j][i]+=A[i];
0
Let’s have a look at the uses of
A[0]
j
0
i
j=0
i=0
N-1
M-1

## Slide 58: Loop Interchange
for(i=0; i<M; i++)
for(j=0; j<N; j++) B[j][i]+=A[i];
0
Let’s have a look at the uses of
A[0]
j
0
i
j=1
i=0
N-1
M-1

## Slide 59: Loop Interchange
for(i=0; i<M; i++)
for(j=0; j<N; j++) B[j][i]+=A[i];
0
Let’s have a look at the uses of
A[0]
j
0
i
j=2
i=0
N-1
M-1

## Slide 60: Loop Interchange
for(i=0; i<M; i++)
for(j=0; j<N; j++) B[j][i]+=A[i];
0
Let’s have a look at the uses of
A[0]
j
0
i
j=0
i=1
N-1
M-1
Reuse distance of 0

## Slide 61: How can loop interchange help CNNs ?
for l in layers:
for z in output_maps[l]:
for i in input_maps[l]:
for x in columns[l]:
for y in rows[l]:
for ky in kernel_height[l]:
for kx in kernel_widht[l]:
Y[l][z][x][y]+= X[l][i][x+kx][y+ky]* \
W[l][i][z][kx][ky]
keep weights, input or outputs stationary

## Slide 62: Types of reuse in CNNs
Convolutional reuse
(sliding window)
Input map reuse
Filter reuse for larger batch size
Reuse
activations
weights
Reuse
activations
Reuse
weights

## Slide 63: Overview
RECAP: Constructing a DNN / CNN
  Neuron & Single layer
  Network: multiple layers
Energy
Loop transformations
  data flow
  reordering
  restructuring: tiling
Buffer management
  Store and Compute level

## Slide 64: Loop Tiling
for(j=0; j<N; j++)
for(i=0; i<M; i++)
B[j][i]+=A[i]+C[j];

## Slide 65: Loop Tiling
for(j=0; j<M; j++)
for(i=0; i<N; i++)
B[j][i]+=A[i]+C[j];
j
0
0
i
N-1
M-1

## Slide 66: Loop Tiling
for(j=0; j<M; j++)
for(i=0; i<N; i++)
B[j][i]+=A[i]+C[j];
j
0
0
i
N-1
M-1

## Slide 67: Loop Tiling
for(j=0; j<M; j++)
for(i=0; i<N; i++)
B[j][i]+=A[i]+C[j];
j
0
0
i
Reuse distances of:
A[0] = M-1
C[0] = 0
N-1
M-1

## Slide 68: Loop Tiling
for(j=0; j<M; j++)
for(i=0; i<N; i++)
B[j][i]+=A[i]+C[j];
j
0
0
i
Reuse distances of:
A[0] = M-1
C[0] = 0
For M=8 a memory of size 5 with LRU policy would miss A[0]
N-1
M-1

## Slide 69: Loop Tiling
for(i=0; i<M; i++)
for(j=0; j<N; j++)
B[j][i]+=A[i]+C[j];
j
0
0
i
Reuse distances of:
A[0] = M-1
C[0] = 0
N-1
M-1

## Slide 70: Loop Tiling
for(i=0; i<M; i+=Ti)
for(j=0; j<N; j++)
for(ii=0; ii<i+Ti;ii++)
B[j][ii]+=A[ii]+C[j];
0
Reuse distances of:
A[0] = M-1
C[0] = 0
j
0
0
i
N-1
M-1

## Slide 71: Loop Tiling
for(i=0; i<M; i+=Ti)
for(j=0; j<N; j++)
for(ii=0; ii<i+Ti;ii++)
B[j][ii]+=A[ii]+C[j];
j
0
0
i
N-1
M-1
Reuse distances of:
A[0] = M-1  Ti-1
C[0] = 0  0 / N-1

## Slide 72: Loop Tiling
for(i=0; i<M; i+=Ti)
for(j=0; j<N; j++)
for(ii=0; ii<i+Ti;ii++)
B[j][ii]+=A[ii]+C[j];
j
0
0
i
Reuse distances of:
A[0] = M-1  Ti-1
C[0] = 0  0 / j*Ti-1
For M=8 a memory of size 5 with LRU policy would hit A and C*
* Except when: (i mod Ti) = 0 and j=0
N-1
M-1

## Slide 73: Study a matrix multiplication : Loop interchange
for(i=0; i<Bi; i++){
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
C[i][j] += A[i][k] * B[k][j];
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
for(i=0; i<Bi; i++){
C[i][j] += A[i][k] * B[k][j];

## Slide 74: Adding Loop tiling
Can be done in multiple dimensions
Manual exploration is intractable
for(i=0; i<Bi; i++){
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
C[i][j] += A[i][k] * B[k][j];
for(i=0; i<Bi; i++){
for(jj=0; jj<Bj; jj+=Tj){
for(k=0; k<Bk; k++){
for(j=jj; j<jj+Tj; j++)
C[i][j] += A[i][k] * B[k][j];

## Slide 75: Overview
RECAP: Constructing a DNN / CNN
  Neuron & Single layer
  Network: multiple layers
Energy
Loop transformations
  data flow
  reordering
  restructuring: tiling
Buffer management
  Store and Compute level

## Slide 76: Scratchpads: explicit scheduling of memory transfers
CNN Accelerator
On Chip Scratchpad Memory
Data Path
MAC
MAC
MAC
MAC

## Slide 77: Introducing: Store level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Implementation for 1 (input and output) Feature map*
*Weights omitted
Filter kernel

## Slide 78: Introducing: Store level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
x
y
Ky
Kx

## Slide 79: Introducing: Store level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
x
y
Ky
Kx

## Slide 80: Introducing: Store level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
x
y
Ky
Kx

## Slide 81: Introducing: Store level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
x
y
Ky
Kx

## Slide 82: Introducing: Store level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Ky
Kx

## Slide 83: Introducing: Store level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Ky
Kx
Store level says what to store in local buffer (volume for 1 iteration)
For every iteration of y, we load
all required data once

## Slide 84: Introducing: Store level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Ky
Kx
Store level says what to store in local buffer (volume for 1 iteration)
For every iteration of y, we load
all required data once

## Slide 85: Introducing: Store level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Ky
Kx
Store level says what to store in local buffer (volume for 1 iteration)
For every iteration of x, we load
all required input data once

## Slide 86: Introducing: Store level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Store level says what to store in local buffer (volume for 1 iteration)
For every iteration of x, we load
all required input data once
Missed overlap!
But less buffer space required than higher store level.

## Slide 87: Transfer volume != Buffer size
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Ky
Kx

## Slide 88: Transfer volume != Buffer size
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Ky
Kx
Live volume at any time is only KxKy

## Slide 89: Transfer volume != Buffer size
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Ky
Kx
Live volume at any time is only KxKy

## Slide 90: Transfer volume != Buffer size
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Ky
Kx
Live volume at any time is only KxKy

## Slide 91: Introducing: Compute Level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Ky
Kx
Live volume at any time is only KxKy
By not transferring data at the start of y, but later a smaller buffer is required.

## Slide 92: Introducing: Compute Level
for y from 0->Dy:
for x from 0->Dx:
for l from 0->Ky:
for k from 0->Kx:
out[x][y]+=in[x+kx][y+ky]
Store Level
x
y
Ky
Kx
Live volume at any time is only KxKy
Compute level determines when data is transferred
Compute lvl

## Slide 93: Pareto front of 6 CNNs
VDSR
Traffic Sign Detect
VGG16
Resnet 101
Resnet 152
MobileNet V2
Orders of Magnitude better than baseline!

## Slide 94
#pragma omp parallel for
for (int yTile = 0; yTile < out.height(); yTile += 32) {
__m128i a, b, c, sum, avg;
__m128i tmp[(128/8) * (32 + 2)];
for (int xTile = 0; xTile < out.width(); xTile += 128) {
__m128i *tmpPtr = tmp;
for (int y = 0; y < 32+2; y++) {
const uint16_t *inPtr = &(in(xTile, yTile+y));
for (int x = 0; x < 128; x += 8) {
a = _mm_load_si128((const __m128i*)(inPtr));
b = _mm_loadu_si128((const __m128i*)(inPtr+1));
c = _mm_loadu_si128((const __m128i*)(inPtr+2));
sum = _mm_add_epi16(_mm_add_epi16(a, b), c);
avg = _mm_mulhi_epi16(sum,one_third);
_mm_store_si128(tmpPtr++, avg);
inPtr+=8;
}
}
tmpPtr = tmp;
for (int y = 0; y < 32; y++) {
__m128i *outPtr = (__m128i *)(&(out(xTile, yTile+y)));
for (int x = 0; x < 128; x += 8) {
a = _mm_load_si128(tmpPtr+(2*128)/8);
b = _mm_load_si128(tmpPtr+128/8);
c = _mm_load_si128(tmpPtr++);
sum = _mm_add_epi16(_mm_add_epi16(a, b), c);
avg = _mm_mulhi_epi16(sum, one_third);
_mm_store_si128(outPtr++, avg);
}
}
}
}
Code can become extremely complex after some transformations !!

## Slide 95
#pragma omp parallel for
for (int yTile = 0; yTile < out.height(); yTile += 32) {
__m128i a, b, c, sum, avg;
__m128i tmp[(128/8) * (32 + 2)];
for (int xTile = 0; xTile < out.width(); xTile += 128) {
__m128i *tmpPtr = tmp;
for (int y = 0; y < 32+2; y++) {
const uint16_t *inPtr = &(in(xTile, yTile+y));
for (int x = 0; x < 128; x += 8) {
a = _mm_load_si128((const __m128i*)(inPtr));
b = _mm_loadu_si128((const __m128i*)(inPtr+1));
c = _mm_loadu_si128((const __m128i*)(inPtr+2));
sum = _mm_add_epi16(_mm_add_epi16(a, b), c);
avg = _mm_mulhi_epi16(sum,one_third);
_mm_store_si128(tmpPtr++, avg);
inPtr+=8;
}
}
tmpPtr = tmp;
for (int y = 0; y < 32; y++) {
__m128i *outPtr = (__m128i *)(&(out(xTile, yTile+y)));
for (int x = 0; x < 128; x += 8) {
a = _mm_load_si128(tmpPtr+(2*128)/8);
b = _mm_load_si128(tmpPtr+128/8);
c = _mm_load_si128(tmpPtr++);
sum = _mm_add_epi16(_mm_add_epi16(a, b), c);
avg = _mm_mulhi_epi16(sum, one_third);
_mm_store_si128(outPtr++, avg);
}
}
}
}
Func blur_3x3(Func in) {
Func bx, by;
Var x, y, xi, yi;
// The algorithm - no storage or order
bx(x, y) = (in(x-1, y) + in(x, y) + in(x+1, y));
by(x, y) = (bx(x, y-1) + bx(x, y) + bx(x, y+1));
// The schedule - defines order, locality; implies storage
by.tile(x, y, xi, yi, 128, 32)
.vectorize(xi, 8).parallel(y);
bx.compute_at(by, x).vectorize(x, 8);
return by;
}
Halide alternative

## Slide 96: Main Take-Aways
Data-Flow-Based Transformations
  Good compilers can help
Iteration Reordering Transformations
  High-level transformations
  Compilers are often not enough
  Huge gains for parallelims and locality/data reuse
  Be carefull with dependencies
Loop Restructuring Transformations
  Similar to reordering
Halide can help you