## Slide 1: Optimizing neural networks for deployment and execution
Quantization: from float32 to int8 and beyond
Floran de Putter
Electrical Engineering – Electronic Systems group

## Slide 2: Recap optimization lectures
Pruning
  Eliminating as many neurons/connections as possible while preserving accuracy
Quantization
  Transforming a real-valued number to a finite number of distinct values while preserving accuracy
Data reuse
  Preventing costly data movements as much as possible
  Does not influence the accuracy
Today: extreme quantization

## Slide 3: Extreme quantization
Usually 8-bit quantization is sufficient for many applications
Can we do better?
Yes, to the extremes:
  Binary values
    Single bit per symbol
  Ternary values
    1.585 bits per symbol ()
Reminder: during training all values are kept in full-precision!

## Slide 4: Overview of today’s lecture
Recap
Preliminary
  Binary and ternary quantization
  Backwards pass
Naive binary neural network
Overview of common repair methods
Specialized bitwise accelerators
Summary and conclusions

## Slide 5: Basic operation of DNNs
Convolutional layer:
  Large number of (floating-point) multiplications and additions
  MAC is the majority of calculations during inference
Inputs A
Weights W
X
+
Accumulator
K times
Non-linear activation

## Slide 6: Binary quantization
function is used for binarization:
Convolutional layer becomes:
denotes binary multiply-accumulate!

## Slide 7: Binary multiply-accumulate
Multiplication and addition are replaced by bitwise XNOR and PopCount.
Why and not ?
  XNOR- vs AND-gate multiply
+2
0
1
1
1
0
1
0
0
1
1
0
0
+2
-1
+1
+1
+1
-1
+1
-1
-1
XNOR
PopCount
Mul
Accumulate
+1
+1
-1
-1

## Slide 8: Binary convolutions – savings
Savings on off-the-shelf platforms (compared to float32 version):
  Memory size and accesses: 1/32 → memory energy savings: >32x*
  Speedup:
    CPU (64-bit): ~58x**
    GPU: ~23x***
  Energy per operation:
    *→ bitwise XNOR
    + → popcount
    We will see the Joules/Op later
Reminder: with quantization comes accuracy loss!
Notes: XNOR-net has the following repairs already:
Scaling factors
Pooling layer before activation

## Slide 9: Ternary quantization
Popular definition for ternarization is as follows:
Convolutional layer becomes:
denotes ternary multiply-accumulate!

## Slide 10: Ternary multiply-accumulate
Ternary encoding requires 1.585 bits per symbol ()
  In practice we need to use 2 bits
Example encoding from GXNOR-Net:
Other encodings are possible too!
Encoding | 
+1 | 11
0 | 00
-1 | 10

## Slide 11: Ternary multiply-accumulate
+1
10
11
00
11
10
11
00
10
11
11
10
10
+1
-1
+1
0
+1
-1
+1
0
-1
Multiplication and addition are replaced by Gated XNORs and two PopCounts.
GX(N)OR
PopCount
Mul
Accumulate
+1
+1
-1
-1
Encoding | 
+1 | 11
0 | 00
-1 | 10

## Slide 12: Gated XNOR and ternary MAC implementation
Gated XNOR:
Gated XOR:
x[msb]
y[msb]
x[lsb]
y[lsb]
x[lsb]
y[lsb]
Popcount +1’s
Popcount -1’s
-
Encoding | 
+1 | 11
0 | 00
-1 | 10
x[msb]
y[msb]
1 if non-zero

## Slide 13: Backwards pass: how to backpropagate?
quantize
quantize
Forward pass
Backward pass
?

## Slide 14: Backwards pass: how to backpropagate?
quantize
quantize
Forward pass
Backward pass
Straight-through
estimator

## Slide 15: Backwards pass: how to backpropagate?
quantize
quantize
Forward pass
Backward pass
Clipped
straight-through
estimator
Straight-through
estimator

## Slide 16: Overview of today’s lecture
Recap
Preliminary
Naive binary neural network
Overview of common repair methods
Specialized bitwise accelerators
Summary and conclusions

## Slide 17: Naive BNN: BinaryNet
  VGG9 architecture
  CIFAR10 dataset
  First and last layer remain full precision (orange blocks)
  Convolution and linear (red blocks) are fully binary!
  Binarization using sign-function with clipped straight-through estimator
  88.6% top-1 accuracy, promising results?
batchnorm
sign
3x3 conv
batchnorm
sign
3x3 conv
batchnorm
sign
3x3 conv
batchnorm
sign
linear
linear
batchnorm
sign
linear
batchnorm
sign
3x3 conv
maxpool
batchnorm
sign
3x3 conv
maxpool
batchnorm
sign
3x3 conv
maxpool

## Slide 18: BinaryNet on ImageNet
  ImageNet
  ResNet-18 architecture as base
  ResNet uses Basic block:
From 69.7% to 42.2% top-1 accuracy on ImageNet…
ResNet-18 architecture
batchnorm
sign
3x3 conv
batchnorm
sign
3x3 conv
+

## Slide 19: Accuracy of state-of-the-art BNNs
Chart: ResNet-18 based BNNs
| FP ResNet18 | BinaryResNet | ABCNet | GroupNet | ReActNet
Accuracy | 69.7 | 42.2 | 65 | 67 | 65.9
Note: accuracy repair methods do not come for free!

## Slide 20: Overview of today’s lecture
Recap
Preliminary
Naive binary neural network
Overview of common repair methods
  ABCNet
  GroupNet
  ReActNet
Specialized bitwise accelerators
Summary and conclusions

## Slide 21: ABC-Net – intuition
Say you want to binarize :
With two bases (zero and one) we can derive a more accurate bound:
After evaluating and we can determine in what range lies:
This predicate holds for

## Slide 22: ABC-Net – weight approximation
Estimate real-value weights using a linear combination of binary filters , , …, , such that the full precision weights are estimated as
Every binary base , is constructed using a user-defined set of shifting parameters over the standard deviation i.e.
Scaling parameters , are calculated by solving the following linear regression problem for every i.e.

## Slide 23: ABC-Net – weight approximation implementation
Observations:
    Binarized input data is the same for all binary convolutions.
    Binary convolutional workload increases by the number of bases.
Approximate weights using 3 binary bases
Conv
BinConv
BinConv
BinConv
+

## Slide 24: ABC-Net – weight approximation numerical example
Say you want to approximate by three binary bases .
, then bases are:
From, it follows that , thus
Notes: Idea: with binary weights and scaling factors you can recover the original weights.
Python code:
import numpy as np
vec = lambda x: x.flatten() # matrix to vector
sign = lambda x: np.where(x >= 0, 1, -1) # sign activation
# base parameters and input weights
u = [-1, 0, 1]
W = np.array([[-0.135, -0.065],[0.125, 0.075]])
# compute reconstruction
mu, std = np.mean(W), np.std(W, ddof=1)
B = np.array([vec(sign(W - mu + i*std)) for i in u]) # compute bases
a, _, _, _ = np.linalg.lstsq(B.T, vec(W))
W_hat = (B * a[:,None]).sum(axis=0).reshape(W.shape)

## Slide 25: ABC-Net – activation approximation
Full precision activations are estimated with binary bases using a similar idea as weights:
Each activation is binarized for every base as follows using shift vector :
This approximates a bounded rectifier activation!
Two examples (assuming , for simplicity):
  3 bases;
  10 bases;
Notes: import numpy as np
import matplotlib.pyplot as plt
sign = lambda x: np.where(x >= 0, 1, -1) # sign activation
clip = lambda x: np.clip(sign(x), 0, 1)
v1 = np.linspace(-1/5,1/5,3)
v2 = np.linspace(-1,1,10)
x = np.linspace(-10,5,1000)
y1 = np.array([clip(x+i) for i in v1]).sum(axis=0)
y2 = np.array([clip(x+i) for i in v2]).sum(axis=0)
fig,ax = plt.subplots(dpi=80)
ax.scatter(x, y1, marker='.', c='r')
ax.scatter(x, y2, marker='.', c='b')
ax.set_xlabel("x", fontsize=18)
ax.set_ylabel("y", fontsize=18)
ax.set_title("y = sum(clip(x+v_i, 0, 1))", fontsize=18)
plt.xticks(fontsize=14)
plt.yticks(fontsize=14)
ax.spines['right'].set_visible(False)
ax.spines['top'].set_visible(False)
ax.set_xlim([-2,2])

## Slide 26: ABC-Net – block structure
  Convolution becomes:
  Workload increases by plus some scaling multiplications
  Number of weights increases by times (number of weight bases)
Approximated convolution
Binary weights and activations
Shifted Sign
BatchNorm
ApproxConv
Shifted Sign
Shifted Sign
ApproxConv
ApproxConv
Weighted Sum
Weighted Sum
BinConv
BinConv
BinConv

## Slide 27: Group-Net
Group-wise creation of binary bases instead of layer-wise
  Quantization error is accumulated less
Binary base weights are learned
Workload increases by plus some scaling multiplications
Number of weights increases by times
BinConv
BinConv
BinConv
+
BinConv
BinConv
BinConv
+
ABCNet layer-wise expansion
BinConv
BinConv
BinConv
BinConv
BinConv
BinConv
+
GroupNet group-wise expansion

## Slide 28: ReActNet
  More residuals to improve information flow
  RSign and RPReLU
    Channel-wise bias
BatchNorm
Conv
+
ReLU
BatchNorm
Conv
ReLU
BatchNorm
BinaryConv
+
RSign
BatchNorm
BinaryConv
+
RSign
RPReLU
RPReLU
ReActNet basic block
ResNet basic block

## Slide 29: Repair methods summary
More input/output feature maps
  ABCNet
  GroupNet
Distribution shifts using biases
  ABCNet
  ReActNet
Full-precision scaling factors
  ABCNet (per binary base)
  GroupNet (per binary base)
  ReActNet (per channel, not shown in this lecture)
More residuals
  ReActNet

## Slide 30: Overview of today’s lecture
Recap
Preliminary
Naive binary neural network
Overview of common repair methods
Specialized bitwise accelerators
Summary and conclusions

## Slide 31: Specialized BNN/TNN accelerators
Binary:
  XNOR Neural Engine: a Hardware Accelerator IP for 21.6 fJ/op Binary Neural Network Inference – Conti et al. (2018)
  A 617TOPS/W All Digital Binary Neural Network Accelerator in 10nm FinFET CMOS – Knag et al. (2020)
  An Always-On 3.8μJ/86% CIFAR-10 Mixed-Signal Binary CNN Processor with All Memory on Chip in 28nm CMOS – Bankman et al. (2018)
Ternary:
  CUTIE: Beyond PetaOp/s/W Ternary DNN Inference Acceleration with Better-than-Binary Energy Efficiency – Scherer et al. (2020)

## Slide 32: XNOR Neural engine – System on Chip overview

## Slide 33: XNE accelerator overview
Streamer
  TP x 32-bit memory interface for input data, weights, and activations.
  Address generation and word-alignment functionality.
Controller
  Small 28 Byte register file to load layer configuration for execution.
  Small micro-processor to generate loop counters and addresses.
Engine
  XNE datapath that can processor binary convolution and fully-connected layers.
Throughput Parameter TP = 4

## Slide 34: XNE engine
  TP XNORs are computed in parallel
  Input data is stored in Feature Register
  A new weight bit vector is loaded every cycle
  PopCount can be masked
  16-bit accumulators are used to compute TP pixels
  Dedicated threshold stage
  21.6 fJ per operation in 22nm!
Throughput Parameter TP = 8

## Slide 35: All Digital Binary Neural Network Accelerator
  Compute Near Memory design principle
  Increase energy efficiency by interleaving memory sub-arrays and (MAC) units
  Smaller sub-arrays reduce weight access energy and shorter interconnect decreases weight routing energy
  1.62 fJ/OP in 10nm FinFET!

## Slide 36: Mixed-Signal Binary CNN Processor
  Mix of digital and analog computation
  Accumulation (popcount operation) is done in analog fashion
  Only on-chip memory to reduce data transfer cost
  1.30 fJ/OP in 28nm CMOS!

## Slide 37: CUTIE: Ternary DNN Inference
  Completely unrolled data path w.r.t. all feature map and filter dimensions to reduce data transfer cost
  Capitalizes on the inherent sparsity of TNNs and tunes training methods to increase sparsity. Reduces switching activity
  0.32 fJ/Op in 7 nm!

## Slide 38: BNN/TNN accelerator limitations
Most accelerators assume that all data can be stored on-chip
  Not valid for large networks -> Costly memory traffic is ignored
Most accelerators assume they can directly calculate an output pixel
  Not valid for large networks -> partial high-bitwidth sums!
Most accelerators cannot skip the thresholding phase
  Needed for state-of-the-art BNNs
Most accelerators fix the amount of input/output channels
  Flexibility issue

## Slide 39: Summary and conclusion
BNNs or TNNs might be the holy grail for running DNNs on the edge
MAC can be replaced by cheap bitwise operations: XNOR and Popcount
There is still some research required to make them competitive in terms of accuracy without a large increase in computational workload
State-of-the-art BNN/TNN accelerators achieve down to ≤1fJ/Op