## Slide 1: Intelligent Architectures 5LIL0 Network Restructuring
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/IA
h.corporaal@tue.nl
TUEindhoven
2021

## Slide 2: Overview
We discussed 3 DNN optimizations:
  Pruning, reducing connections / neurons
  Quantization, from 32-bits float to …. 1-bit binary NWs
  Scheduling to exploit data reuse and vector&thread-parallelim
In this lecture a 4th optimization, related to pruning:
  Changing the Network Structure
    filter decomposition
    Structured approaches
But first some Halide scheduling options

## Slide 3: Brightening an Image Example Halide code:
#include "halide_image_io.h"
using namespace Halide::Tools;
Halide::Buffer<uint8_t> input = load_image("image_name");
Halide::Func brighter;
Halide::Var x, y, c;
Halide::Expr value = input(x, y, c);
value = Halide::cast<float>(value);
value = value * 1.5f;
value = Halide::min(value, 255.0f);
value = Halide::cast<uint8_t>(value);
Halide::Buffer<uint8_t> output = brighter.realize(input.width(),input.height(), input.channels());
save_image(output, "brighter.png");
More info on I/O
Notes: // A 'Func' object represents a pipeline stage. It's a pure // function that defines what value each pixel should have.
You // can think of it as a computed image.
Halide::Func gradient; // Var objects are names to use as variables in the definition of // a Func. They have no meaning by themselves. Halide::Var x, y; // We typically use Vars named 'x' and 'y' to correspond to the x // and y axes of an image, and we write them in that order. If // you're used to thinking of images as having rows and columns, // then x is the column index, and y is the row index. // Funcs are defined at any integer coordinate of its variables as // an Expr in terms of those variables and other functions. // Here, we'll define an Expr which has the value x + y. Vars have // appropriate operator overloading so that expressions like // 'x + y' become 'Expr' objects.

## Slide 4: Implementing Convolutional Layers
Dataflow taxonomy:
  Output Stationary: minimize movement of partial sums
  Weight Stationary: minimize movement of weights
  Input Stationary: minimize movement of inputs
filter weight fmap activation partial sum
updated partial sum
Memory Read MAC Memory Write

## Slide 5: 1D Convolution – Output Stationary (OS)
int I[H]; // Input activations
int W[R]; // Filter weights
int O[E]; // Output activations
for (e = 0; e < E; e++)
for (r = 0; r < R; r++)
O[e] += I[e+r] * W[r];
R
Weights
H
Inputs
E = H-R+1
Outputs
*
=
e = 0:
  O[0] += I[0]*W[0]
  O[0] += I[1]*W[1]
  O[0] += I[2]*W[2]

## Slide 6: 1D Convolution – Output Stationary (OS)
int I[H]; // Input activations
int W[R]; // Filter weights
int O[E]; // Output activations
for (e = 0; e < E; e++)
for (r = 0; r < R; r++)
O[e] += I[e+r] * W[r];
R
Weights
H
Inputs
E = H-R+1
Outputs
*
=
Output movement is minimum
e = 1:
  O[1] += I[1]*W[0]
  O[1] += I[2]*W[1]
  O[1] += I[3]*W[2]

## Slide 7: 1D Convolution – Output Stationary (OS)
for (e = 0; e < E; e++)
for (r = 0; r < R; r++)
O[e] += I[e+r] * W[r];
Func I, W, O;
Var x, e;
I(x) = x; // I = {0, 1, 2, 3, 4, 5}
W(x) = 1; // W = {1, 1, 1}
RDom r(0, 3); // r iterates from 0 to 2
O(e) = 0;
O(e) += I(e + r) * W(r);
O.trace_stores();
Buffer<int32_t> output = O.realize(4);
O.print_loop_nest();
produce O:
for e:
O(...) = ...
for e:
for r:
O(...) = ...
Store O.0(0) = 0
Store O.0(1) = 0
Store O.0(2) = 0
Store O.0(3) = 0
Store O.0(0) = 0
Store O.0(0) = 1
Store O.0(0) = 3
Store O.0(1) = 1
Store O.0(1) = 3
Store O.0(1) = 6
Store O.0(2) = 2
Store O.0(2) = 5
Store O.0(2) = 9
Store O.0(3) = 3
Store O.0(3) = 7
Store O.0(3) = 12
Initialize by 0
Final output
Study for more details: section 9 of the Halide tutorial
Notes: RDom
Say we want an update that multiplies the first 10 rows by 3. We could do this by adding 10 update definitions. But it is easier to do it using a "reduction domain" and using it inside an update definition.
RDom r(0, 10);
f(x, r) = 3 * f(x, r);
If you want to study these in more depth with examples and visualizations I would strongly recommend you to quickly browse through section 9 of the Halide tutorial.

## Slide 8: 1D Convolution – Weight Stationary (WS)
int I[H]; // Input activations
int W[R]; // Filter weights
int O[E]; // Output activations
for (r = 0; r < R; r++)
for (e = 0; e < E; e++)
O[e] += I[e+r] * W[r];
R
Weights
H
Inputs
E = H-R+1
Outputs
*
=
r = 0:
  O[0] += I[0]*W[0]
  O[1] += I[1]*W[0]
  O[2] += I[2]*W[0]
  …
  O[E-1] += I[E-1]*W[0]

## Slide 9: 1D Convolution – Weight Stationary (WS)
int I[H]; // Input activations
int W[R]; // Filter weights
int O[E]; // Output activations
for (r = 0; r < R; r++)
for (e = 0; e < E; e++)
O[e] += I[e+r] * W[r];
R
Weights
H
Inputs
E = H-R+1
Outputs
*
=
Weight movement is minimum
r = 1:
  O[0] += I[1]*W[1]
  O[1] += I[2]*W[1]
  O[2] += I[3]*W[1]
  …
  O[E-1] += I[E]*W[1]

## Slide 10: 1D Convolution – Weight Stationary (WS)
for (r = 0; r < R; r++)
for (e = 0; e < E; e++)
O[e] += I[e+r] * W[r];
Func I, W, O;
Var x, e;
I(x) = x; // I = {0, 1, 2, 3, 4, 5}
W(x) = 1; // W = {1, 1, 1}
RDom r(0, 3); // r iterates from 0 to 2
O(e) = 0;
O(e) += I(e + r) * W(r);
O.update(0).reorder(e, r); //inner, outer
O.trace_stores();
Buffer<int32_t> output = O.realize(4);
O.print_loop_nest();
produce O:
for e:
O(...) = ...
for r:
for e:
O(...) = ...
Store O.0(0) = 0
Store O.0(1) = 0
Store O.0(2) = 0
Store O.0(3) = 0
Store O.0(0) = 0
Store O.0(1) = 1
Store O.0(2) = 2
Store O.0(3) = 3
Store O.0(0) = 1
Store O.0(1) = 3
Store O.0(2) = 5
Store O.0(3) = 7
Store O.0(0) = 3
Store O.0(1) = 6
Store O.0(2) = 9
Store O.0(3) = 12
Initialize by 0
Final output
Note: update(0) indicates first non-functional update of O(e)
Notes: Func::update(int):
Assume that you want to define a function for the first time like:
f (x, y) = x + 2 * y;
This first definition is called the "pure" definition. Then, let's assume you want to change a particular point:
f (20, 10) = 33;
These extra definitions are called "update" definitions or "reduction" definitions. A reduction definition is an update definition that recursively refers back to the function's current value at the same site. If we confine our update to a single row, we can recursively refer to values in the same column:
f(x, 0) = f(x, 8);
For each realization of f, each step runs in its entirety before the next one begins. You can test this with trace_loads/stores() if you like.
We use Func::update(int) to get a handle to an update step for the purposes of scheduling. The following line vectorizes the second update step across x.
f.update(1).vectorize(x, 4);

## Slide 11: 1D Convolution – Input Stationary (IS)
int I[H]; // Input activations
int W[R]; // Filter weights
int O[E]; // Output activations
for (h = 0; h < H; h++)
for (r = 0; r < R; r++)
O[h-r] += I[h] * W[r];
R
Weights
H
Inputs
E = H-R+1
Outputs
*
=
h = 0:
  O[0] += I[0]*W[0]
Beware h-r must be >= 0 and <E

## Slide 12: 1D Convolution – Input Stationary (IS)
int I[H]; // Input activations
int W[R]; // Filter weights
int O[E]; // Output activations
for (h = 0; h < H; h++)
for (r = 0; r < R; r++)
O[h-r] += I[h] * W[r];
R
Weights
H
Inputs
E = H-R+1
Outputs
*
=
h = 1:
  O[1] += I[1]*W[0]
  O[0] += I[1]*W[1]
Beware h-r must be >= 0 and <E

## Slide 13: 1D Convolution – Input Stationary (IS)
int I[H]; // Input activations
int W[R]; // Filter weights
int O[E]; // Output activations
for (h = 0; h < H; h++)
for (r = 0; r < R; r++)
O[h-r] += I[h] * W[r];
R
Weights
H
Inputs
E = H-R+1
Outputs
*
=
h = 2:
  O[2] += I[2]*W[0]
  O[1] += I[2]*W[1]
  O[0] += I[2]*W[2]
Beware h-r must be >= 0 and <E
Input movement is minimum
Because the iteration order is not rectangular anymore, we cannot implement input stationary in Halide

## Slide 14: 2D Convolution for CNNs
Func input, weights, output;
Var x, y, c;
RDom k(0, kernel_widht, 0, kernel_height, 0, input_maps);
output(x, y, c) += weights(k.x, k.y, k.z, c) * input(x + k.x, y + k.y, k.z);
for c in output_maps:
for y in rows:
for x in columns:
for kz in input_maps:
for ky in kernel_height:
for kx in kernel_widht:
output[c][y][x]+= input[kz][y+ky][x+kx] * \
W[c][kz][ky][kx]

## Slide 15: Overview
We discussed 3 DNN optimizations:
  Pruning, reducing connections / neurons
  Quantization, from 32-bits float to …. 1-bit binary NWs
  Scheduling to exploit data reuse and vector&thread-parallelim
  Changing the Network Structure
    filter decomposition
    Structured approaches

## Slide 16: Pruning: reduce the Network
Fine grain pruning
  removing connections with small weigths
  remove neurons
Coarse grain pruning
  remove kernel (2D): i.e., skip input feature map for a certain filter
  removing complete filter (3D), i.e. reduce nr. of output feature maps
Structured pruning:
  try to keep e.g. SIMD regularity (vector computing)
Typically fine tune weights after pruning steps

## Slide 17: Reducing filter sizes: filter decomposition

## Slide 18: Remember the CNN terminology (single layer)
N = batch size
C input feature maps of size HxW
M output feature maps of size ExF
M filters of size RxS
Total filter size = Mx (RxSxC)
Dream this picture !

## Slide 19: Reducing filter sizes: decouple correlations
+
Decouple the cross-channels correlations and spatial correlations in the feature maps of the DNN: depth wise convolution
Number of operations for M output channels reduces dramatically:
Left: H*W*(R*S*C)*M
Right: H*W*(R*S)*C + H*W*C*M = H*W*C*(R*S + M)

## Slide 20: Network scaling
Different scaling options
  Width scaling: more channels, i.e. more filters
  Depth scaling: more layers
  Resolution scaling: increase image size
Some methods do this in systematic ways
  EfficientNet: Rethinking model scaling for CNNs
  Searching for MobileNetV3
  Many NAS, Network Architecture Search, methods

## Slide 21: Evolution of separable convolution blocks
Diagonally hatched layers do not use non-linearities.
Thickness of each block indicates its relative number of channels.
Note: c and d are equivalent blocks when stacked.
AlexNet, VGG
MobileNetV1
MobileNetV2/3
MnasNet
EfficientNet
Notes: see MobileNetv2 paper for more explanation

## Slide 22: MobileNetV2: bottleneck with residual
Each MobileNetV2 block consists of
narrow C-channel input and output (low number of channels)
expansion by D (1x1xC) filters to much higher D-dimensional space: tunable dimension
depth wise convolution (followed by Relu6 activation)
projection by C (1x1xD) to lower C-dimensional space, i.e. reducing nr. of output channels
residual connection over the whole block
C
C
D
D

## Slide 23: MnasNet: MobileNetV2 + Squeeze-and-Excite
Squeeze-and-Excite attention layer:
squeeze: averaging each input channel to 1 value
excite: determine scale factor
  using C fully connected learnable convolutions
scale input channels

## Slide 24: MobileNetV3
adds to MobileNetV2
replaces ReLU by Swish
  actually an approximation:
  h-swish(x) = x*(ReLU6(x+3))/6
network scaling using NAS

## Slide 25: Different scaling methods, combined in EfficientNet

## Slide 26: EfficientNet: Flops vs ImageNet Accuracy
Red line shows EfficientNet
options for different scalings

## Slide 27: What did you learn
How to express reuse options in Halide for a 1-D convolution filter
4th Optimization: Several changes to Network Structure:
  decomposition
  depth wise convolution
  squeeze-and-excite
  scaling options: width, depth, resolution
  adding more residual connections
Later we’ll discuss automated & structured approaches for this:
  NAS: Network Architecture Search