## Slide 1: Embedded Computer Architecture 5SAI0 Micro Processor Architecture (Chapter 3 - part 1)
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2016-2017

## Slide 2: Overview Processor Microarchitecture
Instruction set architecture (ISA)
  we use the MIPS ISA as example
Statically scheduled pipelines
  discuss the MIPS 5-stage pipeline in detail
  Hazards = problems with the pipeline
  RISC vs CISC
  other architecture styles

## Slide 3: ISA in relation to other abstraction layers
Notes: The ISA is the interface between software and hardware
Design objectives
Functionality and flexibility for os and compilers
Implementation efficiency in available technology
Backward compatibility

## Slide 4: Instruction Set Architectures (ISA)
What’s an ISA?
  we use MIPS as main example
Instruction types and opcode
Instruction operands
Exceptions
RISC vs. CISC
  sidestep: Micro-coded implementations

## Slide 5: Instruction types: 3 classes
Arithmetic
  Integer arithmetic/logic instructions
    ADD, SUB, MULT
    ADDU, SUBU,MULTU
    OR, AND, NOR, NAND
  Floating point instructions
    FADD, FMUL, FDIV
Memory transfer instructions
  Loads and Stores
  TEST-and-SET, and SWAP
  May apply to various operand sizes: bytes, half-words, words, doubles, etc.
Control instructions
  Branches are conditional
    Condition may be condition bits (ZCVXN)
    Condition may test the value of a register (set by SLT instruction)
    Condition may be computed in the branch instruction itself
  Jumps are unconditional with absolute address or address in register
  JAL (jump and link) needed for procedures

## Slide 6: MIPS arithmetic
Most instructions have 3 operands
Operand order is fixed (destination first) Example: C code: A = B + C MIPS code: add $s0, $s1, $s2 ($s0, $s1 and $s2 are associated with variables by compiler, and each correspond to one of the 32 registers r0-r31)

## Slide 7: MIPS arithmetic
C code: A = B + C + D; E = F - A; MIPS code: add $t0, $s1, $s2 add $s0, $t0, $s3 sub $s4, $s5, $s0
Operands must be registers, only 32 registers provided
Design Principle: smaller is faster. Why?

## Slide 8: Registers vs. Memory
Arithmetic instruction operands must be registers, — only 32 registers provided
Compiler associates variables with registers
What about programs with lots of variables ?
CPU
Memory
IO
register file

## Slide 9: Register allocation
Compiler tries to keep as many variables in registers as possible
Some variables can not be allocated
  large arrays (too few registers)
  aliased variables (variables accessible through pointers in C)
  dynamic allocated variables
    heap
    stack
Compiler may run out of registers => spilling

## Slide 10: Stack vs Heap

## Slide 11: Heap

## Slide 12: Memory Organization
Viewed as a large, single-dimension array, with an address
A memory address is an index into the array
"Byte addressing" means that successive addresses are one byte apart
0
1
2
3
4
5
6
...
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 13: Memory Organization
Bytes are nice, but most data items use larger "words"
For MIPS, a word is 32 bits or 4 bytes.
232 bytes with byte addresses from 0 to 232-1
230 words with byte addresses 0, 4, 8, ... 232-4
...
0
4
8
12
32 bits of data
32 bits of data
32 bits of data
32 bits of data
Registers hold 32 bits of data

## Slide 14: Memory layout: Alignment
For a RISC: Instruction words are aligned
What are the least 2 significant bits of a word address?
this word is aligned; the others are not!
address
0
4
8
12
16
20
24
31
0
7
15
23

## Slide 15: Instructions: load and store
Example: C code: A[8] = h + A[8]; MIPS code: lw $t0, 32($s3) add $t0, $s2, $t0 sw $t0, 32($s3)
Store word operation has no destination (reg) operand
Remember arithmetic operands are registers, not memory!

## Slide 16: Let's translate some C-code
Can we figure out the code?
swap(int v[], int k);
{ int temp;
temp = v[k]
v[k] = v[k+1];
v[k+1] = temp;
}
swap:
muli $2 , $5, 4
add $2 , $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31
Explanation:
index k : $5
base address of v: $4
address of v[k] is $4 + 4.$5

## Slide 17: Machine Language: R-format
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t0, $s1, $s2
  Registers have numbers: $t0=9, $s1=17, $s2=18
Instruction Format:
Can you guess what the field names stand for?
6 bits
5 bits
5 bits
5 bits
6 bits
5 bits
000000 10001 10010 01001 00000 100000
op rs rt rd shamt funct

## Slide 18: Machine Language: I-format
Introduce a new type of instruction format
  I-type for data transfer instructions
  other format was R-type for register
Example: lw $t0, 32($s2) 35 18 9 32 op rs rt 16 bit number

## Slide 19: Control flow
Decision making instructions
  alter the control flow,
  i.e., change the "next" instruction to be executed
MIPS conditional branch instructions: BNE $t0, $t1, Label BEQ $t0, $t1, Label
Example: if (i==j) h = i + j; BNE $s0, $s1, Label ADD $s3, $s0, $s1 Label: ....

## Slide 20: Control flow
MIPS unconditional branch instructions: j label
Example: if (i!=j) BEQ $s4, $s5, Lab1 h=i+j; ADD $s3, $s4, $s5 else J Lab2 h=i-j; Lab1: SUB $s3, $s4, $s5 Lab2: ...
Can you build a simple for loop?

## Slide 21: So far:
Instruction Meaning
add $s1,$s2,$s3 $s1 = $s2 + $s3 sub $s1,$s2,$s3 $s1 = $s2 – $s3 lw $s1,100($s2) $s1 = Memory[$s2+100] sw $s1,100($s2) Memory[$s2+100] = $s1 bne $s4,$s5,L Next instr. is at Label if $s4 ° $s5 beq $s4,$s5,L Next instr. is at Label if $s4 = $s5 j Label Next instr. is at Label
Formats:
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 22: Control Flow
We have: beq, bne, what about Branch-if-less-than?
New instruction: meaning: if $s1 < $s2 then $t0 = 1
slt $t0, $s1, $s2 else $t0 = 0
Can use this instruction to build "blt $s1, $s2, Label"
  note: this is a pseudo instruction, i.e. the assembler understands it, but translates it to other instructions
  you can now build all general control structures
  Note that the assembler needs a register to do this,
  use conventions for registers

## Slide 23: MIPS compiler/assembler conventions

## Slide 24: Constants
Small constants are used quite frequently (50% of operands) e.g., A = A + 5; B = B + 1; C = C - 18;
Solutions? Why not?
  put 'typical constants' in memory and load them
  create hard-wired registers (like $zero) for constants like 0, 1, 2, …
  or …….
MIPS Instructions: addi $29, $29, 4 slti $8, $18, 10 andi $29, $29, 6 ori $29, $29, 4

## Slide 25: How about larger constants?
We'd like to be able to load a 32 bit constant into a register
Must use two instructions; new "load upper immediate" instruction lui $t0, 1010101010101010
1010101010101010
0000000000000000
0000000000000000
1010101010101010
1010101010101010
1010101010101010
ori
1010101010101010
0000000000000000
filled with zeros
Then must get the lower order bits right, i.e., ori $t0, $t0, 1010101010101010

## Slide 26: Assembly Language vs. Machine Language
Assembly provides convenient symbolic representation
  much easier than writing down numbers
  e.g., destination first
however: Machine language is the underlying reality
  e.g., destination is no longer first
Assembly can provide 'pseudoinstructions'
  e.g., “move $t0, $t1” exists only in Assembly
  would be implemented using “add $t0,$t1,$zero”
  Another pseudo instr: blt $t1, $t2, label
When considering performance you should count real instructions

## Slide 27: Addresses in Branches and Jumps
Instructions:
  bne $t4,$t5,Label Next instruction is at Label if $t4  $t5
  beq $t4,$t5,Label Next instruction is at Label if $t4 = $t5
  j Label Next instruction is at Label
Formats:
Addresses are not 32 bits — How do we handle this with load and store instructions?
op rs rt 16 bit address
op 26 bit address
I
J

## Slide 28: What's the next address?
Instructions:
  bne $t4,$t5,Label Next instruction is at Label if $t4  $t5
  beq $t4,$t5,Label Next instruction is at Label if $t4 = $t5
Formats:
Most branches are local (principle of locality):
  use Instruction Address Register (PC = program counter), and use relative addressing: PC_next = PC + 4 + (16-bit address)
Jump instructions just use high order bits of PC
  address boundaries of 256 MB
op rs rt 16 bit address
I

## Slide 29: To summarize:

## Slide 30: MIPS (3+2) addressing modes overview

## Slide 31: Pipelining
Why: Ideal speedup = number of stages
Do we achieve this? NO! HAZARDS
Let’s look at Pipeline implementation (= processor organization)

## Slide 32: Pipelining
Improve performance by increasing instruction throughput
I
n
s
t
r
u
c
t
i
o
n
f
e
t
c
h
R
e
g
A
L
U
D
a
t
a
a
c
c
e
s
s
R
e
g
8
n
s
I
n
s
t
r
u
c
t
i
o
n
f
e
t
c
h
R
e
g
A
L
U
D
a
t
a
a
c
c
e
s
s
R
e
g
8
n
s
I
n
s
t
r
u
c
t
i
o
n
f
e
t
c
h
8
n
s
T
i
m
e
l
w
$
1
,
1
0
0
(
$
0
)
l
w
$
2
,
2
0
0
(
$
0
)
l
w
$
3
,
3
0
0
(
$
0
)
2
4
6
8
1
0
1
2
1
4
1
6
1
8
2
4
6
8
1
0
1
2
1
4
.
.
.
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
I
n
s
t
r
u
c
t
i
o
n
f
e
t
c
h
R
e
g
A
L
U
D
a
t
a
a
c
c
e
s
s
R
e
g
T
i
m
e
l
w
$
1
,
1
0
0
(
$
0
)
l
w
$
2
,
2
0
0
(
$
0
)
l
w
$
3
,
3
0
0
(
$
0
)
2
n
s
I
n
s
t
r
u
c
t
i
o
n
f
e
t
c
h
R
e
g
A
L
U
D
a
t
a
a
c
c
e
s
s
R
e
g
2
n
s
I
n
s
t
r
u
c
t
i
o
n
f
e
t
c
h
R
e
g
A
L
U
D
a
t
a
a
c
c
e
s
s
R
e
g
2
n
s
2
n
s
2
n
s
2
n
s
2
n
s
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)

## Slide 33: Pipelining
What makes it easy
  all instructions are the same length
  just a few instruction formats
  memory operands appear only in loads and stores
What makes it hard?
  structural hazards: suppose we had only one memory
  control hazards: need to worry about branch instructions
  data hazards: an instruction depends on a previous instruction
We’ll build a simple pipeline and look at these issues
We’ll talk about modern processors and what really makes it hard:
  exception handling
  trying to improve performance with out-of-order execution, etc.

## Slide 34: Basic idea: start from single cycle impl.
What do we need to add to actually split the datapath into stages?
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
A
d
d
r
e
s
s
4
3
2
0
A
d
d
A
d
d
r
e
s
u
l
t
S
h
i
f
t
l
e
f
t
2
I
n
s
t
r
u
c
t
i
o
n
M
u
x
0
1
A
d
d
P
C
0
W
r
i
t
e
d
a
t
a
M
u
x
1
R
e
g
i
s
t
e
r
s
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
1
6
S
i
g
n
e
x
t
e
n
d
W
r
i
t
e
r
e
g
i
s
t
e
r
W
r
i
t
e
d
a
t
a
R
e
a
d
d
a
t
a
A
d
d
r
e
s
s
D
a
t
a
m
e
m
o
r
y
1
A
L
U
r
e
s
u
l
t
M
u
x
A
L
U
Z
e
r
o
I
F
:
I
n
s
t
r
u
c
t
i
o
n
f
e
t
c
h
I
D
:
I
n
s
t
r
u
c
t
i
o
n
d
e
c
o
d
e
/
r
e
g
i
s
t
e
r
f
i
l
e
r
e
a
d
E
X
:
E
x
e
c
u
t
e
/
a
d
d
r
e
s
s
c
a
l
c
u
l
a
t
i
o
n
M
E
M
:
M
e
m
o
r
y
a
c
c
e
s
s
W
B
:
W
r
i
t
e
b
a
c
k

## Slide 35: Pipelined Datapath
Can you find a problem even if there are no dependencies? What instructions can we execute to manifest the problem?
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
A
d
d
r
e
s
s
4
3
2
0
A
d
d
A
d
d
r
e
s
u
l
t
S
h
i
f
t
l
e
f
t
2
I
n
s
t
r
u
c
t
i
o
n
I
F
/
I
D
E
X
/
M
E
M
M
E
M
/
W
B
M
u
x
0
1
A
d
d
P
C
0
W
r
i
t
e
d
a
t
a
M
u
x
1
R
e
g
i
s
t
e
r
s
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
1
6
S
i
g
n
e
x
t
e
n
d
W
r
i
t
e
r
e
g
i
s
t
e
r
W
r
i
t
e
d
a
t
a
R
e
a
d
d
a
t
a
1
A
L
U
r
e
s
u
l
t
M
u
x
A
L
U
Z
e
r
o
I
D
/
E
X
D
a
t
a
m
e
m
o
r
y
A
d
d
r
e
s
s

## Slide 36: Corrected Datapath
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
A
d
d
r
e
s
s
4
3
2
0
A
d
d
A
d
d
r
e
s
u
l
t
S
h
i
f
t
l
e
f
t
2
I
n
s
t
r
u
c
t
i
o
n
I
F
/
I
D
E
X
/
M
E
M
M
E
M
/
W
B
M
u
x
0
1
A
d
d
P
C
0
A
d
d
r
e
s
s
W
r
i
t
e
d
a
t
a
M
u
x
1
R
e
g
i
s
t
e
r
s
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
1
6
S
i
g
n
e
x
t
e
n
d
W
r
i
t
e
r
e
g
i
s
t
e
r
W
r
i
t
e
d
a
t
a
R
e
a
d
d
a
t
a
D
a
t
a
m
e
m
o
r
y
1
A
L
U
r
e
s
u
l
t
M
u
x
A
L
U
Z
e
r
o
I
D
/
E
X

## Slide 37: Graphically Representing Pipelines
Can help with answering questions like:
  how many cycles does it take to execute this code?
  what is the ALU doing during cycle 4?
  use this representation to help understand datapaths
I
M
R
e
g
D
M
R
e
g
I
M
R
e
g
D
M
R
e
g
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
l
w
$
1
0
,
2
0
(
$
1
)
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
s
u
b
$
1
1
,
$
2
,
$
3
A
L
U
A
L
U

## Slide 38: Pipeline Control
P
C
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
A
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
I
n
s
t
r
u
c
t
i
o
n
[
2
0
–
1
6
]
M
e
m
t
o
R
e
g
A
L
U
O
p
B
r
a
n
c
h
R
e
g
D
s
t
A
L
U
S
r
c
4
1
6
3
2
I
n
s
t
r
u
c
t
i
o
n
[
1
5
–
0
]
0
0
R
e
g
i
s
t
e
r
s
W
r
i
t
e
r
e
g
i
s
t
e
r
W
r
i
t
e
d
a
t
a
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
S
i
g
n
e
x
t
e
n
d
M
u
x
1
W
r
i
t
e
d
a
t
a
R
e
a
d
d
a
t
a
M
u
x
1
A
L
U
c
o
n
t
r
o
l
R
e
g
W
r
i
t
e
M
e
m
R
e
a
d
I
n
s
t
r
u
c
t
i
o
n
[
1
5
–
1
1
]
6
I
F
/
I
D
I
D
/
E
X
E
X
/
M
E
M
M
E
M
/
W
B
M
e
m
W
r
i
t
e
A
d
d
r
e
s
s
D
a
t
a
m
e
m
o
r
y
P
C
S
r
c
Z
e
r
o
A
d
d
A
d
d
r
e
s
u
l
t
S
h
i
f
t
l
e
f
t
2
A
L
U
r
e
s
u
l
t
A
L
U
Z
e
r
o
A
d
d
0
1
M
u
x
0
1
M
u
x

## Slide 39: Pipeline control
We have 5 stages. What needs to be controlled in each stage?
  Instruction Fetch and PC Increment
  Instruction Decode / Register Fetch
  Execution
  Memory Stage
  Write Back
How would control be handled in an automobile plant?
  a fancy control center telling everyone what to do?
  should we use a finite state machine (FSM)?

## Slide 40: Datapath with Control
P
C
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
I
n
s
t
r
u
c
t
i
o
n
A
d
d
I
n
s
t
r
u
c
t
i
o
n
[
2
0
–
1
6
]
M
e
m
t
o
R
e
g
A
L
U
O
p
B
r
a
n
c
h
R
e
g
D
s
t
A
L
U
S
r
c
4
1
6
3
2
I
n
s
t
r
u
c
t
i
o
n
[
1
5
–
0
]
0
0
M
u
x
0
1
A
d
d
A
d
d
r
e
s
u
l
t
R
e
g
i
s
t
e
r
s
W
r
i
t
e
r
e
g
i
s
t
e
r
W
r
i
t
e
d
a
t
a
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
S
i
g
n
e
x
t
e
n
d
M
u
x
1
A
L
U
r
e
s
u
l
t
Z
e
r
o
W
r
i
t
e
d
a
t
a
R
e
a
d
d
a
t
a
M
u
x
1
A
L
U
c
o
n
t
r
o
l
S
h
i
f
t
l
e
f
t
2
R
e
g
W
r
i
t
e
M
e
m
R
e
a
d
C
o
n
t
r
o
l
A
L
U
I
n
s
t
r
u
c
t
i
o
n
[
1
5
–
1
1
]
6
E
X
M
W
B
M
W
B
W
B
I
F
/
I
D
P
C
S
r
c
I
D
/
E
X
E
X
/
M
E
M
M
E
M
/
W
B
M
u
x
0
1
M
e
m
W
r
i
t
e
A
d
d
r
e
s
s
D
a
t
a
m
e
m
o
r
y
A
d
d
r
e
s
s

## Slide 41: Pipeline Control
Pass control signals along
just like the data:

## Slide 42
Hazards
New Hazard Symbols

## Slide 43: Hazards: problems due to pipelining
Three Hazard types:
Structural
  same resource is needed multiple times in the same cycle
Data
  data dependencies limit pipelining
Control
  next executed instruction may not be the next specified instruction

## Slide 44: Structural hazards
Examples:
Two accesses to a single ported memory
Two operations need the same function unit at the same time
Two operations need the same function unit in successive cycles, but the unit is not pipelined
Solutions:
stalling
add more hardware

## Slide 45: Structural hazards on MIPS
Q: Do we have structural hazards on our simple MIPS pipeline?
- is there any resource clash?
time
Instruction stream
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB

## Slide 46: Data hazards; due to data dependences
Data dependences:
  RaW (read-after-write)
  WaW (write-after-write)
  WaR (write-after-read)
  between register operands and/or between memory operands
Hardware solution:
  Forwarding / Bypassing
  Detection logic
  Stalling
Software solution: Scheduling

## Slide 47: 3 Data dependences types: RaW, WaR, WaW
add r1, r2, 5 ; r1 := r2+5
sub r4, r1, r3 ; RaW of r1
add r1, r2, 5
sub r2, r4, 1 ; WaR of r2
add r1, r2, 5
sub r1, r1, 1 ; WaW of r1
st r1, 5(r2) ; M[r2+5] := r1
ld r5, 0(r4) ; RaW if 5+r2 = 0+r4
WaW and WaR do not occur in simple pipelines, but they limit
scheduling freedom!
Problems for your compiler and your Laptop processor!
 use register renaming to solve this!

## Slide 48: RaW on MIPS pipeline
I
M
R
e
g
I
M
R
e
g
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
s
u
b
$
2
,
$
1
,
$
3
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
a
n
d
$
1
2
,
$
2
,
$
5
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
I
M
D
M
R
e
g
C
C
7
C
C
8
C
C
9
1
0
1
0
1
0
1
0
1
0
/
–
2
0
–
2
0
–
2
0
–
2
0
–
2
0
o
r
$
1
3
,
$
6
,
$
2
a
d
d
$
1
4
,
$
2
,
$
2
s
w
$
1
5
,
1
0
0
(
$
2
)
V
a
l
u
e
o
f
r
e
g
i
s
t
e
r
$
2
:
D
M
R
e
g
R
e
g
R
e
g
R
e
g
D
M

## Slide 49: Use forwarding hardware
- Do not wait till the result is in the register file
ALU forwarding circuitry principle:
buf
buf
ALU
buf
from register file
from register file
to register file
Note: there are two options
buf - ALU – bypass – mux - buf
buf - bypass – mux – ALU - buf

## Slide 50: Forwarding example
What if this
$2 was $13?
I
M
R
e
g
I
M
R
e
g
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
s
u
b
$
2
,
$
1
,
$
3
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
a
n
d
$
1
2
,
$
2
,
$
5
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
I
M
D
M
R
e
g
C
C
7
C
C
8
C
C
9
1
0
1
0
1
0
1
0
1
0
/
–
2
0
–
2
0
–
2
0
–
2
0
–
2
0
o
r
$
1
3
,
$
6
,
$
2
a
d
d
$
1
4
,
$
2
,
$
2
s
w
$
1
5
,
1
0
0
(
$
2
)
V
a
l
u
e
o
f
r
e
g
i
s
t
e
r
$
2
:
D
M
R
e
g
R
e
g
R
e
g
R
e
g
X
X
X
–
2
0
X
X
X
X
X
V
a
l
u
e
o
f
E
X
/
M
E
M
:
X
X
X
X
–
2
0
X
X
X
X
V
a
l
u
e
o
f
M
E
M
/
W
B
:
D
M

## Slide 51: Forwarding
P
C
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
R
e
g
i
s
t
e
r
s
M
u
x
M
u
x
C
o
n
t
r
o
l
A
L
U
E
X
M
W
B
M
W
B
W
B
I
D
/
E
X
E
X
/
M
E
M
M
E
M
/
W
B
D
a
t
a
m
e
m
o
r
y
M
u
x
F
o
r
w
a
r
d
i
n
g
u
n
i
t
I
F
/
I
D
I
n
s
t
r
u
c
t
i
o
n
M
u
x
R
d
E
X
/
M
E
M
.
R
e
g
i
s
t
e
r
R
d
M
E
M
/
W
B
.
R
e
g
i
s
t
e
r
R
d
R
t
R
t
R
s
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
d
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
t
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
t
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
s
ForwardA
ForwardB

## Slide 52: Forwarding check
Check for matching register-ids:
  For each source-id of operation in the EX-stage check if there is a matching pending dest-id
if (EX/MEM.RegWrite) 
(EX/MEM.RegisterRd  0) 
(EX/MEM.RegisterRd = ID/EX.RegisterRs) then ForwardA = 10
Example:
Q. How many comparators do we need?

## Slide 53: Can't always forward: Load !!
Load word can still cause a hazard:
  an instruction tries to read register r following a load to the same r
Need a hazard detection unit to “stall” the load instruction
R
e
g
I
M
R
e
g
R
e
g
I
M
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
l
w
$
2
,
2
0
(
$
1
)
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
a
n
d
$
4
,
$
2
,
$
5
I
M
R
e
g
D
M
R
e
g
I
M
D
M
R
e
g
I
M
D
M
R
e
g
C
C
7
C
C
8
C
C
9
o
r
$
8
,
$
2
,
$
6
a
d
d
$
9
,
$
4
,
$
2
s
l
t
$
1
,
$
6
,
$
7
D
M
R
e
g
R
e
g
R
e
g
D
M

## Slide 54: Stalling
We can stall the pipeline by keeping an instruction in the same stage
l
w
$
2
,
2
0
(
$
1
)
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
a
n
d
$
4
,
$
2
,
$
5
o
r
$
8
,
$
2
,
$
6
a
d
d
$
9
,
$
4
,
$
2
s
l
t
$
1
,
$
6
,
$
7
R
e
g
I
M
R
e
g
R
e
g
I
M
D
M
C
C
1
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
I
M
R
e
g
D
M
R
e
g
I
M
I
M
D
M
R
e
g
I
M
D
M
R
e
g
C
C
7
C
C
8
C
C
9
C
C
1
0
D
M
R
e
g
R
e
g
R
e
g
R
e
g
b
u
b
b
l
e
In CC4 the ALU is not used,
Reg, and IM are redone

## Slide 55: Hazard Detection Unit
P
C
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
R
e
g
i
s
t
e
r
s
M
u
x
M
u
x
M
u
x
C
o
n
t
r
o
l
A
L
U
E
X
M
W
B
M
W
B
W
B
I
D
/
E
X
E
X
/
M
E
M
M
E
M
/
W
B
D
a
t
a
m
e
m
o
r
y
M
u
x
H
a
z
a
r
d
d
e
t
e
c
t
i
o
n
u
n
i
t
F
o
r
w
a
r
d
i
n
g
u
n
i
t
0
M
u
x
I
F
/
I
D
I
n
s
t
r
u
c
t
i
o
n
I
D
/
E
X
.
M
e
m
R
e
a
d
I
F
/
I
D
W
r
i
t
e
P
C
W
r
i
t
e
I
D
/
E
X
.
R
e
g
i
s
t
e
r
R
t
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
d
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
t
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
t
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
s
R
t
R
s
R
d
R
t
E
X
/
M
E
M
.
R
e
g
i
s
t
e
r
R
d
M
E
M
/
W
B
.
R
e
g
i
s
t
e
r
R
d

## Slide 56: Software only solution?
Have compiler guarantee that no hazards occur
Example: where do we insert the “NOPs” ? sub $2, $1, $3 and $12, $2, $5 or $13, $6, $2 add $14, $2, $2 sw $13, 100($2)
Problem: this really slows us down!
sub $2, $1, $3
nop
nop
nop and $12, $2, $5 or $13, $6, $2 add $14, $2, $2
nop
nop sw $13, 100($2)

## Slide 57: Scheduling data hazards: example 1
Try and avoid RaW stalls (in this case load interlocks)!
E.g., reorder these instructions:
lw $t0, 0($t1)
lw $t2, 4($t1)
sw $t2, 0($t1)
sw $t0, 4($t1)
?
lw $t0, 0($t1)
lw $t2, 4($t1)
sw $t0, 4($t1)
sw $t2, 0($t1)

## Slide 58: Scheduling data hazards example 2
Avoiding RaW stalls:
Reordering instructions for following program
(by you or the compiler)
Code:
a = b + c
d = e - f
Unscheduled code:
Lw R1,b
Lw R2,c
Add R3,R1,R2 interlock
Sw a,R3
Lw R1,e
Lw R2,f
Sub R4,R1,R2 interlock
Sw d,R4
Scheduled code:
Lw R1,b
Lw R2,c
Lw R5,e extra reg. needed!
Add R3,R1,R2
Lw R2,f
Sw a,R3
Sub R4,R5,R2
Sw d,R4

## Slide 59: Control hazards
Control operations may change the sequential flow of instructions
  branch (conditional)
  jump (unconditional)
  call (unconditional jump and link)
  return (unconditional)
  exception/interrupt and RTI / return from interrupt

## Slide 60: Control hazard: Branch
Branch requires 3 actions:
Compute new address
Determine condition
Perform the actual branch (if taken): if Cond=True : PC := new address

## Slide 61: Branch example
R
e
g
R
e
g
C
C
1
T
i
m
e
(
i
n
c
l
o
c
k
c
y
c
l
e
s
)
4
0
b
e
q
$
1
,
$
3
,
7
P
r
o
g
r
a
m
e
x
e
c
u
t
i
o
n
o
r
d
e
r
(
i
n
i
n
s
t
r
u
c
t
i
o
n
s
)
I
M
R
e
g
I
M
D
M
I
M
D
M
I
M
D
M
D
M
D
M
R
e
g
R
e
g
R
e
g
R
e
g
R
e
g
R
e
g
I
M
4
4
a
n
d
$
1
2
,
$
2
,
$
5
4
8
o
r
$
1
3
,
$
6
,
$
2
5
2
a
d
d
$
1
4
,
$
2
,
$
2
7
2
l
w
$
4
,
5
0
(
$
7
)
C
C
2
C
C
3
C
C
4
C
C
5
C
C
6
C
C
7
C
C
8
C
C
9
R
e
g

## Slide 62: Branching
Squash pipeline:
When we decide to branch, other instructions are in the pipeline!
We are predicting “branch not taken”
  need to add hardware for flushing instructions if we are wrong

## Slide 63: Branch with predict not taken
Branch L
Predict not taken
L:
Clock cycles
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB

## Slide 64: Branch speedup
Earlier address computation
Earlier condition calculation
Put both in the ID pipeline stage
  adder
  comparator
Branch L
Predict not taken
L:
Clock cycles
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB

## Slide 65: Improved branching / flushing IF/ID
P
C
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
4
R
e
g
i
s
t
e
r
s
M
u
x
M
u
x
M
u
x
A
L
U
E
X
M
W
B
M
W
B
W
B
I
D
/
E
X
0
E
X
/
M
E
M
M
E
M
/
W
B
D
a
t
a
m
e
m
o
r
y
M
u
x
H
a
z
a
r
d
d
e
t
e
c
t
i
o
n
u
n
i
t
F
o
r
w
a
r
d
i
n
g
u
n
i
t
I
F
.
F
l
u
s
h
I
F
/
I
D
S
i
g
n
e
x
t
e
n
d
C
o
n
t
r
o
l
M
u
x
=
S
h
i
f
t
l
e
f
t
2
M
u
x

## Slide 66: Scheduling control hazards
Texecution = Ninstructions x CPI x Tcycle,
where:
CPI = CPIideal + fbranch x Pbranch
Pbranch = Ndelayslots x miss_rate
Modern processors tend to have large branch penalty, Pbranch, due to:
  many pipeline stages
  multi-issue
  so the pipeline contains many operations !
Note: penalties have larger effect when CPIideal is low

## Slide 67: Scheduling control hazards
What can we do about control hazards and CPI penalty?
Make penalty Pbranch low:
  Early computation of new PC
  Early determination of condition
  Visible branch delay slots filled by compiler (MIPS)
Branch prediction
Reduce control dependencies (control height reduction) [Schlansker and Kathail, Micro’95]
Remove branches: if-conversion
  Conditional instructions: CMOVE, cond skip next
  Guarding all instructions: e.g. in the TriMedia

## Slide 68: Branch delay slot
Add a branch delay slot:
  the next instruction after a branch is always executed
  rely on compiler to “fill” the slot with something useful
Is this a good idea?
  let's look how it works

## Slide 69: Branch delay slot scheduling
op 1
beq r1,r2, L
.............
op 2
L: op 3
.............
.............
'fall-through'
branch target
Q. What to put in the delay slot?

## Slide 71: Exceptions, traps and interrupts
Exceptions are rare events triggered by the hardware and forcing the processor to execute an exception handler
  Includes traps and interrupts
Examples:
  I/o device interrupts
  Operating system calls
  Instruction tracing and breakpoints
  Integer or floating-point arithmetic exceptions (e.g. overflow)
  Page faults
  Misaligned memory accesses
  Memory protection violations
  Undefined operation
  Hardware failure/alarms
  Power failures

## Slide 72: Exception handling
User program
Exception handling
RTI
Disable exceptions
Enter kernel
mode
Enable exceptions
Return to user
mode
Save process state
Enable exceptions
Disable exceptions
Restore process state
Optional, if handler
is re-entrable
Optional
Note, typically user program is put in 'ready queue'
instead of return to it directly
Exception raised
instructions
Notes: Note, practice is a little different
- after finishing the exception, the user program enters the OS ready state, and will be scheduled later for running.

## Slide 73: Exceptions
Pipeline benefits come from overlapped instruction executions
  Things go wrong when the flow of instructions is suddenly interrupted (exceptions)
Many exceptions must be precise, i.e.:
  All instructions preceding the faulting instruction must complete
  The faulting instruction and all following instructions must be squashed (flushed)
  The handler must start its execution
It is not practical to take an exception in the cycle when it happens
  Multiple exceptions in the same cycle
  It is complex to take exceptions in various pipeline stages
  The major reason is that exceptions must be taken in process order and not in temporal order
Instead, flag the exception and record its cause when it happens, keep it “silent” and wait until the instruction reaches the WB stage to take it.
1
2
3
4
except.
except.

## Slide 74: Possible problems for precise exceptions in CISC machines
Exceptions are handled easily in the WB stage because our ISA is RISC
  machine states are updated at the end of the pipeline
Precise exceptions are much more difficult in CISC machines because of:
  Early (in the pipeline) register changes due to complex addressing modes
    Auto-increment and auto-decrement addressing modes
  Condition codes
    Problem if they can be set in multiple stages
    If set early they must be restored on an exception
  Multi-cycle instructions
    Where to stop?
    How to restart?
  Use of registers as working storage in the microcode of complex instructions

## Slide 75: Out-of-order execution completion
Integer unit: handles integer instructions, branches, and loads/stores
Floating-point instructions take 5 clocks and are pipelined
Two separate register files, for integer and fp (not shown)
Forwarding paths into ex and FP1
  FP values forwarded from FP/ME and ME/WB to ID/EX because of stores
Instructions wait in ID until they can proceed data hazard free
  Static scheduling of instructions
Still in-order execution, but out-of-order completion
Notes: pipeline executing integer (EX) and floating-point (FP) instructions with two specialized pipelines, one for Loads, Stores, Integer and Branch instructions, and the other for floating-point arithmetic operations. FP takes 5 cycles in a pipelined fashion. Hence, FP instructions may complete AFTER a later integer instruction.
Forwarding is complicated because of floating-point Stores, which need the values of both an integer (address) register and a floating-point (data) register in order to proceed through the decode stage. To forward the data value to floating-point Stores, a forwarding path has been added from pipeline register FP/ME to the input of the EX stage.

## Slide 76: LATENCY vs REPEAT INTERVAL
Latency of operation:
  Minimum number of cycles between an instruction producing a result and the instruction consuming it (= execution time, in cycles, minus 1)
    Note: many books just take Latency = Number of Execution cycles
  Dependent instruction must stall in ID until its operand is forwarded
Repeat/initiation interval
  Number of cycles that must elapse between consecutive issues of instructions to the same unit
  Assume for example that the fp unit is not pipelined.
    Then FP instructions could only be issued every 5 clocks
For the new FP capable machine
FUNCTIONAL UNITS | LATENCY | INITIATION INTERVAL
INTEGER ALU | 0 | 1
LOAD | 1 | 1
FP Operation | 4 | 1 (5 IF NOT PIPELINED)

## Slide 77: New structural hazards
Scan columns for common resource usage
  At cycle C8: i1 and i5 are both in the ME stage
    Does not matter since i1 does not access memory
  At cycle C9: i1 and i5 are both in the WB stage and both store in FP registers
    Structural hazard on FP register file write port
    Could add one write port to register file : that’s expensive
    Solution: make sure that only one FP operand accesses the FP register file in each cycle
    Structural hazard on register file write port is solved in ID by stalling i5 in ID stage
Also: structural hazards on execution units
In general: 2 techniques to remove structural hazards:
  Add hardware resources
  Deal with it by stalling instructions to serialize conflicts
 | CLOCK ==> | C1 | C2 | C3 | C4 | C5 | C6 | C7 | C8 | C9 | C10
I1 | ADD.S F1,F2,F1 | IF | ID | FP1 | FP2 | FP3 | FP4 | FP5 | ME | WB | 
I2 | ADD.S F4,F2,F3 |  | IF | ID | FP1 | FP2 | FP3 | FP4 | FP5 | ME | WB
I3 | L.S F10 |  |  | IF | ID | EX | ME | WB |  |  | 
I4 | L.S F12 |  |  |  | IF | ID | EX | ME | WB |  | 
I5 | L.S F14 |  |  |  |  | IF | ID | EX | ME | WB | 

## Slide 78: New data hazards
WAW hazards on FP registers: instructions can reach WB out of order
      ADD.D F2,F4,F6
      L.D F2, 0(R2) // WaW on F2
  The L.D must stall in ID
Still no WAR hazards on registers since reads happen early
More RAW hazard stalls due to longer latency instructions, e.g.:
No data hazards on memory
  Loads and Stores follow the same pipeline path
  Are processed in thread order in the MEM stage
Control hazards are unchanged
  Take branch in EX and flush IF and ID
 | CLOCK ==> | C1 | C2 | C3 | C4 | C5 | C6 | C7 | C8 | C9 | C10 | C11
I1 | L.D F4, 0(R2) | IF | ID | EX | ME | WB |  |  |  |  |  | 
I2 | MULT.D F0,F4,F6 |  | IF | ID | ID | FP1 | FP2 | FP3 | FP4 | FP5 | ME | WB
I3 | S.D F0, 0(R2) |  |  | IF | IF | ID | ID | ID | ID | ID | EX | ME

## Slide 79: Structural and data hazards
Checked in the ID-stage
Structural hazards:
  Wait until the functional unit is not busy (initiation interval)
  Make sure the register write port will be available
RAW hazards on register
  Forwarding
  Stalling: HDU (Hazard Detection Unit) must check that none of the source operands of the current instruction is the destination of one of the instructions in the pipelines (check write register field in pipeline registers)
WAW hazards
  Handle like stalls for RAW hazards in HDU (hazard detection unit)
  Check that the destination register of the current instruction-id is not the destination of any of the instructions in the pipelines
  WAW hazards are very rare because it does not make much sense to update a register twice without using the first value
    ADD.D F2,F4,F6
    L.D F2,0(R2)
  If an instruction reading F2 is inserted between the two instruction then the waw hazard is solved by the hardware solving raw hazards

## Slide 80: Precise exceptions
Consider the following code;
    ADD.S F1, F2, F1
    ADD R2, R1, R3
No dependency! Totally independent
However, there are problems w.r.t. precise exception
  What happens if ADD.S causes an exception late in the FP pipeline?
  The ADD has already been executed
  Add stores its result in C6
  In C7 ADD.S causes an exception
  R2 has already been modified
 | C1 | C2 | C3 | C4 | C5 | C6 | C7 | C8 | 9 | 10 | 11
ADD.S F1,F2,F1 | IF | ID | FP1 | FP2 | FP3 | FP4 | FP5 | ME | WB |  | 
ADD R2,R1,R3 |  | IF | ID | EX | ME | WB |  |  |  |  | 

## Slide 81: Coping with precise exceptions
Forget precision on exceptions
  Not really viable today in machines supporting virtual memory and IEEE floating point standard
  Give state to software and let the software figure it out
    Only possible for simple pipelines
Deal with exceptions as if they were hazards
  Do not issue an instruction in ID until it is sure that all prior instructions are exception free
  Detect exceptions as early as possible in the execution
  May stiffle pipelining
Force in-order completion :

## Slide 82: Superpipelined CPU
Some stages in the 5-stage integer pipeline are further pipelined
  To increase the clock rate
  Here if, EX, and me are now 2 pipeline stages
  Clock is 2x as fast (hopefully)
  Not “free”
    Branch penalty when taken is now 3 clocks
    Latencies in clock are higher
Assuming unchanged 5-stages for FP
FUNCTIONAL UNITS | LATENCY | INITIATION INTERVAL
INTEGER ALU | 1 | 1
LOAD | 3 | 1
FP OP | 4 | 1(5 IF NOT PIPELINED)

## Slide 83: Superscalar CPU
Fetch, decode and execute e.g. up to 2 instructions per clock
  Same clock rate as basic pipeline
  Easy because of the 2 (INT and FP) register files
  Issue a pair of instructions
    Pair must be integer/branch/memory and FP pair (compiler)
    Instructions in pair must be independent and have no hazard with prior instructions
  Same latencies as basic pipeline; branches execute in EX
  Branches and latencies waste more instruction slots
  Exceptions are more complex
IPC (instructions per clock) instead of CPI (IPC = 1/CPI)

## Slide 84: Static branch prediction
Hardwired (fixed) branch prediction
  Always predict untaken and execute in EX
  Conditional branches at the bottom of a loop are mostly mispredicted
  No compiler assist is possible
  Could predict taken, but not very useful here (why?)
  Could be more flexible
  Based on opcode and/or sign/size of branch opcode
  Decisions are made at micro-architecture design time (benchmarking)
Compile-time branch prediction
  Each branch instruction has a “hint” bit set by the compiler
  Compiler profiles the code and sets the hint bit in branch instructions
  Taken/not taken prediction is much more flexible

## Slide 85: Static instruction scheduling
To maximize performance compiler moves code up or down
  Local (basic block)
  Global (across basic blocks)
    Cyclic (loops)
    Non-cyclic (traces)
Example For (i=0;i<100;i++)
A[i]:= a[i] + b[i];
An unoptimized code:
Loop: | L.S F0,#4(R1) | (1)
 | L.S F1,#4(R2) | (1)
 | ADD.S F2,F1,F0 | (2)
 | S.S F2,#4(R1) | (5)
 | ADDI R1,R1,#8 | (1)
 | ADDI R2,R2,#8 | (1)
 | SUBI R3,R3,#2 | (1)
 | BNEZ R3,Loop | (3)
TOTAL EXECUTION TIME =
15 Clock cycles;
CPI = 15/8 = 1.88
cycles
Notes: S.S takes 5 cycles to execute since it is immediately storing Ai+_Bi in Ai location. However, unfortunately, it has to wait for the ADD.S to finish before it can go. BNEZ takes 3 cycles because branch is predicted non-taken but it is taken.

## Slide 86: Local code scheduling
Compiler moves instructions inside the loop body:
  Move SUBI up
  Move S.S down
  Must change the displacement of the store (war hazard on R1)
Execution time = 12 clock clycles, a speed up of 15/12 = 1.25
The penalty of the branch cannot be improved
  Change the code and use a branch at the top of the loop body
  Delayed branches
Easy but limited because basic blocks are small
Use global scheduling: loop unrolling and software pipelining
Loop: | L.S F0,#4(R1) | (1)
 | L.S F1,#4(R2) | (1)
 | SUBI R3,R3,#2 | (1)
 | ADD.S F2,F1,F0 | (1)
 | ADDI R1,R1,#8 | (1)
 | ADDI R2,R2,#8 | (1)
 | S.S F2,#4(R1) | (3)
 | BNEZ R3,Loop | (3)
Notes: Rearrange the code to remove delays. Move SUBI which is independent of L.s F1. Thus ADD.S can eliminate penalty. Similarly S.S is moved after ADDI instructions to reduce its wait. But note that we need to change displacement because R1 is already changed (added 4 so decrement 4).

## Slide 87: Loop unrolling
Unroll twice | Rename FP register | Schedule | Times(basic/super)
L.S F0,0(R1) | L.S F0,0(R1) | L.S F0,0(R1) | (1) (1)
L.S F1,0(R2) | L.S F1,0(R2) | L.S F1,0(R2) | (1) (1)
ADD.S F2,F1,F0 | ADD.S F2,F1,F0 | L.S F3,#4(R1) | (1) (1)
S.S F2,0(R1) | S.S F2,0(R1) | L.S F4,#4(R2) | (1) (1)
L.S F0,#4(R1) | L.S F3,#4(R1) | ADD.S F2,F1,F0 | (1) (2)
L.S F1,#4(R2) | L.S F4,#4(R2) | ADD.S F5,F3,F4 | (1) (2)
ADD.S F2,F1,F0 | ADD.S F5,F3,F4 | SUBI R3,R3,#2 | (1) (1)
S.S F2,#4(R1) | S.S F5,#4(R1) | ADDI R1,R1,#8 | (1) (1)
ADDI R1,R1,#8 | ADDI R1,R1,#8 | ADDI R2,R2,#8 | (1) (1)
ADDI R2,R2,#8 | ADDI R2,R2,#8 | S.S F2,#-8(R1) | (1) (1)
SUBI R3,R3,#2 | SUBI R3,R3,#2 | S.S F5,#-4(R1) | (1) (1)
BNEZ R3,Loop | BNEZ R3,Loop | BNEZ R3,Loop | (3) (4)
Copy loop twice, remove instructions, adjust displacements | Remove WAW and WAR hazards by renaming | Move loads up, move stores down, adjust displacements | 
Time =14 clocks => 7 clocks per iteration. SPEEDUP: 15/7 = 2.14
Notes: Let’s revisit the program adding two vectors together. In Figure 3.12 we unroll the loop twice. At
first (3.12(a)) the compiler replicates the code, removes the branch and redundant updates of
address registers, and adjusts the displacement of the two Stores. The basic block size is now
almost doubled. However, code motion inside that larger basic block is very limited because of
WAW and WAR hazards on registers. For example, the compiler cannot move the third Load up
across the first ADD.S because of the WAR hazard on F0. Similarly, the first Store cannot be
moved down across the second ADD.S because of the WAW hazard on F2.
To remove these false dependencies (WAW and WAR) the compiler renames the FP registers, as
shown in Figure 3.12(b). Renaming is a general technique to avoid hazards due to false (naming)
dependencies. False dependencies and their resulting hazards are due to limited storage (register or
memory) size. With an infinite number of registers or memory locations the compiler would always
allocate a new value to a new register or memory address and WAW and WAR hazards would be
eliminated. In Figure 3.12 new FP registers are allocated to the values of the second iteration in the
body of the loop. Thus registers F0, F1and F2 have been renamed to registers F3, F4, and F5 in the
second part of the new loop body. Now, Loads can be moved up and Stores can be moved down, as
shown in Figure 3.12(c). This code has no stall in the pipelined CPU of Figure 3.8. Note that
addresses of Stores have been adjusted. The number of clocks taken by each instruction in the ID
stage is shown between parentheses in the schedule after each instruction (1st number). The number
of clocks for the body of the unrolled loop is 14 or 7 clocks per iteration of the original loop.
The speedup with respect to the unoptimized loop is 15/7 or 2.14.

## Slide 88: Loop unrolling
Superpipelined processor (2nd column)
  Total time = 18 clocks => 8.5 clocks per iteration of original loop
  Clock rate (frequency) is 2x as fast
  Speedup = 2x 15/8.5 = 3.52

## Slide 89: Loop unrolling
Superscalar processor
  Not so good because the fraction int/fp instruction far from 50-50
  14 clocks for 2 iterations => speedup: 15/7 = 2.1
Schedule | (2nd-issue-width) | Time | Program
L.S F0,0(R1) |  | (1) | L.S F0,0(R1)
L.S F1,0(R2) |  | (1) | L.S F1,0(R2)
L.S F3,#4(R1) |  | (1) | L.S F3,#4(R1)
L.S F4,#4(R2) |  | (1) | L.S F4,#4(R2)
SUBI R3,R3,#2 | ADD.S F2,F1,F0 | (1) | ADD.S F2,F1,F0
ADDI R1,R1,#8 | ADD.S F5,F3,F4 | (1) | ADD.S F5,F3,F4
ADDI R2,R2,#8 |  | (1) | SUBI R3,R3,#2
S.S F2,#-8(R1) |  | (3) | ADDI R1,R1,#8
S.S F5,#-4(R1) |  | (1) | ADDI R2,R2,#8
BNEZ R3,Loop |  | (3) | S.S F2,#-8(R1)
 |  |  | S.S F5,#-4(R1)
 |  |  | BNEZ R3,Loop

## Slide 90: Loop unrolling: limitations
Works well if loop iterations are independent
Problem with loop-carried RaW dependency
  Example:
For (i=5;i<100;i++)
A[i]:= a[i-5] + b[i];
  Recurrence with distance 5 iterations
  Unroll up to 4 times
  5 times ==> loop carried dependency limits code motion
Consumes architectural registers due to renaming
Code expansion
  Affects I-cache and memory
Problem when the number of iterations is unknown at compile time

## Slide 91: Software pipelining
Original loop is translated into pipelined loop
  Pipeline dependent instructions in different iterations
Let’s look again at our simple loop adding two vectors
Since the ADD.S is the long latency operation, we can pipeline the two loads and the ADD.S with the store
 | O_ITE1 | O_ITE2 | O_ITE3 | O_ITE4
Prologue | L.S F0,0(R1) L.S F1,0(R2) ADD.S F2,F1,F0 | --- | --- | ---
P_ITE1 | S.S F2,0(R1) | L.S F0,0(R1) L.S F1,0(R2) ADD.S F2,F1,F0 | --- | ---
P_ITE2 | --- | S.S F2,0(R1) | L.S F0,0(R1) L.S F1,0(R2) ADD.S F2,F1,F0 | ---
P_ITE3 | --- | --- | S.S F2,0(R1) | L.S F0,0(R1) L.S F1,0(R2) ADD.S F2,F1,F0
Epilogue |  |  |  | S.S F2,0(R1)
O_ITE : Original Loop Iteration
P_ITE Pipelined Iteration
time or cycles
Notes: O_ITE : Original Loop Iteration
P_ITE Pipelined Iteration

## Slide 92: Software pipelining
Prologue: | L.S F0,0(R1)
 | L.S F1,0(R2)
 | SUBI R3,R3,#1
 | ADD.S F2,F1,F0
 | ADDI R1,R1,#4
 | ADDI R2,R2,#4
Loop | S.S F2,#-4(R1) (1)
 | L.S F0,0(R1) (1)
 | L.S F1,0(R2) (1)
 | SUBI R3,R3,#1 (1)
 | ADD.S F2,F1,F0 (1)
 | ADDI R1,R1,#4 (1)
 | ADDI R2,R2,#4 (1)
 | BNEZ R3,Loop (3)
Epilogue | S.S F2,#-4(R1)
No stall, no code expansion, no register renaming
Use both: first loop unrolling then software pipelining
Notes: Let’s revisit the program adding two vectors together. In Figure 3.12 we unroll the loop twice. At
first (3.12(a)) the compiler replicates the code, removes the branch and redundant updates of
address registers, and adjusts the displacement of the two Stores. The basic block size is now
almost doubled. However, code motion inside that larger basic block is very limited because of
WAW and WAR hazards on registers. For example, the compiler cannot move the third Load up
across the first ADD.S because of the WAR hazard on F0. Similarly, the first Store cannot be
moved down across the second ADD.S because of the WAW hazard on F2.
To remove these false dependencies (WAW and WAR) the compiler renames the FP registers, as
shown in Figure 3.12(b). Renaming is a general technique to avoid hazards due to false (naming)
dependencies. False dependencies and their resulting hazards are due to limited storage (register or
memory) size. With an infinite number of registers or memory locations the compiler would always
allocate a new value to a new register or memory address and WAW and WAR hazards would be
eliminated. In Figure 3.12 new FP registers are allocated to the values of the second iteration in the
body of the loop. Thus registers F0, F1and F2 have been renamed to registers F3, F4, and F5 in the
second part of the new loop body. Now, Loads can be moved up and Stores can be moved down, as
shown in Figure 3.12(c). This code has no stall in the pipelined CPU of Figure 3.8. Note that
addresses of Stores have been adjusted. The number of clocks taken by each instruction in the ID
stage is shown between parentheses in the schedule after each instruction (1st number). The number
of clocks for the body of the unrolled loop is 14 or 7 clocks per iteration of the original loop.
The speedup with respect to the unoptimized loop is 15/7 or 2.14.

## Slide 93: Strength and weakness of static pipelines
Strengths
  Hardware simplicity: clock rate advantage over more complex designs
  Very predictable: static performance predictions are reliable
  COMPILER HAS A GLOBAL VIEW OF THE CODE: e.g., Optimize loops
  Power/energy advantage
Weaknesses
  Dynamic events
    Cache misses
    Conditional branches
  No mechanism to deal with cache misses
    Freeze the processor on a miss
    Only one access at a time==>no tolerance for miss latency
Lack of dynamic information
  Memory addresses==>this limits code motion
No good solution for precise exceptions with out-of-order completion
  Embedded vs. General purpose environments
Compilers are complex

## Slide 94: Wrap-Up

## Slide 95: Why RISC? Keep it simple
RISC characteristics:
Reduced number of instructions
Limited addressing modes
  load-store architecture
  enables pipelining
Large register set
  uniform (no distinction between e.g. address and data registers)
Limited number of instruction sizes (preferably one)
  know directly where the following instruction starts
Limited number of instruction formats
Memory alignment restrictions
......
Based on quantitative analysis
  " the famous MIPS one percent rule": don't even think about it when its not used more than one percent

## Slide 96: Other architecture styles
Accumulator architecture
  one operand (in register or memory), accumulator almost always implicitly used
Stack
  zero operand: all operands implicit (on TOS)
Register (load store)
  three operands, all in registers
  loads and stores are the only instructions accessing memory (i.e. with a memory (indirect) addressing mode
Register-Memory
  two operands, one in memory
Memory-Memory
  three operands, may be all in memory
(there are more varieties / combinations)

## Slide 97: Accumulator architecture
Accumulator
ALU
Memory
registers
address
latch
latch
Example code: a = b+c;
load b; // accumulator is implicit operand
add c;
store a;

## Slide 98: Stack architecture
Example code: a = b+c;
push b;
push c;
add;
pop a;
b
b
c
b+c
push b
push c
add
pop a
stack:
ALU
Memory
top of
stack
stack pt
latch
latch
latch

## Slide 99: Other architecture styles
Stack Architecture | Accumulator Architecture | Register-Memory | Memory-Memory | Register (load-store)
Push A | Load A | Load r1,A | Add C,B,A | Load r1,A
Push B | Add B | Add r1,B |  | Load r2,B
Add | Store C | Store C,r1 |  | Add r3,r1,r2
Pop C |  |  |  | Store C,r3
Let's look at the code for C = A + B
Q: What are the advantages / disadvantages of load-store (RISC) architecture?

## Slide 100: General addressing modes
MODE | EXAMPLE | MEANING
REGISTER | ADD R4,R3 | reg[R4] <- reg[R4] +reg[R3]
IMMEDIATE | ADD R4, #3 | reg[R4] <- reg[R4] + 3
DISPLACEMENT | ADD R4, 100(R1) | reg[R4] <- reg[R4] + Mem[100 + reg[R1]]
REGISTER INDIRECT | ADD R4, (R1) | reg[R4] <- reg[R4] + Mem[reg[R1]]
INDEXED | ADD R3, (R1+R2) | reg[R3] <- reg[R3] + Mem[reg[R1] + reg[R2]]
DIRECT OR ABSOLUTE | ADD R1, (1001) | reg[R1] <- reg[R1] + Mem[1001]
MEMORY INDIRECT | ADD R1, @R3 | reg[R1] <- reg[R1] + Mem[Mem[Reg[3]]]
POST INCREMENT | ADD R1, (R2)+ | ADD R1, (R2) then R2 <- R2+d
PREDECREMENT | ADD R1, -(R2) | R2 <- R2-d then ADD R1, (R2)
PC-RELATIVE | BEZ R1, 100 | if R1==0, PC <- PC+100
PC-RELATIVE | JUMP 200 | Concatenate bits of PC and offset

## Slide 101: RISC vs. CISC
COMPLEX vs REDUCED (i.e., Simple) instruction set computers
  Not directly related to implementation
    Complex risc implementations
    Simple cisc implementations
Simple implementation of CISC machines use microcode
  Translation overhead from instruction to micro instruction

## Slide 102
ISA
Assembly, Machine formats
RISC implementation
(Static) Pipelining
Hazards,
  HW solutions
  SW solutions
Out-of-Order pipelines
SW techniques
  Re-scheduling code to reduce stalls, improve performance
  Loop unroling
  Software pipelining
Other architecture styles and other addressing modes
What did you learn?