## Slide 1: Embedded Computer Architecture 5SAI0 Interconnection Networks
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2016-2017

## Slide 2: Overview
Connecting multiple processors or processing elements
How to connect
  Topologies
  Routing
    Deadlock
  Switching
  Performance: Bandwidth and Latency
Material from book:
  Chapter 6

## Slide 3: Parallel computer systems
Interconnect between processor chips (system area network--san)
Interconnect between cores on each chip (Network On Chip -- NOC)
Others (not covered):
  WAN (wide-area network)
  LAN (local area network)

## Slide 4: Bus (shared) or Network (switched)
Network:
  claimed to be more scalable
  no bus arbitration
  point-to-point connections
  but router overhead
node
R
node
R
node
R
node
R
node
R
node
R
node
R
node
R
Example:
NoC with 2x4 mesh
routing network

## Slide 5: Example: MESH
Connects nodes: cache and modules, processing elements, processors, …
  Nodes are connected to switches through a network interface (NI)
  Switch: connects input ports to output ports
  Link: wires transferring signals between switches
Links
  Width and Clock rate determine Bandwidth
  Transfer can be synchronous or asynchronous
From A to B: hop from switch to switch
Decentralized (direct)

## Slide 6: Simple communication model
Point-to-point message transfer
Request/reply: request carries ID of sender
Multicast: one to many
Broadcast: one to all

## Slide 7: Messages and packets
Messages contain the information transferred
  Messages are broken down into packets
Packets are sent one by one
  Payload: message--not relevant to interconnection
  Header/trailer: contains information to route packet
  Error Correction Code: ECC to detect and correct transmission errors

## Slide 8: Example: Bus
Bus = set of parallel wires
  Broadcast communication.
Needs arbitration
Centralized vs distributed arbitration
Line (wire) multiplexing (e.g. address & data)
Pipelining
  For example: arbitration => address => data
Split-transaction bus vs Circuit-switched bus
Properties
  Centralized (indirect)
  Low cost
  Shared
  Low bandwidth

## Slide 9: Design Characteristics of a Network
Topology (how things are connected):
  Crossbar, ring, 2-D and 3-D meshes or torus, hypercube, tree, butterfly, perfect shuffle, ....
Routing algorithm (path used):
  Example in 2D torus: first east-west, then north-south (avoids deadlock)
Switching strategy:
  Circuit switching: full path reserved for entire message, like the telephone.
  Packet switching: message broken into separately-routed packets, like the post office.
Flow control and buffering (what if there is congestion):
  Stall, store data temporarily in buffers
  re-route data to other nodes
  tell source node to temporarily halt, discard, etc.
QoS guarantees
Error handling
etc, etc.

## Slide 10: Switch / Network Topology
Topology determines:
Degree: number of links from a node
Diameter: max number of links crossed between nodes
Average distance: number of links to random destination
Bisection: minimum number of links that separate the network into two halves
Bisection bandwidth = link bandwidth * bisection

## Slide 11: Bisection Bandwidth
Bisection bandwidth: bandwidth across smallest cut that divides network into two equal halves
Bandwidth across “narrowest” part of the network
bisection
cut
not a
bisection
cut
bisection bw= link bw
bisection bw = sqrt(n) * link bw
Bisection bandwidth is important for algorithms in which all processors need to communicate with all others

## Slide 12: Linear and Ring Topologies
Linear array
  Diameter = n-1; average distance ~n/3
  Bisection bandwidth = 1 (in units of link bandwidth)
Torus or Ring
  Diameter = n/2; average distance ~ n/4
  Bisection bandwidth = 2
  Natural for algorithms that work with 1D arrays

## Slide 13: Meshes and Tori
Two dimensional mesh
Diameter = 2 * (sqrt( n ) – 1)
Bisection bandwidth = sqrt(n)
Two dimensional torus
Diameter = sqrt( n )
Bisection bandwidth = 2* sqrt(n)
Generalizes to higher dimensions
Natural for algorithms that work with 2D and/or 3D arrays

## Slide 14: Hypercubes
Number of nodes n = 2d for dimension d
  Diameter = d
  Bisection bandwidth = n/2
0d 1d 2d 3d 4d
Popular in early machines (Intel iPSC, NCUBE, CM)
  Lots of clever algorithms
  Extension: k-ary n-cubes (k nodes per dimension, so kn nodes)
Greycode addressing:
  Each node connected to others with 1 bit different
001
000
100
010
011
111
101
110

## Slide 15: Trees
Diameter = log n.
Bisection bandwidth = 1
Easy layout as planar graph
Many tree algorithms (e.g., summation)
Fat trees avoid bisection bandwidth problem:
  More (or wider) links near top
  Example: Thinking Machines CM-5

## Slide 16: Fat Tree example
A multistage fat tree (CM-5) avoids congestion at the root node
Randomly assign packets to different paths on way up to spread the load
Increase degree near root, decrease congestion

## Slide 17: Common Topologies
Type Degree Diameter Ave Dist Bisection
1D mesh 2 N-1 N/3 1
2D mesh 4 2(N1/2 - 1) 2N1/2 / 3 N1/2
3D mesh 6 3(N1/3 - 1) 3N1/3 / 3 N2/3
nD mesh 2n n(N1/n - 1) nN1/n / 3 N(n-1) / n
Ring 2 N/2 N/4 2
2D torus 4 N1/2 N1/2 / 2 2N1/2
Hypercube Log2N n=Log2N n/2 N/2
2D Tree 3 2Log2N ~2Log2 N 1
Crossbar N-1 1 1 N2/2
N = number of nodes, n = dimension

## Slide 18: More examples
2D-Grid/Mesh
Hypercube
2D-Torus
Criteria | Bus | Ring | 2D-Mesh | 2D-torus | 6-cube | Fully connected
Performance Bisection bandwidth | 1 | 2 | 8 | 16 | 32 | 1024
Cost Ports/switch Total #links | 1 | 3 128 | 5 176 | 5 192 | 7 256 | 64 2080
Assume 64 nodes:

## Slide 19: Butterflies with n = (k-1)2k switches
Connecting 2k processors, with Bisection bandwidth = 2*2k
Cost: lots of wires
2log(k) hop-distance for all connections, however blocking possible
Used in BBN Butterfly
Natural for FFT
O 1
O 1
O 1
O 1
Butterfly switch
Multistage butterfly network: k=3
PE
Switch

## Slide 20: Real machines use all kinds of topologies
Red Storm (Opteron + Cray network, future) | 3D Mesh
Blue Gene/L | 3D Torus
SGI Altix | Fat tree
Cray X1 | 4D Hypercube*
Myricom (Millennium) | Arbitrary
Quadrics (in HP Alpha server clusters) | Fat tree
IBM SP | Fat tree (approx)
SGI Origin | Hypercube
Intel Paragon (old) | 2D Mesh
BBN Butterfly (really old) | Butterfly
older newer

## Slide 21: Routing algorithms
Dimension-order routing (deterministic) = route 1-dimension at a time

## Slide 22: Deadlock
4 necessary conditions for deadlock, given a set of agents accessing a set of shared resources:
  Mutual exclusion
    Only one agent can access the resource at a time
  No preemption
    No mechanism can force agent to relinquish acquired resource
  Hold and wait
    Agent holds on its acquired resources while waiting for others
  Circular wait
    A set of agents wait on each other to acquire each others’ resources => no one can make any progress
shared resources can be SW or HW: critical sections, disk, printer, ..
In NW: Agents = packets; resources = physical or logical channels

## Slide 23: Deadlock avoidance
Assume Mesh or Tori
Assume that packets are free to follow any route
In this example each node is trying to send a packet to the diagonally opposite node at the same time, e.g. (0,0) to (1,1)
To avoid link conflicts, (1,0) uses c3 then c0, and (0,0) uses c0 then c1, etc...
The resource acquisition graph (or channel-dependency graph) on the right shows circular wait => DEADLOCK Possible

## Slide 24: Deadlock avoidance
Enforce dimension-order routing (xy-routing)
  Packet moves first horizontally, then vertically
  No cycle!!!
Problem: contention for channels
  If (0,0) wants to send a packet to (1,1), it must first use c3
  If c3 is occupied, could take alternate route c0 => c1
To avoid deadlocks, use virtual channels
  Alternate set of channels in which yx routing is enforced e.g., c’1
  If c3 is occupied, the packet can safely route through c’0 and c’1.

## Slide 25: Routing in butterflies: Omega NW
Use source and/or destination addresses

## Slide 26: Switch micro-architecture
Physical channel = link
Virtual channel = buffers + link
  link is time-multiplexed among flits

## Slide 27: Switching strategy
Defines how connections are established in the network
Circuit switching = Establish a connection for the duration of the network service
  Example: circuit switching in mesh
    Establish path in network
    Transmit packet
    Release path
    Low latency; high bandwidth
    Good when packets are transmitted continuously between two nodes
Packet switching = Multiplex several services by sending packets with addresses
  Example: remote memory access on a bus
    Send a request packet to remote node
    Release bus while memory access takes place
    Remote node sends reply packet to requester
    In between send and reply, other transfers are supported
  Example: remote memory access on a mesh

## Slide 28: 2 Packet switching strategies
store-and-forward = packet switching, packets move from node to node and are stored in buffers in each node
cut-through = packets move through nodes in pipeline fashion, so that the entire packet moves through several nodes at one time
  Two implementations of cut-through:
    Virtual cut-through switching:
      The entire packet is buffered in the node when there is a transmission conflict
      When traffic is congested and conflicts are high, virtual cut through behaves like store-and-forward
    Wormhole switching:
      Each node has enough buffering for a flit (flow control unit)
      A flit is made of consecutive phits (physical transfer unit), which basically is the width of a link (= number of bits transferred per clock)
      A flit is a fraction of the packet, so the packet can be stored in several nodes (one or more flits per node) on its path
  Note: In virtual cut-through the flit is the whole packet

## Slide 29: Latency models
Sender overhead: creating the envelope and moving packet to NI
Time of flight: time to send a bit from source to destination when the route is established and without conflicts. (Includes switching time.)
Transmission time: time to transfer a packet from source to destination, once the first bit has arrived at destination
  phit: number of bits transferred on a link per cycle
  Basically: packet size/phit size
  flit: flow control unit

## Slide 30: Latency models
Routing time: time to set up switches
Switching time: depends on switching strategy (store-and-forward vs cut-through vs circuit-switched). Affects time of flight and included in that.
Receiver overhead: time to strip out envelope and move packet in

## Slide 31: Measures of latency
Routing distance: Number of links traversed by a packet
Average routing distance: average over all pairs of nodes
Network diameter: longest routing distance over all pairs of nodes
Packets of a message can be pipelined
  Transfer pipeline has 3 stages
    Sender overhead-->transmission -->receiver overhead
  Total message time = time for the first packet + (n-1)/pipeline throughput
End-to-end message latency = sender overhead + time of flight + transmission time + routing time + (n-1) * MAX(sender ov, transmission time, receiver overhead)

## Slide 32
summarize what you learned

## Slide 33: Extra slides

## Slide 34: Comparison between topologies
Switch degree: # of ports for each switch (switch complexity)
Network diameter: worst-case routing distance between any two nodes
Bisection width: # of links in bisection (worst-case bandwidth)
Network size: # of nodes
Interconnection network | Switch degree | Network diameter | Bisection width | Network size
Crossbar switch | N | 1 | N | N
Butterfly (built from k-by-k switches) | k | logk N | N/2 | N
k-ary tree | k+1 | 2logk N | 1 | N
Linear array | 2 | N-1 | 1 | N
Ring | 2 | N/2 | 2 | N
n-by-n mesh | 4 | 2(n-1) | n | N=n2
n-by-n torus | 4 | n | 2n | N=n2
k-dimensional hypercube | k | k | 2k-1 | N=2k
k-ary n-cube | 2k | nk/2 | 2kn-1 | N=nk

## Slide 35: Flow control
Refers to mechanisms to handle conflicts in switch-based networks
Buffers at input and output ports
    In virtual cut-through: buffer for entire packet
    In wormhole: buffer for integral number of flits
Link-level flow control
  Handshake signal
    Rdy indicates whether flits can be transmitted to the destination
    Buffering for cut-through (whole packet) vs wormhole (a few flits

## Slide 36: Switching strategies
Circuit switching:
  Route is set up first
  Routing time = l x r + time of flight
    R to set each switch, l number of switches, and tof to inform the node back
Packet switching
  Route is set up as the packet moves from switch to switch
  Store-and-forward, cut-through

## Slide 37: Switching strategies
Packet latency = sender ov + tof (incl.Switching time) + transmission time + routing time + receiver ov
R: routing time per switch; n: # of phits; l: # of switches; tof: time of flight
Circuit switching
  Packet latency = sender ov + 2xtof + n + lxr + receiver ov
  Tof = l because there are l switches and nb of phits to switch is one
Store-and-forward
  Packet latency = sender ov + tof + n + lxr + receiver ov
  Tof = lxn because switching involves a whole packet (n phits)
Cut-through switching
  Packet latency = sender ov + tof + n + lxr + receiver ov
  Tof = l as in circuit switching
Virtual cut-through switching
  Similar to circuit switching but better bw
  Note that when traffic is congested, cut-through = store-and-forward
Wormhole switching
  Handles conflicts differently
  Switch port has at least enough buffering for a flit
  Blocked packets simply stay in the flit buffers provided in their path
  Packet flits hold circuits in multiple switches

## Slide 38: Bandwidth models
Bottlenecks increase latency
  Transfers are pipelined
  Effective bandwidth = packet_size/max(sender ov, receiver ov, transmission time)
Network contention affects latency and effective bandwidth (not counted in above formula)
Bisection width
  Network is seen as a graph
  Vertices are switches and edges are links
  Bisection is a cut through a minimum set of edges such that the cut divides the network graph into two isomorphic --i.E., Same-- subgraphs
    Example: mesh
  Measures bandwidth when all nodes in one subgraph communicate only with nodes in the other subgraph
Aggregate bandwidth
  Bandwidth across all links divided by the number of nodes

## Slide 39: Topologies
Indirect networks: in is centralized
Bus
Crossbar switch
Multistage interconnection network (min)

## Slide 40: Topologies
Indirect networks: in is centralized
Tree
Butterfly
Best to connect different types of nodes

## Slide 41: Topologies
Direct networks: nodes are directly connected to one another
Decentralized
Linear array and ring
Mesh and tori

## Slide 42: Topologies
Direct networks: nodes are directly connected to one another
Hypercube and k-ary n-cube

## Slide 43: Routing algorithms
Butterfly network