## Slide 1: Embedded Computer Architecture 5SAI0 Chip Multi-Processors (ch 8)
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2016-2017

## Slide 2: Welcome back
Chip Multi-Processors
8.3: Multi-threading:
  Coarse grain multi-threading
  Fine-grain multi-threading
  SMT (simultaneous multi-threading)
    called hyperthreading by Intel
Material:
  Book chapter 8
    8.3: SMT

## Slide 3: New Approach: Multi-Threaded
Multithreading = multiple threads share the functional units of 1 processor
  duplicate independent state of each thread e.g., a separate copy of register file, a separate PC
  HW for fast thread switch; much faster than full process switch  100s to 1000s of clocks
When to switch?
  Next instruction next thread (fine grain), or
  When a thread is stalled, perhaps for a cache miss, another thread can be executed (coarse grain)

## Slide 4: Multithreaded Categories
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 5: Fine-Grained Multithreading
Switches between threads on each instruction, causing the execution of multiples threads to be interleaved
Usually done in a round-robin fashion, skipping any stalled threads
CPU must be able to switch threads every clock
Advantage: it can hide both short and long stalls, since instructions from other threads executed when one thread stalls
Disadvantage: may slow down execution of individual threads
Used in e.g. Sun’s Niagara

## Slide 6: Course-Grained Multithreading
Switches threads only on costly stalls, such as L2 cache misses
Advantages
  Relieves need to have very fast thread-switching
  Doesn’t slow down thread, since instructions from other threads issued only when the thread encounters a costly stall
Disadvantage: hard to overcome throughput losses from shorter stalls, due to pipeline start-up costs
  Since CPU issues instructions from 1 thread, when a stall occurs, the pipeline must be emptied or frozen
  New thread must fill pipeline before instructions can complete
Because of this start-up overhead, coarse-grained multithreading is better for reducing penalty of high cost stalls, where pipeline refill << stall time
Used in e.g. IBM AS/400

## Slide 7: Simultaneous Multi-threading ...
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  | 
M
M
FX
FX
FP
FP
BR
CC
Cycle
One thread, 8 units
M = Load/Store, FX = Fixed Point, FP = Floating Point, BR = Branch, CC = Condition Codes
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  | 
M
M
FX
FX
FP
FP
BR
CC
Cycle
Two threads, 8 units

## Slide 8: Simultaneous Multithreading (SMT)
SMT: dynamically scheduled processors already has many HW mechanisms to support multithreading:
  Large set of virtual registers that can be used to hold the register sets of independent threads
  Register renaming provides unique register identifiers, so instructions from multiple threads can be mixed in datapath without confusing sources and destinations across threads
  Out-of-order completion allows the threads to execute out of order, and get better utilization of the HW
Just adding a per thread renaming table and keeping separate PCs

## Slide 9: IBM Power4
Single threaded
8 FUs
4-issue out-of-order

## Slide 10: IBM Power5: supports 2 threads
2 fetch (PC), 2 initial decodes
2 commits (architected register sets)

## Slide 11: Changes in Power 5 to support SMT
Increased associativity of L1 instruction cache and the instruction address translation buffers
Added per thread load and store queues
Increased size of the L2 (1.92 vs. 1.44 MB) and L3 caches
Added separate instruction prefetch and buffering per thread
Increased the number of virtual registers from 152 to 240
Increased the size of several issue queues
The Power5 core is about 24% larger than the Power4 core because of the addition of SMT support

## Slide 12: Power 5 thread performance ...
Relative priority of each thread controllable in hardware.
For balanced operation, both threads run slower than if they “owned” the machine.

## Slide 13
Do you like Multi-Threading?
Do we need it?
  when?
Can you compare pros and cons of MT and Multi-Processing ?