## Slide 1: Embedded Computer Architecture 5SAI0 Memory hierarchy - an analogy -
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2019-2020

## Slide 2: Huge book depot

## Slide 3: Really huge

## Slide 4: You are “book depot manager”, a librarian
All your books are in a huge depot
Clients can borrow books from this depot
  Getting or storing a book requires 10 minutes (on average; per customer)
  Your clients don’t like this !
  You neither !
You urgently need a solution; preferably cheap. Please find solutions !!

## Slide 5: Suggested Solutions
More books at a time =>
  higher throughput, but
  longer delay (latency) per customer !
Borrowers have to send requests in advance
  not customer friendly; perhaps he/she wants advice first
Robotize the depot =>
  costs 2 Million €
Hire more people =>
  higher throughput, but
  same delay per customer
We need something else !

## Slide 6: Local Shelves
Why does it work?
  temporal locality !!
What about spatial locality?

## Slide 7: Exercise 1: Local shelves
Assume getting/storing a book from/on the local shelves takes 10 seconds
Questions:
  Calculate the average access time (AAT) of a book
    Give also the general formula for AAT
  You miss some information; what? Make reasonable assumption for this.

## Slide 8: Answer 1
Getting/storing a book from/on the local shelves takes 10 seconds
  Calculate the average access time (AAT) of a book
    Give also the general formula for AAT
  You miss some information; what? Make reasonable assumption for this
Answer
  Missing knowledge is the ‘hit-rate’
    assume f_hit = 90 % or 0.9 =>
    miss-rate f_miss = 10 % or 0.1
  AAT = hit-time + f_miss * miss-time = 10 s + 0.10*600 s = 70 s per book
  (still over a minute / book; 7 times slower than the shelves)

## Slide 9: Exercise 2: How to store books
What is an efficient storage system? How/where to store the books?
  for the depot?
  for the local shelves?
What are the issues to look at?
  find a book:
    how to quickly locate a book
    what if a book is not on the shelves
  adding new books:
    how/where to store a returned book?
    how/where to store a new book?
  what if the shelves are full?
    how to replace a book?

## Slide 10: Answer 2
Issues
  quickly finding the location
  easy to store a book / adding a book
Depot:
  could use linear / alphabetic numbering system
  what if a certain shelve is full =>
  dynamically linked shelves
Local shelves
  use part of the number for indicating a shelve
  E.g. if we have 100 shelves, and booknr. = 123456 =>
    use shelvenr. 12 (or any other 2 digits)

## Slide 11: Still not fast enough
How can we further improve the AAT?
Intermediate (second) level shelves (= the traditional library)

## Slide 12: Exercise 3: 2-level shelves
Assume for the library (= second level)
  Book access time = 1 minute,
  hit-rate = 80%
  Shelves are in front of the library.
Questions:
  Why is hit-rate_library (80%) < hit-rate_shelves (90%)?
  What’s the AAT?
  Give a general formula for 2 level shelve solution.

## Slide 13: Answer 3
Assume for the library
  Book access time = 1 minute,
  hit-rate = 80%
  Shelves are in front of the library.
Question
  why is hit-rate_library < hit-rate_shelves?
  what’s the AAT?
    give also general formula for 2 level shelve solution
Answers
  AAT = hit_time + miss_rate_shelves*miss_time_shelves = 10s + 0.10*180s = 28s per book
  where
    miss-time_shelves = hit_time_library + miss-rate_library* miss-time_library = 60s+0.2*600s=180s

## Slide 14: What has a library depot in common with a computer?
Computer has slow memory
  Computer runs at 2 GHz (1 clock cycle = 0.5 ns)
  Memory runs at 10 MHz (access = 100 ns) =>
    memory access requires 200 clock cycles !!
    slows down the calculation about 200 times.
Solution:
  Multiple levels of cache between main memory and processor

## Slide 15: Multi-level cache
Questions:
  Calculate the AAT in ns.
  A program executes 10^10 instructions; every instruction requires 1 processor cycle; what is the total execution time (including memory delay)?
  Invent an efficient storage system for a cache
processor
*,/,+,-
Level-1
$
Level-2
$
Main
memory
t = 0.5 ns
t = 1 ns
hit-rate = 90%
t = 10 ns
hit-rate = 70%
t = 100 ns
hit-rate = 100%
how can this
be 100% ?