## Slide 1: Embedded Computer Architecture 5SAI0 Introduction
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2019-2020

## Slide 2: Lecture overview
Trends
  Performance increase
  Technology factors
Computing classes
Cost
Performance measurement
  Benchmarks
  Metrics
Dependability

## Slide 3: Trends
International Roadmap for Devices and Systems (IRDS) en.wikipedia.org/wiki/International_Roadmap_for_Devices_and_Systems https://irds.ieee.org
before 2017 this was the ITRS roadmap, International Technology Roadmap Semiconductors

## Slide 4: Performance Improvement: from where?
Semi-conductor Technology
  More transistors per chip
  Faster logic
Micro Architecture: Machine Organization
  Deeper pipelines
  More instructions executed in parallel
Architecture: ISA, etc.
  Reduced Instruction Set Computers (RISC > 1985)
  Multimedia extensions
  Explicit parallelism
Compiler technology (see lecture 5LIM0 in Q3)
  Finding more parallelism in code
  Greater levels of optimization
Computer
(Micro) Architecture

## Slide 5: Performance trends of processors (for 1 core)

## Slide 6: Trends in Computer Architecture
Cannot continue to leverage Instruction-Level parallelism (ILP)
  Single processor performance improvement ended in 2003
New models for performance:
  Data-level parallelism (DLP)
  Thread-level parallelism (TLP)
  Request-level parallelism (RLP)
These require explicit restructuring of the application

## Slide 7: Trends in Technology
Integrated circuit technology (Moore’s Law)
  Transistor density: 35%/year
  Die size: 10-20%/year
  Integration overall: 40-55%/year
DRAM capacity: 25-40%/year (slowing)
  8 Gb (2014), 16 Gb (2019), possibly no 32 Gb
Flash capacity: 50-60%/year
  8-10X cheaper/bit than DRAM
Magnetic disk capacity: recently slowed to 5%/year
  Density increases may no longer be possible, maybe increase from 7 to 9 platters
  8-10X cheaper/bit then Flash
  200-300X cheaper/bit than DRAM

## Slide 8: Bandwith vs Latency (developments since 1978 till 2017)
Bandwidth or throughput
  Total work done in a given time
  32,000-40,000X improvement for processors
  300-1200X improvement for memory and disks
Latency or response time
  Time between start and completion of an event
  50-90X improvement for processors
  6-8X improvement for memory and disks
  (for more on above numbers see next slide)

## Slide 9: Bandwith vs Latency
Log-log plot of bandwidth
and latency milestones

## Slide 10: Transistors and Wires
Feature size
  Minimum size of transistor or wire in x or y dimension
  10 microns in 1971 to .011 microns in 2017
  Transistor performance scales linearly
    Wire delay does not improve with feature size!
  Integration density scales quadratically

## Slide 11: Power / Energy
Problem: Get power in, get power out
Thermal Design Power (TDP)
  Characterizes sustained power consumption
  Used as target for power supply and cooling system
  Lower than peak power (1.5X), higher than average power consumption
Clock rate can be reduced dynamically to limit power consumption
Energy per task is often a better measurement

## Slide 12: Frequency and Power trends (of processors)
Intel 80386 consumed ~ 2 W
3.3 GHz Intel Core i7 consumes 130 W
Heat must be dissipated from 1.5 x 1.5 cm chip
This is about the limit of what can be cooled by air

## Slide 13: Power / Energy
Energy E = P*t (power P, execution time t)
P = Pstatic + Pdynamic
static: leakage ~ chip area
dynamic: switching (0->1 or 1->0
  Pdynamic = ½ α f C Vdd2
  Edynamic = ½ α C Vdd2
Reducing clock rate reduces power, not energy
Power vs Energy

## Slide 14: Static Power Consumption
25-50% of total power
Currentstatic x Voltage
Scales with number of transistors
To reduce: power gating:

## Slide 15: Where is the energy / power going?
Static power ~ Area
Dynamic power ~ Switching energy

## Slide 16: Dynamic power reduction
Reduce switching (dynamic) energy by clock gating:

## Slide 17: Dynamic power reduction
Dynamic Voltage-Frequency Scaling (DVFS)

## Slide 18: Classes of Computers
Personal Mobile Device (PMD)
  E.g. smartphones, tablets
  Emphasis on energy efficiency (battery life time) and real-time (short latency)
Desktop Computing
  Emphasis on price-performance
Servers
  Emphasis on availability, scalability, throughput
Clusters / Warehouse Scale Computers / Clouds
  Used for “Software as a Service (SaaS)”
  Emphasis on availability and price-performance
  Sub-class: Supercomputers, emphasis: floating-point performance and fast internal networks
Internet of Things/Embedded Computers (on the IoT Edge)
  Emphasis: price

## Slide 19: Some history: Earliest computers
Mechanical
  Charles Babbage: Difference Engines
Electro-Mechanical
  Konrad Zuse's Z1, Z2, Z3
Electronic
  ENIAC
Part of Difference Engine 1, 1832

## Slide 20: Mechanical: Difference Engine no.2
Science museum
Compute values of polynomial functions using finite differences
Smaller version no.0 in 1822

## Slide 21: Electro-Mechanical
Z3, 1941
1400 relais
Museum Munchen

## Slide 22: ENIAC: Electronic Numerical Integrator And Computer, 1946

## Slide 23: VLSI Developments: Technology Improvement
1946: ENIAC electronic numerical integrator and computer
Floor area
  140 m2
Performance
  multiplication of two 10-digit numbers in 2 ms
Power
  160 KWatt
Today: High Performance microprocessor
Chip area
  100-400 mm2 (for multi-core)
Board area
  200 cm2; improvement of 104
Performance:
  64-bit multiply in O(1 ns); improvement of 106
Power
  ~20 Watt; improvement ~8000
And: cost reduction!!

## Slide 24: 8” MIPS64 R20K wafer (564 dies)
Drawing single-crystal Si ingot from furnace….
Then, slice into wafers and pattern it…

## Slide 25: What's the price of an IC ?
Die cost + Testing cost + Packaging cost
Final test yield
Final test yield = fraction of packaged dies which pass the final testing state
Wafer cost
Dies per Wafer * Die yield
IC cost =
Die cost =
Dies per wafer

## Slide 26: Die yield
Die yield: fraction of good dies on a wafer
Bose-Einstein formula:
  Die yield = Wafer yiels * 1/(1+Defects per unit area * Die area)N
    Defects per unit area = 0.016-0.057 defects per square cm (2010)
    N = process-complexity factor = 11.5-15.5 (40 nm, 2010)

## Slide 27: What's the price of the final product ?
Component Costs
Direct Costs (add 25% to 40%)
  recurring costs: labor, purchasing, warranty
Gross Margin (add 82% to 186%)
  nonrecurring costs: R&D, marketing, sales, equipment maintenance, rental, financing cost, pretax profits, taxes
Average Discount to get List Price (add 33% to 66%):
  volume discounts and/or retailer markup
Component
Cost
Direct Cost
Gross
Margin
Average
Discount
Avg. Selling Price
List Price
15% to 33%
6% to 8%
34% to 39%
25% to 40%

## Slide 28: Quantitative Principles of Design
Take Advantage of Parallelism
Principle of Locality
Focus on the Common Case
  E.g. common case supported by special hardware; uncommon cases in software
  However, check Amdahl’s Law, or Gustafson's Law
The Performance Equation

## Slide 29: 1. Parallelism
Parallelism helps performance, ..... but also energy !!
  having more performance allows to reduce Vdd (and frequency)
How to improve performance?
  Pipelining (see next slides; other methods come later during the course)
    single cycle throughput with multi-cycle latency (i.e. latency > 1/throughput)
  Powerful instructions
    MD-technique: Multiple Data operands per operation
    MO-technique: Multiple Operations per instruction
  Multiple instruction issue
    Issue more instructions per cycle in a single instruction-program stream
  Multiple (instruction) streams (or programs, or tasks)

## Slide 30: Example of Pipelined Instruction Execution
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5

## Slide 31: Pipelining Limitations: Hazards:
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Hazards: prevent next instruction from executing during its designated clock cycle
Structural hazards:
  Use same hardware to do two different things at once
Data hazards:
  Instruction depends on result of prior instruction still in the pipeline
Control hazards:
  It takes several cycles before knowing whether a conditional branch should be taken or not

## Slide 32: 2. The Principle of Locality
Programs access a relatively small portion of the address space at any instant of time (boths for Instructions and for Data).
Two Different Types of Locality:
  Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon (e.g., instruction loops, data reuse)
  Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon (e.g., straight-line code, array access)
Last 30 years, HW relied on locality for memory perf.
Proc.
Memory
Instr$
Data$
Notes: The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
This is kind of like in real life, we all have a lot of friends. But at any given time most of us can only keep in touch with a small group of them.
There are two different types of locality: Temporal and Spatial. Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
This is like saying if you just talk to one of your friends, it is likely that you will talk to him or her again soon.
This makes sense. For example, if you just have lunch with a friend, you may say, let’s go to the ball game this Sunday. So you will talk to him again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon.
Once again, using our analogy. We can usually divide our friends into groups. Like friends from high school, friends from work, friends from home.
Let’s say you just talk to one of your friends from high school and she may say something like: “So did you hear so and so just won the lottery.”
You probably will say NO, I better give him a call and find out more.
So this is an example of spatial locality. You just talked to a friend from your high school days. As a result, you end up talking to another high school friend. Or at least in this case, you hope he still remember you are his friend.
+3 = 10 min. (X:50)

## Slide 33: Memory Hierarchy Levels
CPU Registers
100s Bytes
300 – 500 ps (0.3-0.5 ns)
L1 and L2 Cache
10s-100s K Bytes
~1 ns - ~10 ns
~ $100s/ GByte
Main Memory
many G Bytes
80ns- 200ns
~ $10/ GByte
Disk
10s T Bytes, 10 ms (10,000,000 ns)
~ $0.1 / GByte
Capacity
Access Time
Cost
Tape
infinite
sec-min
~$0.1 / GByte
Registers
L1 Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Xfer Unit
prog./compiler
1-32 bytes
cache cntl
32-64 bytes
OS
4K-8K bytes
user/operator
Gbytes
Upper Level
Lower Level
faster
Larger
L2 Cache
cache cntl
64-128 bytes
Blocks
still needed?

## Slide 34: 3. Focus on the Common Case
Favor the frequent case, e.g.
  Instruction fetch and decode units used more frequently than multiplier, so optimize it first
  If database server has 50 disks / processor, storage dependability dominates system dependability, so optimize it first
Frequent case is often simpler and can be done faster
  E.g., overflow is rare when adding 2 numbers, so improve performance by optimizing more common case of no overflow
  May slow down overflow, but overall performance improved by optimizing for the normal case
What is frequent case? How much performance improved by making case faster? => Amdahl’s Law

## Slide 35: Amdahl’s Law
Speedupoverall =
Texec,old
Texec,new
=
1
(1 - fparallel) + fparallel
Speedupparallel
exc. time
serial part
parallel part
serial part
fparallel= parallel fraction

## Slide 36: Amdahl’s Law: exercise
Floating point instructions improved to run 2 times faster, but only 10% of actual instructions are FP
Speedupoverall
=
Texec,new =

## Slide 37: Amdahl’s Law
Floating point instructions improved to run 2 times faster; but only 10% of actual instructions are FP
Speedupoverall
=
1
0.95
=
1.053 => 5.3%
Texec,new = Texec,old x (0.9 + 0.1/2) = 0.95 x Texec,old

## Slide 38: Amdahl's law

## Slide 39: Are we rescued by Gustafson's law ?
Gustafson proposed a change to Amdahl's law
  assumes the data (input) set for the parallel part scales (increases) linearly with the number of processors => much better scaling
Speedup = P - fseq(P-1) where:
  P = # of processors (parallel speedup), fseq = sequential fraction of the original program = 1-fpar
Notes: Easy to derive
On sequential (single) single processor T = 1 ( = fseq + fpar)
On parallel system with P processors : we have much more data, the parallel part is P times bigger =>
Tseq = fseq + P*fpar, Tpar = 1 =>
Speedup = Tseq/Tpar = fseq + P*fpar = fseq + P (1- fseq) = P – fseq (P-1)

## Slide 40: Gustafson's law

## Slide 41: 4. The performance equation
Main performance metric:
Total Execution Time (Texec)
Texec = Ncycles * Tcycle
= Ninstructions * CPI * Tcycle
  CPI = (Average number of) Cycles Per Instruction
  IPC = ....

## Slide 42: Example: Calculating CPI
Typical Mix
Base Machine (Reg / Reg)
Op Freq Cycles CPI(i) (% Time)
ALU 50% 1 .5 (33%)
Load 20% 2 .4 (27%)
Store 10% 2 .2 (13%)
Branch 20% 2 .4 (27%)
1.5

## Slide 43: Measurement Tools
Benchmarks, Traces, Mixes
Hardware: Cost, delay, area, power estimation
Simulation (many levels, see ch. 9)
  ISA, RT, Gate, Circuit level
Queuing Theory (analytic models)
Rules of Thumb
Fundamental “Laws”/Principles

## Slide 44: Aspects of CPU Performance what influences what?
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
Instr. Cnt CPI Clock Rate
Program
Compiler
Instr. Set
Organization
Technology

## Slide 45: Aspects of CPU Performance check the ‘x’
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
Inst Count CPI Clock Rate
Program X X
Compiler X X
Inst. Set. X X
Organization X X
Technology X

## Slide 46: SPEC benchmarks, since 1989
CPU: CPU2006: CINT2006 and CFP2006
Graphics: SPECviewperf12 e.o.
HPC/OMP: HPC2002; OMP2001, MPI2006
Java Client/Server: jAppServer2004
Java runtime: SPECjvm2008
Mail Servers: MAIL2001
Network File System: SDS97_R1
Power: under development
Web Servers: WEB2005
Handheld: under development
Cloud: SPEC Cloud_laaS 2016
see for updates: www.spec.org

## Slide 47: SPEC CPU benchmarks

## Slide 48: How to Summarize Performance?
Arithmetic mean (or weighted arithmetic mean)
  tracks execution time: (Ti)/n , or weighted: (Wi*Ti)
Normalized execution time is handy for scaling performance
  e.g., speedup: X times faster than VAX-780 (a famous computer in 1978)
Do not take the arithmetic mean of normalized execution time!
  Use the Geometric Mean = (i Ratioi)1/n
  Ratio can e.g. be the Speedup (compared to a Reference machine)

## Slide 49: Dependability: How reliable is your system?
Metrics:
MTTF: mean time between failure (in hours)
MTTR: mean time to repair (in hours)
Availability = MTTF / (MTTF + MTTR)
FIT: failures in time (per 1 billion hours = 114k years!)
Example
  MTTF = 1,000,000 hours (= 114 years!)
  FIT = 109 / MTTF = 1000 failures per billion hours

## Slide 50: Dependability of a Disk subsystem
10 disks MTTF = 1,000,000 hours
1 Disk controller MTTF = 500,000
1 power-supply MTTF = 200,000
1 fan MTTF = 200,000
1 Disk cable MTTF = 1,000,000
Question: What is MTTF of this subsystem?
  assuming lifetimes are exponential distributed &
  failures are independ
FIT = Σi FITi = 109 * {10 *1/106 + 1/(5.105) + .. } = 23000 failures / billion hours
MTTF = 1/FIT = 109 hours / 23000 = 43,500 hours (~ 5 years)

## Slide 51: Dependability: let's use redundancy
Two powersupplies:
  each MTTF = 20,000 hours (2.3 years) and
  MTTR = 1 day
What is the MTTF of the combined power supply?
On average the first disk fails in MTTF/2 = 10,000 hours
During repair second failure happens with probability p = MTTR / MTTF = 24/20,000
MTTFpair = 10,000/p = 83,000,000 hours (= 9475 years)

## Slide 52: What did you learn?
Trends
  Performance increase slows down
    almost none for single processor
  Technology factors, Energy problem
Energy and Performance equations / issues
Main design issues, like parallelism, performance, cost & energy
How the cost of a computer is build up
Performance measurement
  Benchmarks & Metrics; summarizing performance
System reliability: Dependability calculations

## Slide 53: Backup
some recent computer chips / systems
example of calculating Geometric mean
some extra info about course topics

## Slide 54: Intel Dunnington 6-core

## Slide 55: AMD Hydra 8 core
45 nm
L2: 1MByte/core
L3: shared 6MByte

## Slide 56: Intel Xeon Phi
Knights Landing (2015):
build on Silvermont (Atom) x86 cores
with 512-bit (SIMD) AVX units
up to 72 cores / chip => 3 TeraFlops
14 nm
using Micron’s DRAM 3D techn. (hybrid memory cube)

## Slide 57: Nr 1 in the Top 500 supercomputers
IBM Summit
  122.3 petaflops on Linpack
  4356 nodes
  per node:
    2x 22-core Power9
    6 NVIDIA Tesla V100 GPUs

## Slide 58: Summarize performance: example of Geometric mean
  Mean speedup comparisons between two machines are independent of the used reference machine
 | Program A | Program B | Arithmetic Mean | Speedup (ref 1) | Speedup (ref 2)
Machine 1 | 10 sec | 100 sec | 55 sec | 91.8 | 10
Machine 2 | 1 sec | 200 sec | 100.5 sec | 50.2 | 5.5
Reference 1 | 100 sec | 10000 sec | 5050 sec |  | 
Reference 2 | 100 sec | 1000 sec | 550 sec |  | 
 |  | Program A | Program B | Arithmetic | Harmonic | Geometric
Wrt Reference 1 | Machine 1 | 10 | 100 | 55 | 18.2 | 31.6
 | Machine 2 | 100 | 50 | 75 | 66.7 | 70.7
Wrt Reference 2 | Machine 1 | 10 | 10 | 10 | 10 | 10
 | Machine 2 | 100 | 5 | 52.5 | 9.5 | 22.4
Speedup

## Slide 59: Computer Architecture Topics
Instruction Set Architecture
Pipelining, Hazard Resolution,
Superscalar, Reordering,
Prediction, Speculation,
Vector, DSP
Addressing,
Protection,
Exception Handling
L1 Cache
L2 Cache
DRAM
Disks, WORM, Tape
Coherence,
Bandwidth,
Latency
Emerging Technologies
Interleaving
Bus protocols
RAID
VLSI
Input/Output and Storage
Memory
Hierarchy
Pipelining and Instruction
Level Parallelism

## Slide 60: Computer Architecture Topics
M
Interconnection Network
S
P
M
P
M
P
M
P
° ° °
Topologies,
Routing,
Bandwidth,
Latency,
Dependability /
Reliability
Network Interfaces
Programming model
Shared Memory,
Message Passing,
Data Parallelism
Processor-Memory-Switch
Multiprocessors
Networks and Interconnections