## Slide 1: CGRA Cookbook 2019

## Slide 2: Task Implementing Butterworth filter on the CGRA
Naive implementation of Butterworth filter

## Slide 3: Task Implementing Butterworth filter on the CGRA
Naive implementation of Butterworth filter
Goal Finding the best performance for minimal energy & area.

## Slide 4: Where can you optimize?
Change the algorithm.
Change the architecture.
Optimized code mapping.

## Slide 5: Changing the architecture.
SIMD
Exploit data level parallelism (DLP)

## Slide 6: Changing the architecture.
VLIW
Exploit instruction level parallelism (ILP)

## Slide 7: Changing the architecture.
ILP + DLP

## Slide 8: Changing the architecture.

## Slide 9: Changing the architecture.
Graphical view.
$ xdot ~/CGRA/build/butterworth/<name>/report/architecture.dot

## Slide 10: Changing the architecture.
Important points.
Each ID must have a unique name.
All IDs must be connected to the ABU, for the program to advance.
FUs are connected to their corresponding IDs.

## Slide 11: Optimizing code mapping.
Parallel Assembly (PASM)

## Slide 12: Optimizing code mapping.
Important points.
All IDs are specified in different columns.
Parallel Assembly (PASM)

## Slide 13: Optimizing code mapping.
Important points.
All IDs are specified in different columns
Instruction execution starts at count 1 ,
(not count 0)
Parallel Assembly (PASM)

## Slide 14: Optimizing code mapping.
Important points.
All IDs are specified in different columns
Instruction execution starts at count 1 ,
(not count 0)
3. “jai 0” ends program execution.
Parallel Assembly (PASM)
Detailed ISA can be found on https://oncourse.tue.nl

## Slide 15: Debugging
Use Modelsim.
$ cd ~/CGRA/benchmarks/butterworth/<name>
$ make sim
To add register file :
TB_CGRA_Top
dut
CGRA_Core_inst
CGRA_Compute_Wrapper_inst
CGRA_Compute_inst
rf_inst
Parallel Assembly (PASM)

## Slide 16: Makefile
make sim
Runs modelsim with GUI.
make run
Runs modelsim in the command line.
make compare
Runs simulation and compares the output with actual one (given in compare directory).
make performance
Runs simulation and gives quick performance estimates (less accurate).
make report
Runs simulation and generates a report in build/<name>/report (slower but accurate).
make clean
Cleans the build directory for the benchmark.

## Slide 17: Optimization Hints
Bypassing

## Slide 18: Optimization Hints
Bypassing
Multiply

## Slide 19: Optimization Hints
Bypassing
Multiply
Store

## Slide 20: Optimization Hints
Bypassing
Multiply
Store
Load

## Slide 21: Optimization Hints
Bypassing
Multiply
Store
Load
Add

## Slide 22: Optimization Hints
Bypassing
Multiply
Store
Load
Add

## Slide 23: Optimization Hints
Bypassing
Multiply
Store
Load
Add

## Slide 24: Optimization Hints
SIMD

## Slide 25: Optimization Hints
Bypassing + SIMD

## Slide 26: Optimization Hints
Single Cycle Loop

## Slide 27: Optimization Hints
Single Cycle Loop

## Slide 28: Optimization Hints
Data reuse
Automatic address generation
Adding ABU (for accumulation)

## Slide 29: Changing the algorithm
Change the Butterworth algorithm.
Given direct implementation
Biquad
implementation

## Slide 30: Changing the algorithm
Change the Butterworth algorithm.
Given direct implementation
Biquad
implementation
In case, you use a different algorithm, provide us with the C implementation as well.

## Slide 31: Updated Server List
co2.ics.ele.tue.nl
co3.ics.ele.tue.nl
co4.ics.ele.tue.nl
co9.ics.ele.tue.nl
co10.ics.ele.tue.nl
co13.ics.ele.tue.nl
co17.ics.ele.tue.nl

## Slide 32: Resources
Assignment details and guideline
https://oncourse.tue.nl