## Slide 1: Embedded Computer Architecture 5SAI0 Exploiting Data Reuse: From Loop Transformations to Automatic Optimization
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/ECA
h.corporaal@tue.nl
TUEindhoven
2019-2020

## Slide 2: Application Excecution Time
High performance computing
Embedded computing
Small portions of the code dominate execution time
  Hot spots
  Loops
Apply Loop Transformations
for(i=0; i<N; i++){
for(j=0; j<N; j++){
for(k=0; k<N; k++)
c[i][j] += a[i][k] * b[k][j];
}}

## Slide 3: Loop Transformations
Can help you in many compute domains
CPU Code
Parallelism
Memory Hierarchy
Convert Loops to
GPU Threads
Embedded Devices
Fine-tune for architecture
HDL, HW Description Languages

## Slide 4: GoogLeNet: Energy
Energy breakdown
[Yang.e.a CVPR'17]
CNN layers: 21 depth, 57 in total
FC layer: 1
Weights: 7.0 M
MACs: 1.43 G per input

## Slide 5: Where is the energy going

## Slide 6: Another example: VGG16
Conv layers: 13
FC Layers: 3
Weights: 138 M
MACs: 15.5 G per input
Simonyan, ICLR 2015

## Slide 7: Reducing external memory accesses
Original code
Rescheduled code
VGG16 example
Conclusion: we need advanced loop transformation to exploit data locality (in local buffers),
reducing external accesses

## Slide 8: Loop Transformation Classes
Data-Flow-Based Transformations
Iteration Reordering Transformations
Loop Restructuring Transformations

## Slide 9: Data-Flow-Based Transformations
Can be very useful in case of a:
  Simple compiler
  Simple architecture
    No Hardware Multiplier
    No Out-Of-Order Superscalar
    No Speculative Branch Prediction
  If you are in a hurry and missing a few percent
* Examples are from: D.F. Bacon, S.L. Graham, and O.J. Sharp, Compiler transformations for high-performance computing. ACM Comput. Surv. 26, (1994)

## Slide 10: Loop-Based Strength Reduction
Replace an expensive operation
Can be multiplication, especially for embedded cores
No HW multiplier, e.g. MicroBlaze
An optimizing compiler can help
c=3;
for(i=0; i<N; i++){
a[i] = a[i] + i*c;
}
c=3;
T=0;
for(i=0; i<N; i++){
a[i] = a[i] + T;
T = T + c;
}

## Slide 11: Induction Variable Elimination
Induction variable?
  Compute loop exit conditions
  Compute memory addresses
Given a known final value and relation to addresses
  Possible to eliminate index calculations
Again an optimizing compiler can help
A = &a[0];
T = &a[0] + N;
while(A<T){
*A = *A + c;
A++;
}
for(i=0; i<N; i++){
a[i] = a[i] + c;
}
Notes: Performing the control of a loop is basically overhead. I refer to the increment of i and the compare of i<N to check if the exit condition is not met.
With induction variable elimination we can reduce this overhead.

## Slide 12: Loop-Invariant Code Motion
Index of c[] does not change
Move one loop up and store in register
Reuse it over iterations of inner loop
Most compilers can perform this
Example is similar to Scalar Replacement Transformation
for(i=0; i<N; i++){
for(j=0; j<N; j++){
a[i][j]=b[j][i]+c[i];
}
}
for(i=0; i<N; i++){
T=c[i];
for(j=0; j<N; j++){
a[i][j]=b[j][i]+T;
}
}

## Slide 13: Loop Unswitching
Conditional execution in body
Speculative branch prediction helps but
This branch is loop invariant code
  Move it outside the loop
  Each execution path independent loops
Increases code size
for(i=0; i<N; i++){
a[i] = b[i];
if(x<7){a[i]+=5;}
}
if(x<7){
for(i=0; i<N; i++){
a[i]=b[i];
a[i]+=5;
}
}
else{
for(i=0; i<N; i++){
a[i]=b[i];
}
}

## Slide 14: Loop Transformation Classes
Data-Flow-Based Transformations
Iteration Reordering Transformations
Loop Restructuring Transformations

## Slide 15: Iteration Reordering Transformations
Change the relative ordering
  Expose parallelism by altering iteration dependencies
  Improve locality by matching with a memory hierarchy
We need more theory to understand these
Or combine the tricks to form a methodology
Normal compilers don’t help you with this
Only state-of-the-art compilers can help
  Often research compilers ;)
*Based on:
M. Wolf, M. Lam, A Data Locality Optimizing Algorithm. ACM SIGPLAN, PLDI (1991)

## Slide 16: Loop representation as Iteration Space
for(i=0; i<N; i++){
for(j=0; j<N; j++){
A[i][j] = B[j+3][i+2];
Each position represents an iteration
  At each position 1 or more array elements are accessed

## Slide 17: Visitation order in Iteration Space
for(i=0; i<N; i++){
for(j=0; j<N; j++){
A[i][j] = B[j+3][i+2];
Iteration space is not data space

## Slide 18: But we don’t have to be regular
A[j][j] = B[j+3][i+2];
But order can have huge impact on:
  Memory Hierarchy
    E.g. Reuse of data
  Parallelism
  Loop or control overhead

## Slide 19: Types of data reuse
for i := 0 to 2
for j := 0 to 100
A[i][j] = B[j+1][0] + B[j][0];
Assumptions:
1. Memory layout row mayor
2.Cache line size=4 elements
Notes: Spatial reuse = reuse of neighboring values in cache lines; Temporal reuse = Single value reused at different moment in time;
Group reuse = multiple memory references in the loop body point to the same memory location at different iteration values (temporal) or they point to neighboring values (spatial)

## Slide 20: Types of data reuse
for i := 0 to 2
for j := 0 to 100
A[i][j] = B[j+1][0] + B[j][0];
Notes: Spatial reuse = reuse of neighboring values in cache lines; Temporal reuse = Single value reused at different moment in time;
Group reuse = multiple memory references in the loop body point to the same memory location at different iteration values (temporal) or they point to neighboring values (spatial)

## Slide 21: When do cache misses occur?
for(i=0; i<N; i++){
for(j=0; j<N; j++){
A[i][j] = B[j][i]; // again row major ordering
// assumed
Notes: Note: assuming limited cache size, such that number of elements in 1 row of B is bigger than the number of cache lines.

## Slide 22: Optimize array accesses for memory hierarchy
Solve the following questions?
  When do misses occur?
    Use “locality analysis”
  Is it possible to change iteration order to produce better behavior?
    Evaluate the cost of various alternatives
  Does the new ordering produce correct results?
    Use “dependence analysis”
Notes: Introduce theory for memory hierarchy optimization

## Slide 23: Different Reordering Transformations
Loop Interchange
Tiling
Skewing
Loop Reversal
Can improve locality
Can enable above

## Slide 24: Loop Interchange or Loop Permutation
for(i=0; i<N; i++){ for(j=0; j<N; j++){
for(j=0; j<N; j++){ for(i=0; i<N; i++){
A[j][i] = i*j; A[j][i] = i*j;
N is large with respect to cache size
Normal compilers will not help you!
Chart: Execution Time [ms]
| -O0 | -O3
Without | 809.7 | 385
With | 545.3 | 77
Notes: Example to demonstrate the possible locality increase due to interchange

## Slide 25: Tiling the Iteration Order
Result in Iteration Space
for(jj=0; jj<N; jj+=Tj){
for(i=0; i<N; i++){ for(i=0; i<N; i++){
for(j=0; j<N; j++){ for(j=jj; j<jj+Tj; j++){
f(A[i],A[j]); f(A[i],A[j]);
assume
Tj=4
Notes: Example to show the potential locality increase due to tiling

## Slide 26: Cache Effects of Tiling
for(jj=0; jj<N; jj+=Tj){
for(i=0; i<N; i++){ for(i=0; i<N; i++){
for(j=0; j<N; j++){ for(j=jj; j<jj+Tj; j++){
f(A[i],A[j]); f(A[i],A[j]);
assume Tj=4
Iteration
space (i,j)
Again, assume N >> cache size - A does not fit in the cache

## Slide 27: Is this always possible?
No, dependencies can prevent transformations
Interchange and Tiling is not always valid!
Example Interchange
  Spatial locality
  Dependency (1,-1) (see figure)
for(i=1; i<N; i++){
for(j=0; j<N; j++){
a[j][i] = a[j+1][i-1] + 1;
}
}

## Slide 28: Loop Reversal
  Dependency (1,-1) Dependency (1,1)
Interchange is valid now
for(i=0; i<N; i++){
for(j=0; j<N; j++){
a[j][i] = a[j+1][i-1] + 1;
}
}
for(i=0; i<N; i++){
for(j=N-1; j>=0; j--){
a[j][i] = a[j+1][i-1] + 1;
}
}

## Slide 29: More difficult example
For(i=0; i<6; i++){ D={(0,1),(1,0),(1,-1)}
for(j=0; j<7; j++){
A[j+1] += 1/3 * (A[j] + A[j+1] + A[j+2]);
What are other legal visit orders?

## Slide 30: Loop Skewing
for(i=0 i<6; i++){ D = {(0,1),(1,0),(1,-1)}
for(j=0; j<7; j++){
A[j+1] = 1/3 * (A[j] + A[j+1] + A[j+2]);
for(i=0; i<6; i++){ D = {(0,1),(1,1),(1,0)}
for(j=i; j<7+i; j++){
A[j-i+1] = 1/3 * (A[j-i] + A[j-i+1] + A[j-i+2]);
Notes: Original dependence vector top vs dependence vector bottom

## Slide 31: Enables Tiling
Apply Skew Transformation
Apply Tiling

## Slide 32: Is It Really That Easy ?
No, we forget a few things
Cache capacity and reuse distance
  If caches were infinitely large, we would be finished
For deep loopnests analysis can be very difficult
It would be much better to automate these steps
We need more theory and tools
Cost models

## Slide 33: Data Reuse distance
The number of unique accesses between a use and a reuse is defined as the (data) reuse distance:
( a[0] a[6] a[20] b[1] a[6] a[0] ) => RD (a[0])= 3
* C. Ding, Y. Zhong, Predicting Whole-Program Locality through Reuse Distance Analysis, PLDI (2003)
Second a[0] access is a cache hit if
  Fully associative cache with n=4 entries
  Optimal LRU, least recently used, replacement policy
In general:
  Cache hit if RD < n
  Cache miss if RD ≥ n
We can measure reuse distance with profiling tools:
  Suggestions for Locality Optimization (SLO)
Beyls, K., D'Hollander, E. Refactoring for Data Locality, IEEE Computer Vol. 42, no. 2 2009
Notes: Can be line adresses

## Slide 34: Study a matrix multiplication kernel
Loop interchange
for(i=0; i<Bi; i++){
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
C[i][j] += A[i][k] * B[k][j];
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
for(i=0; i<Bi; i++){
C[i][j] += A[i][k] * B[k][j];

## Slide 35: Loop tiling
Can be done in multiple dimensions
Manual exploration is intractable
for(i=0; i<Bi; i++){
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
C[i][j] += A[i][k] * B[k][j];
for(i=0; i<Bi; i++){
for(jj=0; jj<Bj; jj+=Tj){
for(k=0; k<Bk; k++){
for(j=jj; j<jj+Tj; j++)
C[i][j] += A[i][k] * B[k][j];

## Slide 36: Loop Transformation Classes
Data-Flow-Based Transformations
Iteration Reordering Transformations
Loop Restructuring Transformations
  Alter the form of the loop

## Slide 37: Loop Unrolling
Duplicate loop body and adjus loop header
  Increases ILP (Instruction Level Parallelism)
  Reduces loop overhead (fewer branches and counter increments)
  Possibilities for common subexpression elimination
If partial unroll, loop should stay in original bound!
Downsides
  Code size increases, can increase I-cache miss-rate
for(i=1; i<N; i++){
a[i]=a[i-1]+a[i]+a[i+1];
}
for(i=1; i<N-1; i+=2){
a[i]=a[i-1]+a[i]+a[i+1];
a[i+1]=a[i]+a[i+1]+a[i+2];
}
if(mod(N-1,2)==1){
a[N-1]=a[N-2]+a[N-1]+a[N];

## Slide 38: Loop Merge or Fusion
Why?
  Improve locality
  Reduce loop overhead
for(i=0; i<N; i++){
b[i]=a[i]+1;
}
for(j=0; j<N; j++){
c[j]=b[j]+a[j];
}
for(i=0; i<N; i++){
b[i]=a[i]+1;
c[i]=b[i]+a[i];
}
Location
Time
Production/Consumption
Consumption(s)
Location
Time
Production/Consumption
Consumption(s)

## Slide 39: Fusion is not always allowed
Data dependencies from first to second loop
Fusion is allowed if
   I: cons(I) in loop 2  prod(I) in loop 1
Enabling transformations: Bump, Reverse, Skew
for(i=0; i<N; i++){
b[i]=a[i]+1;
}
N-1>=i
for(i=0; i<N; i++){
c[i]=b[N-1]+a[i];
}
for(i=0; i<N; i++){
b[i]=a[i]+1;
}
i-2 < i
for(i=0; i<N; i++){
c[i]=b[i-2]+a[i];
}

## Slide 40: Loop Bump: Example as enabler
for(i=2; i<N; i++){
b[i]=a[i]+1;
}
for(i=2; i<N; i++){
c[i-2]=b[i+2-2]*0.5;
}
for(i=2; i<N; i++){
b[i]=a[i]+1;
}
for(i=0; i<N-2; i++){
c[i]=b[i+2]*0.5;
}
for(i=2; i<N; i++){
b[i]=a[i]+1;
c[i-2]=b[i]*0.5;
}
i+2 > i => direct merging not possible
i+2-2 = i => possible to merge

## Slide 41: Automatic frameworks
These are the tools to abstract away from code:
Model reuse (potential for locality)
Local iteration space
Transform loops to take advantage of reuse
Does this still give valid results?
Loop transformation theory
  Iteration space
  Dependence vectors
  Unimodular transformations
  Polyhedral Model

## Slide 42: Tricks of the Trade: Main Take-Aways
Data-Flow-Based Transformations
  Good compilers can help
Iteration Reordering Transformations
  High-level transformations
  Compilers are often not enough
  Huge gains for parallelims and locality
  Be carefull with dependencies
Loop Restructuring Transformations
  Similar to reordering
Tools can help you: Check out SLO
Optimizing source to source compilers as well
  If you are lucky; however don’t support all constructs
  Check out Polyhedral compilers, e.g. Pluto

## Slide 43: Extra Enabler Transformations
Many of these can be very usefull
Especially to enable the bennificial ones:
  Interchange
  Tiling
  Fusion
Often you need combinations to get the job done!
Make sure you can use them all for the:
Data Memory Management Assingment

## Slide 44: Backup
Extra details for
- several (enabling) loop transformations
- and some theory

## Slide 45: Loop Extend
for I = exp1 to exp2
A(I)

for I = exp3 to exp4
if Iexp1 and Iexp2
A(I)
exp3  exp1
exp4  exp2

## Slide 46: Loop Extend: Example as enabler
for (i=0; i<N; i++)
B[i] = f(A[i]);
for (i=2; i<N+2; i++)
C[i-2] = g(B[i]);

Loop Extend
for (i=0; i<N+2; i++)
if(i<N)
B[i] = f(A[i]);
for (i=0; i<N+2; i++)
if(i>=2)
C[i-2] = g(B[i]);

Loop Merge
for (i=0; i<N+2; i++)
if(i<N)
B[i] = f(A[i]);
if(i>=2)
C[i-2] = g(B[i]);

## Slide 47: Loop Reduce

for I = max(exp1,exp3) to
min(exp2,exp4)
A(I)
for I = exp1 to exp2
if Iexp3 and Iexp4
A(I)

## Slide 48: Loop Body Split
for I = exp1 to exp2
A(I)
B(I)
for Ia = exp1 to exp2
A(Ia)
for Ib = exp1 to exp2
B(Ib)

A(I) must be
single-assignment:
its elements should
be written once

## Slide 49: Loop Body Split: Example as enabler
for (i=0; i<N; i++)
A[i] = f(A[i-1]);
B[i] = g(in[i]);
for (j=0; j<N; j++)
C[j] = h(B[j],A[N]);
for (i=0; i<N; i++)
A[i] = f(A[i-1]);
for (k=0; k<N; k++)
B[k] = g(in[k]);
for (j=0; j<N; j++)
C[j] = h(B[j],A[N]);

Loop Body Split
for (i=0; i<N; i++)
A[i] = f(A[i-1]);
for (j=0; j<N; j++)
B[j] = g(in[j]);
C[j] = h(B[j],A[N]);

Loop Merge

## Slide 50: Loop Reverse
for I = exp1 to exp2
A(I)

for I = exp2 downto exp1
A(I)
for I = exp1 to exp2
A(exp2-(I-exp1))
Or written differently:
Location
Time
Location
Time
Production
Consumption

## Slide 51: Loop Reverse: Satisfy dependencies
No loop-carried dependencies allowed ! Can not reverse the loop
for (i=0; i<N; i++)
A[i] = f(A[i-1]);
Enabler: data-flow transformations; exploit associativity of + operator
A[0] = …
for (i=1; i<=N; i++)
A[i]= A[i-1]+ f(…);
… = A[N] …
A[N] = …
for (i=N-1; i>=0; i--)
A[i]= A[i+1]+ f(…);
… = A[0] …

## Slide 52: Loop Reverse: Example as enabler
for (i=0; i<=N; i++)
B[i] = f(A[i]);
for (i=0; i<=N; i++)
C[i] = g(B[N-i]);
N–i > i  merging not possible

Loop Reverse
for (i=0; i<=N; i++)
B[i] = f(A[i]);
for (i=0; i<=N; i++)
C[N-i] = g(B[N-(N-i)]);
N-(N-i) = i 
merging possible

Loop Merge
for (i=0; i<=N; i++)
B[i] = f(A[i]);
C[N-i] = g(B[i]);

## Slide 53: Lexicographical ordering
Each iteration is a node identified by its n-dim. index vector: p = (p1, p2, …, pn)
Iterations are executed in lexicographic order
For p = (p1, p2, …, pn) and q = (q1, q2, …, qn) p is lexicographically greater than q written as p q
  Therefore iteration p must be executed after q
Example:
    (1,1,1), (1,1,2), (1,1,3), …,
    (1,2,1), (1,2,2), (1,2,3), …,
    …,
    (2,1,1), (2,1,2), (2,1,3), …,
  (1,2,1) (1,1,2) ? (1,4,2) (2,1,1) ?
A little quiz?
Notes: Lexicographical ordering introduced this will be used during the dependency analysis later on.

## Slide 54: Dependence vectors
Dependence vector in an n-nested loop is denoted as a vector: d = (d1, d2, …, dn)
A single dependence vector represents a set of distance vectors
A distance vector defines a distance in the iteration space
Distance vector is difference between target and source iterations:
  d = IT – IS
Notes: Dependence distance introduced. Not always possible can also be a direction vector.

## Slide 55: Example of dependence vector
For(i=0; i<N; i++){
for(j=0; j<N; j++)
A[i,j] = …;
= A[i,j];
B[i,j+1] = …;
= B[i,j];
C[i+1,j] = …;
= C[i,j+1];
A yields: B yields: C yields:
A0,0= =A0,0
B0,1= =B0,0
C1,0= =C0,1
A0,1= =A0,1
B0,2= =B0,1
C1,1= =C0,2
A1,0= =A1,0
B1,1= =B1,0
C2,0= =C1,1
A1,1= =A1,1
B1,2= =B1,1
C2,1= =C1,2
A0,2= =A0,2
B0,3= =B0,2
C1,2= =C0,3
A1,2= =A1,2
B1,3= =B1,2
C2,2= =C1,3
A2,0= =A2,0
B2,1= =B2,0
C3,0= =C2,1
A2,1= =A2,1
B2,2= =B2,1
C3,1= =C2,2
A2,2= =A2,2
B2,3= =B2,2
C3,2= =C2,3
i
j

## Slide 56: Plausible dependence vectors
A dependence vector is plausible iff it is lexicographically non-negative
For(i=0; i<N; i++){
for(j=0; j<N; j++)
.......
Plausible: (1,-1)
Implausible: (-1,0)