## Slide 1: Tricks of the Trade: From Loop Transformations to Automatic Optimization
Maurice Peemen
Henk Corporaal
5SIA0 Embedded Computer Architecture
Notes: Introduce the topic: loops and neste loops, optimize their behavior to better match platform or processor architecture. To improve performance (execution time or/and energy). Finally how to automate these processes

## Slide 2: Application Excecution Time
High performance computing
Embedded computing
Small portions of the code dominate execution time
Hot spots
Loops
Improve the small part
Loop Transformations
for(i=0; i<N; i++){
for(j=0; j<N; j++){
for(k=0; k<N; k++)
c[i][j] += a[i][k] * b[k][j];
}}

## Slide 3: Loop Transformations
Can help you in many compute domains
CPU Code
Parallelism
Memory Hierarchy
Convert Loops to
GPU Threads
Embedded Devices
Fine-tune for architecture
HDL, HW Description Languages

## Slide 4: Loop Transformation Classes
Data-Flow-Based Transformations
Iteration Reordering Transformations
Loop Restructuring Transformations

## Slide 5: Data-Flow-Based Transformations
Can be very useful in case of a:
  Simple compiler
  Simple architecture
    No Hardware Multiplier
    No Out-Of-Order Superscalar
    No Speculative Branch Prediction
  If you are in a hurry and missing a few percent
These are the easy tricks
To get ready for the more difficult ones 
* Examples are from: D.F. Bacon, S.L. Graham, and O.J. Sharp, Compiler transformations for high-performance computing. ACM Comput. Surv. 26, (1994)

## Slide 6: Loop-Based Strength Reduction
Replace an expensive operation
Can be multiplication, especially for embedded cores
No HW multiplier, e.g. MicroBlaze
An optimizing compiler can help
c=3;
for(i=0; i<N; i++){
a[i] = a[i] + i*c;
}
c=3;
T=0;
for(i=0; i<N; i++){
a[i] = a[i] + T;
T = T + c;
}

## Slide 7: Induction Variable Elimination
Induction variable?
  Compute loop exit conditions
  Compute memory addresses
Given a known final value and relation to addresses
  Possible to eliminate index calculations
Again an optimizing compiler can help
A = &a[0];
T = &a[0] + N;
while(A<T){
*A = *A + c;
A++;
}
for(i=0; i<N; i++){
a[i] = a[i] + c;
}
Notes: Performing the control of a loop is basically overhead. I refer to the increment of i and the compare of i<N to check if the exit condition is not met.
With induction variable elimination we can reduce this overhead.

## Slide 8: Loop-Invariant Code Motion
Index of c[] does not change
Move one loop up and store in register
Reuse it over iterations of inner loop
Most compilers can perform this
Example is similar to Scalar Replacement Transformation
for(i=0; i<N; i++){
for(j=0; j<N; j++){
a[i][j]=b[j][i]+c[i];
}
}
for(i=0; i<N; i++){
T=c[i];
for(j=0; j<N; j++){
a[i][j]=b[j][i]+T;
}
}

## Slide 9: Loop Unswitching
Conditional execution in body
Speculative branch prediction helps but
This branch is loop invariant code
  Move it outside the loop
  Each execution path independent loops
Increases code size
for(i=0; i<N; i++){
a[i] = b[i];
if(x<7){a[i]+=5;}
}
if(x<7){
for(i=0; i<N; i++){
a[i]=b[i];
a[i]+=5;
}
}
else{
for(i=0; i<N; i++){
a[i]=b[i];
}
}

## Slide 10: This is only the start
“You take the blue pill - the story ends, you wake up in your bed and believe whatever you want to believe. You take the red pill - you stay in Wonderland and I show you how deep the rabbit-hole goes.”
Morpheus, The Matrix (1999)

## Slide 11: Loop Transformation Classes
Data-Flow-Based Transformations
Iteration Reordering Transformations
Loop Restructuring Transformations

## Slide 12: Iteration Reordering Transformations
Change the relative ordering
  Expose parallelism by altering iteration dependencies
  Improve locality by matching with a memory hierarchy
We need more theory to understand these
Or combine the tricks to form a methodology
Normal compilers don’t help you with this
Only state-of-the-art compilers can help
  Often research compilers ;)
*Based on:
M. Wolf, M. Lam, A Data Locality Optimizing Algorithm. ACM SIGPLAN, PLDI (1991)

## Slide 13: Loop representation as Iteration Space
for(i=0; i<N; i++){
for(j=0; j<N; j++){
A[i][j] = B[j+3][i+2];
Each position represents an iteration
  At each position 1 or more array elements are accessed

## Slide 14: Visitation order in Iteration Space
for(i=0; i<N; i++){
for(j=0; j<N; j++){
A[i][j] = B[j+3][i+2];
Iteration space is not data space

## Slide 15: But we don’t have to be regular
A[j][j] = B[j+3][i+2];
But order can have huge impact
Memory Hierarchy
  E.g. Reuse of data
Parallelism
Loop or control overhead

## Slide 16: Types of data reuse
for i := 0 to 2
for j := 0 to 100
A[i][j] = B[j+1][0] + B[j][0];
Assumptions:
1. Memory layout row mayor
2.Cache line size=4 elements
Notes: Spatial reuse = reuse of neighboring values in cache lines; Temporal reuse = Single value reused at different moment in time;
Group reuse = multiple memory references in the loop body point to the same memory location at different iteration values (temporal) or they point to neighboring values (spatial)

## Slide 17: Types of data reuse
for i := 0 to 2
for j := 0 to 100
A[i][j] = B[j+1][0] + B[j][0];
Notes: Spatial reuse = reuse of neighboring values in cache lines; Temporal reuse = Single value reused at different moment in time;
Group reuse = multiple memory references in the loop body point to the same memory location at different iteration values (temporal) or they point to neighboring values (spatial)

## Slide 18: When do cache misses occur?
for(i=0; i<N; i++){
for(j=0; j<N; j++){
A[i][j] = B[j][i]; // again row major ordering
// assumed

## Slide 19: Optimize array accesses for memory hierarchy
Solve the following questions?
  When do misses occur?
    Use “locality analysis”
  Is it possible to change iteration order to produce better behavior?
    Evaluate the cost of various alternatives
  Does the new ordering produce correct results?
    Use “dependence analysis”
Notes: Introduce theory for memory hierarchy optimization

## Slide 20: Different Reordering Transformations
Loop Interchange
Tiling
Skewing
Loop Reversal
Can improve locality
Can enable above

## Slide 21: Loop Interchange or Loop Permutation
for(i=0; i<N; i++){ for(j=0; j<N; j++){
for(j=0; j<N; j++){ for(i=0; i<N; i++){
A[j][i] = i*j; A[j][i] = i*j;
N is large with respect to cache size
Normal compilers will not help you!
Chart: Execution Time [ms]
| -O0 | -O3
Without | 809.7 | 385
With | 545.3 | 77
Notes: Example to demonstrate the possible locality increase due to interchange

## Slide 22: Tiling the Iteration Order
Result in Iteration Space
for(jj=0; jj<N; jj+=Tj){
for(i=0; i<N; i++){ for(i=0; i<N; i++){
for(j=0; j<N; j++){ for(j=jj; j<jj+Tj; j++){
f(A[i],A[j]); f(A[i],A[j]);
assume
Tj=4
Notes: Example to show the potential locality increase due to tiling

## Slide 23: Cache Effects of Tiling
for(jj=0; jj<N; jj+=Tj){
for(i=0; i<N; i++){ for(i=0; i<N; i++){
for(j=0; j<N; j++){ for(j=jj; j<jj+Tj; j++){
f(A[i],A[j]); f(A[i],A[j]);
assume Tj=4

## Slide 24: Is this always possible?
No, dependencies can prevent transformations
Interchange and Tiling is not always valid!
Example Interchange
  Spatial locality
  Dependency (1,-1)
Should be lexicographically correct
for(i=1; i<N; i++){
for(j=0; j<N; j++){
a[j][i] = a[j+1][i-1] + 1;
}
}

## Slide 25: Lexicographical ordering
Each iteration is a node identified by its n-dim. index vector: p = (p1, p2, …, pn)
Iterations are executed in lexicographic order
For p = (p1, p2, …, pn) and q = (q1, q2, …, qn) p is lexicographically greater than q written as p q
Therefore iteration p must be executed after q
Example:
    (1,1,1), (1,1,2), (1,1,3), …,
    (1,2,1), (1,2,2), (1,2,3), …,
    …,
    (2,1,1), (2,1,2), (2,1,3), …,
  (1,2,1) (1,1,2) ? (1,4,2) (2,1,1) ?
A little quiz?
Notes: Lexicographical ordering introduced this will be used during the dependency analysis later on.

## Slide 26: Dependence vectors
Dependence vector in an n-nested loop is denoted as a vector: d = (d1, d2, …, dn)
A single dependence vector represents a set of distance vectors
A distance vector defines a distance in the iteration space
Distance vector is difference between target and source iterations:
  d = IT – IS
Notes: Dependence distance introduced. Not always possible can also be a direction vector.

## Slide 27: Example of dependence vector
For(i=0; i<N; i++){
for(j=0; j<N; j++)
A[i,j] = …; i
= A[i,j];
B[i,j+1] = …;
= B[i,j];
C[i+1,j] = …;
= C[i,j+1]; j
A yields: B yields: C yields:
A0,0= =A0,0
B0,1= =B0,0
C1,0= =C0,1
A0,1= =A0,1
B0,2= =B0,1
C1,1= =C0,2
A1,0= =A1,0
B1,1= =B1,0
C2,0= =C1,1
A1,1= =A1,1
B1,2= =B1,1
C2,1= =C1,2
A0,2= =A0,2
B0,3= =B0,2
C1,2= =C0,3
A1,2= =A1,2
B1,3= =B1,2
C2,2= =C1,3
A2,0= =A2,0
B2,1= =B2,0
C3,0= =C2,1
A2,1= =A2,1
B2,2= =B2,1
C3,1= =C2,2
A2,2= =A2,2
B2,3= =B2,2
C3,2= =C2,3

## Slide 28: Plausible dependence vectors
A dependence vector is plausible iff it is lexicographically non-negative
Plausible: (1,-1)
Implausible: (-1,0)

## Slide 29: Loop Reversal
  Dependency (1,-1) Dependency (1,1)
Interchange is valid now
for(i=0; i<N; i++){
for(j=0; j<N; j++){
a[j][i] = a[j+1][i-1] + 1;
}
}
for(i=0; i<N; i++){
for(j=N-1; j>=0; j--){
a[j][i] = a[j+1][i-1] + 1;
}
}

## Slide 30: More difficult example
For(i=0; i<6; i++){ D={(0,1),(1,0),(1,-1)}
for(j=0; j<7; j++){
A[j+1] += 1/3 * (A[j] + A[j+1] + A[j+2]);
What are other legal visit orders?

## Slide 31: Loop Skewing
for(i=0 i<6; i++){ D = {(0,1),(1,0),(1,-1)}
for(j=0; j<7; j++){
A[j+1] = 1/3 * (A[j] + A[j+1] + A[j+2]);
for(i=0; i<6; i++){ D = {(0,1),(1,1),(1,0)}
for(j=i; j<7+i; j++){
A[j-i+1] = 1/3 * (A[j-i] + A[j-i+1] + A[j-i+2]);
Notes: Original dependence vector top vs dependence vector bottom

## Slide 32: Enables Tiling
Apply Skew Transformation
Apply Tiling

## Slide 33: Is It Really That Easy ?
No, we forget a few things
Cache capacity and reuse distance
  If caches were infinitely large, we would be finished
For deep loopnests analysis can be very difficult
It would be much better to automate these steps
We need more theory and tools
Cost models

## Slide 34: Data Reuse distance
The number of unique accesses between a use and a reuse is defined as the (data) reuse distance:
( a[0] a[6] a[20] b[1] a[6] a[0] ) => RD (a[0])= 3
* C. Ding, Y. Zhong, Predicting Whole-Program Locality through Reuse Distance Analysis, PLDI (2003)
Second a[0] access is a cache hit if
  Fully associative cache with n=4 entries
  Optimal LRU, least recently used, replacement policy
In general:
  Cache hit if RD < n
  Cache miss if RD ≥ n
We can measure reuse distance with profiling tools:
  Suggestions for Locality Optimization (SLO)
Beyls, K., D'Hollander, E. Refactoring for Data Locality, IEEE Computer Vol. 42, no. 2 2009
Notes: Can be line adresses

## Slide 35: Study a matrix multiplication kernel
Loop interchange
for(i=0; i<Bi; i++){
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
C[i][j] += A[i][k] * B[k][j];
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
for(i=0; i<Bi; i++){
C[i][j] += A[i][k] * B[k][j];

## Slide 36: Loop tiling
Can be done in multiple dimensions
Manual exploration is intractable
for(i=0; i<Bi; i++){
for(j=0; j<Bj; j++){
for(k=0; k<Bk; k++){
C[i][j] += A[i][k] * B[k][j];
for(i=0; i<Bi; i++){
for(jj=0; jj<Bj; jj+=Tj){
for(k=0; k<Bk; k++){
for(j=jj; j<jj+Tj; j++)
C[i][j] += A[i][k] * B[k][j];

## Slide 37: Automate the search
“Never send a human to do a machine’s job.” Agent Smith, The Matrix (1999)

## Slide 38: A Practical Intermezzo
Accelerators for energy efficiency
Special Purpose HW
  ~100x better performance, 100x less energy than CPU
A simple processor for control
Multiple accelerators for heavy compute workload
Easy to develop with current HLS languages

## Slide 39: Bandwidth Hungry
Simple RISC core
Accelerator Operations
Interconnect Resources
Aethereal Interconnect 6 cores

## Slide 40: What can we do?
Exploit the data reuse in accelerator workload
Use local buffers
Reduce communication with external memory

## Slide 41: A Different Approach: Inter-Tile Reuse
But how about
DATA OVERLAP?
Accelerator workload is often static
We know the contents of the next tile
Optimize Iteration Order
Formulate the ordering as optimization problem

## Slide 42: Demosaic Benchmark
Convert an 8 Mpix image: 0.6 GMAC
  Intel-i7 0.56 s
  ARM-A9 5.75 s
  Microblaze 22.10 s
  Accelerator 1.35 s @ 50 MB/s

## Slide 43: Demosaic Benchmark
Convert an 8 Mpix image: 0.6 GMAC
  Intel-i7 0.56 s
  ARM-A9 5.75 s
  Microblaze 22.10 s
  Accelerator 1.35 s @ 50 MB/s

## Slide 44: Demosaic Benchmark
Convert an 8 Mpix image: 0.6 GMAC
  Intel-i7 0.56 s
  ARM-A9 5.75 s
  Microblaze 22.10 s
  Accelerator 1.35 s @ 50 MB/s

## Slide 45: Motion Estimation
H264 video encoder ME ~ 30 Gops
for(frame){
for(macroblocks){
for(reference frame){
for(searchrange){
for(pixel){
SAD_operation();
for(find max){
Store vector();

## Slide 46: Block Matching
H264 video encoder ME ~ 30 Gops
  Intel-i7 8.1 sec
  ARM A9 72.3 sec
  Microblaze 283.9 sec
  Accelerator 3.4 sec @ 50MB/s

## Slide 47: Block Matching
H264 video encoder ME ~ 30 Gops
  Intel-i7 8.1 sec
  ARM A9 72.3 sec
  Microblaze 283.9 sec
  Accelerator 3.4 sec @ 50MB/s

## Slide 48: What do we achieve
Cost models

## Slide 49: Loop Transformation Classes
Data-Flow-Based Transformations
Iteration Reordering Transformations
Loop Restructuring Transformations
  Alter the form of the loop

## Slide 50: Loop Unrolling
Duplicate loop body and adjus loop header
  Increases ILP (Instruction Level Parallelism)
  Reduces loop overhead
  Possibilities for common subexpression elimination
If partial unroll, loop should stay in original bound!
Downsides
  Code size increases, can increase I-cache miss-rate
for(i=1; i<N; i++){
a[i]=a[i-1]+a[i]+a[i+1];
}
for(i=1; i<N-1; i+=2){
a[i]=a[i-1]+a[i]+a[i+1];
a[i+1]=a[i]+a[i+1]+a[i+2];
}
if(mod(N-1,2)==1){
a[N-1]=a[N-2]+a[N-1]+a[N];

## Slide 51: Loop Merge or Fusion
Why?
  Improve locality
  Reduce loop overhead
for(i=0; i<N; i++){
b[i]=a[i]+1;
}
for(j=0; j<N; j++){
c[j]=b[j]+a[j];
}
for(i=0; i<N; i++){
b[i]=a[i]+1;
c[i]=b[i]+a[i];
}
Location
Time
Production/Consumption
Consumption(s)
Location
Time
Production/Consumption
Consumption(s)

## Slide 52: Fusion is not always allowed
Data dependencies from first to second loop
Fusion is allowed if
   I: cons(I) in loop 2  prod(I) in loop 1
Enabling transformations: Bump, Reverse, Skew
for(i=0; i<N; i++){
b[i]=a[i]+1;
}
N-1>=i
for(i=0; i<N; i++){
c[i]=b[N-1]+a[i];
}
for(i=0; i<N; i++){
b[i]=a[i]+1;
}
i-2 < i
for(i=0; i<N; i++){
c[i]=b[i-2]+a[i];
}

## Slide 53: Loop Bump: Example as enabler
for(i=2; i<N; i++){
b[i]=a[i]+1;
}
for(i=2; i<N; i++){
c[i-2]=b[i+2-2]*0.5;
}
i+2 > i => direct merging not possible
i+2-2 = i =>
possible to merge
for(i=2; i<N; i++){
b[i]=a[i]+1;
}
for(i=0; i<N-2; i++){
c[i]=b[i+2]*0.5;
}
for(i=2; i<N; i++){
b[i]=a[i]+1;
c[i-2]=b[i]*0.5;
}

## Slide 54: Automatic frameworks
These are the tools to abstract away from code:
Model reuse (potential for locality)
Local iteration space
Transform loops to take advantage of reuse
Does this still give valid results?
Loop transformation theory
  Iteration space
  Dependence vectors
  Unimodular transformations
  Polyhedral Model

## Slide 55: Tricks of the Trade: Main Take-Aways
Data-Flow-Based Transformations
  Good compilers can help
Iteration Reordering Transformations
  High-level transformations
  Compilers are often not enough
  Huge gains for parallelims and locality
  Be carefull with dependencies
Loop Restructuring Transformations
  Similar to reordering
Tools can help you: Check out SLO
Optimizing source to source compilers as well
  If you are lucky; however don’t support all constructs
  Check out Polyhedral compilers, e.g. Pluto

## Slide 56: Extra Enabler Transformations
Many of these can be very usefull
Especially to enable the bennificial ones:
  Interchange
  Tiling
  Fusion
Often you need combinations to get the job done!
Make sure you can use them all for the:
Data Memory Management Assingment

## Slide 57: Backup
Extra details for several (enabling) loop transformations

## Slide 58: Loop Extend
for I = exp1 to exp2
A(I)

for I = exp3 to exp4
if Iexp1 and Iexp2
A(I)
exp3  exp1
exp4  exp2

## Slide 59: Loop Extend: Example as enabler
for (i=0; i<N; i++)
B[i] = f(A[i]);
for (i=2; i<N+2; i++)
C[i-2] = g(B[i]);

Loop Extend
for (i=0; i<N+2; i++)
if(i<N)
B[i] = f(A[i]);
for (i=0; i<N+2; i++)
if(i>=2)
C[i-2] = g(B[i]);

Loop Merge
for (i=0; i<N+2; i++)
if(i<N)
B[i] = f(A[i]);
if(i>=2)
C[i-2] = g(B[i]);

## Slide 60: Loop Reduce

for I = max(exp1,exp3) to
min(exp2,exp4)
A(I)
for I = exp1 to exp2
if Iexp3 and Iexp4
A(I)

## Slide 61: Loop Body Split
for I = exp1 to exp2
A(I)
B(I)
for Ia = exp1 to exp2
A(Ia)
for Ib = exp1 to exp2
B(Ib)

A(I) must be
single-assignment:
its elements should
be written once

## Slide 62: Loop Body Split: Example as enabler
for (i=0; i<N; i++)
A[i] = f(A[i-1]);
B[i] = g(in[i]);
for (j=0; j<N; j++)
C[j] = h(B[j],A[N]);
for (i=0; i<N; i++)
A[i] = f(A[i-1]);
for (k=0; k<N; k++)
B[k] = g(in[k]);
for (j=0; j<N; j++)
C[j] = h(B[j],A[N]);

Loop Body Split
for (i=0; i<N; i++)
A[i] = f(A[i-1]);
for (j=0; j<N; j++)
B[j] = g(in[j]);
C[j] = h(B[j],A[N]);

Loop Merge

## Slide 63: Loop Reverse
for I = exp1 to exp2
A(I)

for I = exp2 downto exp1
A(I)
for I = exp1 to exp2
A(exp2-(I-exp1))
Or written differently:
Location
Time
Location
Time
Production
Consumption

## Slide 64: Loop Reverse: Satisfy dependencies
No loop-carried dependencies allowed ! Can not reverse the loop
for (i=0; i<N; i++)
A[i] = f(A[i-1]);
Enabler: data-flow transformations; exploit associativity of + operator
A[0] = …
for (i=1; i<=N; i++)
A[i]= A[i-1]+ f(…);
… = A[N] …
A[N] = …
for (i=N-1; i>=0; i--)
A[i]= A[i+1]+ f(…);
… = A[0] …

## Slide 65: Loop Reverse: Example as enabler
for (i=0; i<=N; i++)
B[i] = f(A[i]);
for (i=0; i<=N; i++)
C[i] = g(B[N-i]);
N–i > i  merging not possible

Loop Reverse
for (i=0; i<=N; i++)
B[i] = f(A[i]);
for (i=0; i<=N; i++)
C[N-i] = g(B[N-(N-i)]);
N-(N-i) = i 
merging possible

Loop Merge
for (i=0; i<=N; i++)
B[i] = f(A[i]);
C[N-i] = g(B[i]);

## Slide 66: Loop Interchange
for I1 = exp1 to exp2
for I2 = exp3 to exp4
A(I1, I2)
for I2 = exp3 to exp4
for I1 = exp1 to exp2
A(I1, I2)


## Slide 67: Loop Interchange: index traversal
Loop
Interchange
for(i=0; i<W; i++)
for(j=0; j<H; j++)
A[i][j] = …;
for(j=0; j<H; j++)
for(i=0; i<W; i++)
A[i][j] = …;
i
j
i
j