## Slide 1: Intelligent Architectures 5LIL0 Accelerators for Deep Learning
Kanishkan Vadivel
Henk Corporaal
www.ics.ele.tue.nl/~heco/courses/IA
h.corporaal@tue.nl
TUEindhoven
2022

## Slide 2: Deep ANN => Architecture
Apple’s A15 chip
2 high perf. cores
4 efficient (smaller) cores
Neural Engine (16 proc)
Video encoder / decoder
signal processor
display processor
TPU board

## Slide 3: Topics overview
Introduction
  Architecture choices
  Flexibility vs Energy efficiency
Basic Schedules and Architectures exploiting data reuse
Row stationary mapping
TPU & other Architectures
  Systolic array processing
Summary & Conclusion

## Slide 4: Choices for hardware architecture
SIMD
GPU
CPU
ASIC
VLIW
DSP
Energy Efficiency
FPGA
Flexibility
  Quite flexible
  Low efficiency
  Often lack performance.
  Improve efficiency by giving up some flexibility
  More application specific
  Very efficient
  Not flexible
More efficient due to spatial layout
High static control cost
Paper: How flexible is your computing system, Shihua Huang, Luc Waeijen e.a, Transaction on Embedded Computing Systems (TECS) 2022

## Slide 5: Flexibility has its price
Where does the energy go?
RISC @ 45 nm, 0.9 V
32-bit ADD : 0.5 pJ out of 70 pJ for the ADD instruction => efficiency 1/140
Overall efficiency: 1 / 850 = 0.12 %

## Slide 6: Reduce the price of flexibility: SIMD
Perform more effective work per instruction
Very programmable
1/140 vs 16/180 → 10 times efficiency improvement

## Slide 7: Further improve efficiency
Maximize effective operations
  Minimize load stores: exploit RF data reuse
  E.g. 1/5 (1 instr out of 5) effective vs 9/11 → additional 4 times efficiency increase
~40 times efficiency improvement

## Slide 8: XNOR Neural Engine (Conti e.a., 2018)
BNN architecture
Optimum energy point (22 nm, ResNet-34)
SRAM design: 115fJ/op @ 0.5V
SCM design: 21.6fJ/op @ 0.4V
Vector binary MUL-ADD-Threshold unit
SRAM dominates power!
Notes: Closest match = most close to our architecture in terms of flexibility
Able to change computational order in outer loops (enabled by micro-code)
(See next hidden slide to see which loops)

## Slide 9: XNOR-Neural Engine
Blue loops are hard-wired in XNE, μCode implements the rest
HW
core loop (by accel HW)
HW
initialization
(by accel HW)
Outer loops (in SW)
Outer loops (in SW)

## Slide 10: XNOR code
Micro code for the nested 6 SW loops
  W, x, y and x_major = R/W registers
  TPsquare, TP, nif, nof, w_X_nif, ow_X_nof, zero = R/O registers

## Slide 11: Topics overview
Introduction
  Architecture choices
  Flexibility vs Energy efficiency
Basic Schedules and Accelerators exploiting data reuse
  Output stationary
    NVE: Neuro Vector Engine
  Weight stationary
  Input stationary
Row stationary mapping
TPU and other architectures
  Systolic array processing
Summary and Conclusions

## Slide 12: Schedules exploiting data reuse
Output Stationary (OS)
Weight Stationary (WS)
Input Stationary (IS)
In traditional compute platforms such as CPUs and GPUs, these are “Software Optimization” strategies.
In ASIC world, these can be “Hardware Design” strategy!
- With custom hardware, we can exploit maximum data-reuse
- But we still need “Software tricks” to make it really work
Credits: Tutorial on Hardware Accelerators for Deep Neural Networks, MIT, ISCA 2019

## Slide 13: Output Stationary – Simplified View
Minimizes Psum (Partial Sum) R/W to memory
  Maximize local accumulation
Broadcast/Multi-cast filter weight and reuse activations spatially across the PE array

## Slide 14: 1D Convolution – Output Stationary
*
=
Weights
Inputs
Outputs
R
H
E = H – R + 1

## Slide 15: Output Stationary – 1D Conv Reference Pattern
inputs
filter size
outputs

## Slide 16: Output Stationary – 1D Conv Reference Pattern
[0 reads]

## Slide 17: Output Stationary – 1D Conv Reference Pattern
[E x R reads]

## Slide 18: Output Stationary – 1D Conv Reference Pattern
[ExR reads]

## Slide 19: 1D Output Stationary – Summary
Minimize partial sum Reads & Writes
Local accumulation
Minimizes energy
H inputs
R filter size
E outputs

## Slide 20: 2D Convolution Layer – Output Stationary
Input fmap
H
W
C
X
Output fmap
F
E
M
=
M
weights
R
S
C
Output to be calculated

## Slide 21: 2D Convolution Layer – Output Stationary
Input fmap
H
W
C
X
Output fmap
F
E
M
=
Cycle through weight and input fmap
In example we are calculating M output pixels at once (vectorization)
M
weights
R
S
C
Partial sum
Current calculation

## Slide 22: 2D Convolution Layer – Output Stationary
Input fmap
H
W
C
X
Output fmap
F
E
M
=
M
weights
R
S
C
Current calculation
Cycle through weight and fmap
Partial sum

## Slide 23: 2D Convolution Layer – Output Stationary
Input fmap
H
W
C
X
Output fmap
F
E
M
=
Cycle through weight and fmap
M
weights
R
S
C
Current calculation
Partial sum

## Slide 24: 2D Convolution Layer – Output Stationary
Input fmap
H
W
C
X
Output fmap
F
E
M
=
Move to Next pixel
M
weights
R
S
C
Current calculation
Partial sum

## Slide 25: Variants of Output Stationary: Multiple outputs in parallel

## Slide 26: The Neuro Vector Engine: Output stationary
Programmable
SIMD operations
Deep pipelining
ILP
Locality oriented
The neuro vector engine: Flexibility to improve convolutional net efficiency for wearable vision
Maurice Peemen e.a., DATE 2016

## Slide 27: Convolutional Network Processing
M. Peemen et al. “Inter-Tile Reuse Optimization Applied to Bandwidth
Constrained Embedded Accelerators” DATE 2015

## Slide 28: NVE Operation

## Slide 29: VLIW Programming Model
3x3 Convolution filter
Software Pipelining
Steady state 10 cycles
  16 neighboring 3x3 convolutions
  144 Multiply Accumulate ops
Code reuse with instruction buffer
Steady state
(= loop body)
Loop Prologue

## Slide 30: Topics overview
Introduction
  Architecture choices
  Flexibility vs Energy efficiency
Basic Schedules and Architectures exploiting data reuse
  Output stationary
    NVE: Neuro Vector Engine
  Weight stationary
    CIM: Computation in Memory
  Input stationary
Row stationary mapping
TPU and other architectures
  Systolic array
Conclusions

## Slide 31: Weight Stationary

## Slide 32: Weight Stationary – Reference Pattern

## Slide 33: Convolution Layer – Weight Stationary
Input fmap
H
W
C
X
Output fmap
F
E
M
=
Hold weights
M
weights
R
S
C
Partial sum
Current calculation

## Slide 34: Convolution Layer – Weight Stationary
Input fmap
H
W
C
X
Output fmap
F
E
M
=
Hold weights; move window
M
weights
R
S
C
Partial sum
Current calculation
New partial sum

## Slide 35: Convolution Layer – Weight Stationary
Input fmap
H
W
C
X
Output fmap
F
E
M
=
Hold weights; for all output psum
M
weights
R
S
C
Partial sum
Current calculation
Output partial sums

## Slide 36: Convolution Layer – Weight Stationary
Input fmap
H
W
C
X
Output fmap
F
E
M
=
Load new weight and repeat the same
M
weights
R
S
C
Partial sum
Current calculation

## Slide 37: WS – Simplified View
Notes: Weights stationary at the Processing Elements (PEs)

## Slide 38: WS Example: Computation-in-Memory with Memristor crossbar
Memristors
Built in 2008 in HP Labs
Non-Linear, Two terminal device
Computation-in-memory

## Slide 39: WS Example: TDO-CIM Transparent Detection and Offloading for Computation-in-Memory (DATE 2019)
Crossbar performs Matrix-vector computation in analog domain; ideal for GEMM Kernel (FC layer)

## Slide 40: TDO-CIM - Results
Energy-Delay-Product (EDP)
Improvement = ~612x

## Slide 41: WS Example: NVDLA NVIDIA Deep Learning Accelerator
Open-source Verilog !!
Conv Engine
  sparse weight compression
  Winograd
  weight reuse (in conv buffer)

## Slide 42: Topics overview
Introduction
  Architecture choices
  Flexibility vs Energy efficiency
Basic Schedules exploiting data reuse
  Output stationary
    NVE: Neuro Vector Engine
  Weight stationary
  Input stationary
Row stationary mapping
TPU and other architectures
  Systolic array processing
Summary and Conclusions

## Slide 43: Input Stationary – Simplified view
Unicast Weights and accumulates psum spatially across PE array

## Slide 44: Input Stationary
*
=
Weights (R)
Inputs (H)
Outputs ( E = H-R+1)

## Slide 45: Input Stationary – Reference Pattern

## Slide 46: Input Stationary Example – SCNN, ISCA 2017
Input fmap tiling across PEs
  keep these tiles stationary in each PE
Complete unrolling inside PE
  Creates FxI Cartesian products from F and I compressed fmap and filter vectors
  Maps FxI products to Kc x Ht x Wt partial outputs via XBAR
Sparse CNN Architecture

## Slide 47: Input Stationary Example – SCNN, ISCA 2017
PE Architecture in SCNN
Weight Compression
- Input compression follows similar approach
IxF -> O mapping: Huge overhead calculation based on I and F non-zero indices, F.IxA XBAR to instantly map outputs

## Slide 48: Summary of Stationary Schedules

## Slide 49: Topics overview
Introduction
  Architecture choices
  Flexibility vs Energy efficiency
Basic Schedules and Architectures exploiting data reuse
Row stationary mapping
  Eyeriss architecture
TPU and other Architectures
  Systolic array processing
Summary and Conclusions

## Slide 50: Minimum Costs
Which one is the best solution?
Can we do better than OS, WS, and IS?

## Slide 51: Energy-Efficient Dataflow: Row Stationary (RS)
Maximize data reuse at RF level
Slides based on: Chen e.a.: ISCA 2016

## Slide 52: 1-D row convolution in PE (processing element)

## Slide 64
(Batch)

## Slide 66
(Batch)

## Slide 77: Eyeriss: Deep Neural Network Accelerator
Combining reuse in
on-chip global buffer
  see lecture on data reuse, and
row stationary schedule
  reusing data in the Register files within the PEs

## Slide 78: Topics overview
Introduction
  Architecture choices
  Flexibility vs Energy efficiency
Basic Schedules exploiting data reuse
  Architectures exploiting data reuse
Row stationary mapping
TPU: Tensor Processing Unit
  Systolic array processing
Other Architectures supporting DL
Summary and Conclusions

## Slide 79: Example: Google TPU (Tensor Processing Unit)
TPU v1 (Edge) 2016
TPU Data centre
Based upon: In-Data Center Performance Analysis of a tensor Processing Unit
ISCA 2017, Jouppi, Young, Patil, Patterson, et al.

## Slide 80: Implement large 2D systolic matrix multiplication unit
Systolic Execution to compute data on the fly in buffers
Pipeline control and data
Relies on data from different directions arriving at regular intervals and being combined
X11
X12
X13
W11
W21
W31
W12
W22
W32
*

## Slide 81: Implement large 2D systolic matrix multiplication unit
Systolic Execution to compute data on the fly in buffers
Pipeline control and data
Relies on data from different directions arriving at regular intervals and being combined
X2
X3
W11 X1
W21
W31
W12
W22
W32
*
+

## Slide 82: Implement large 2D systolic matrix multiplication unit
Systolic Execution to compute data on the fly in buffers
Pipeline control and data
Relies on data from different directions arriving at regular intervals and being combined
X3
W11
W21 X2
W31
W12 X1
W22
W32
*
+
+

## Slide 83: Implement large 2D systolic matrix multiplication unit
Systolic Execution to compute data on the fly in buffers
Pipeline control and data
Relies on data from different directions arriving at regular intervals and being combined
W11
W21
W31 X3
W12
W22 X2
W32
+
y1=w11x1+w21x2+w31x3

## Slide 84: Implement large 2D systolic matrix multiplication unit
Systolic Execution to compute data on the fly in buffers
Pipeline control and data
Relies on data from different directions arriving at regular intervals and being combined
W11
W21
W31
W12
W22
W32 X3
y1=w11x1+w21x2+w31x3
y2=w12x1+w22x2+w32x3

## Slide 85: Implement large 2D systolic matrix multiplication unit
Systolic Execution to compute data on the fly in buffers
Pipeline control and data
Relies on data from different directions arriving at regular intervals and being combined
Matrix Matrix Multiply takes more cycles and has better utilization
X11
X12
X13
W11
W21
W31
W12
W22
W32
X21
X31
X22
X32
X23
X33

## Slide 86: High-level Chip Architecture
Matrix Unit: 65,536 (256x256) 8-bit multiply-accumulate units
700 MHz clock rate
Peak: 92 TeraOps/second
    65,536 * 2 * 700M
4 MiB of on-chip Accumulator mem.
24 MiB of on-chip Unified Buffer (activation memory)
8 GiB of off-chip weight DRAM mem.
Two 2133MHz DDR3 DRAM channels

## Slide 87: TPUv1 Chip area breakdown
  Main focus:
    On-chip memory 35%
    Matrix Multiply Unit 24%
  Control is just 2%

## Slide 88: TPUv1 from a programmer’s view
5 main (CISC) instructions:
  Read_Host_Memory
    Reads memory from the CPU memory into the unified buffer
  Read_Weights
    Reads weights from the Weight Memory into the Weight FIFO as input to the Matrix Unit
  MatrixMatrixMultiply/Convolve
    Perform a matrix-matrix multiply, a vector-matrix multiply, an element-wise matrix multiply, an element-wise vector multiply, or a convolution from Unified Buffer into the accumulators
    Takes a variable-sized B*256 input, multiplies it by a 256x256 constant input, and produce a B*256 output, taking B pipelined cycles to complete
  Activate (ReLU, Sigmoid, Maxpool, LRN, …)
    Computes activation function
  Write_Host_Memory
    Writes data from unified buffer into host memory
  Average Clock cycles per instruction: >10

## Slide 89: Relative TPU Performance: 3 Contemporary Chips 2015/2016
Processor | mm2 | Clock [MHz] | TDP [Watts] | Idle [Watts] | Memory GB/sec | Peak TOPS/Chip | 
 |  |  |  |  |  | 8b int. | 32b FP
CPU: Haswell (18 core) | 662 | 2300 | 145 | 41 | 51 | 2.6 | 1.3
GPU: Nvidia K80 (2/card) | 561 | 560 | 150 | 25 | 160 | -- | 2.8
TPUv1 | <331 | 700 | 75 | 28 | 34 | 91.8 | --

## Slide 90: Relative Performance of TPUv1 server
Processor | Chips / Server | DRAM | TDP Watts | Idle Watts | Observed Busy Watts in Datacenter
CPU: Haswell (18 cores) | 2 | 256GB | 504 | 159 | 455
NVIDIA K80 (2 die per card; 4 cards per server) | 8 | 256GB (host) + 12GB x 8 | 1838 | 357 | 991
TPUv1 (1Core) | 4 | 256GB (host) + 8GB x 4 | 861 | 290 | 384

## Slide 91: Roofline Visual Performance Model
2 Limits to performance
Peak Computation
Peak Memory Bandwidth (for apps with large data that don’t fit in chache)
Arithetic Intensity (FLOP/Byte or reuse) determines which limit
Weight-reuse = Arithmetic Intensity for DNN roofline
Samuel Williams, Andrew Waterman, and David Patterson. "Roofline: an insightful visual
performance model for multicore architectures."Communications of the ACM 52.4 (2009): 65-76.

## Slide 92: TPUv1 Die Roofline

## Slide 93: Haswell (CPU) Die Roofline

## Slide 94: K80 (GPU) Die Roofline

## Slide 95: Many benchmark far below roofline, e.g. MLP0
Increase Batch Size = More Weight Reuse

## Slide 96: Combined log rooflines CPU, GPU, TPUv1

## Slide 97: Perf/Watt TPUv1 vs CPU & GPU

## Slide 98: Practical Example: Google TPU v2/v3
TPU v2:
8 GiB of HBM for each TPU core
One MXU for each TPU core
Up to 512 total TPU cores
4 TiB of total memory in a TPU Pod
TPU v3:
16 GiB of HBM for each TPU core
Two MXUs for each TPU core
Up to 2048 total TPU cores
32 TiB of total memory in a TPU Pod

## Slide 99: Topics overview
Introduction
  Architecture choices
  Flexibility vs Energy efficiency
Basic Schedules exploiting data reuse
  Architectures exploiting data reuse
Row stationary mapping
TPU: Tensor Processing Unit
  Systolic array processing
Other Architectures supporting Deep Learning:
  Tensor Streaming Processor (TSP)
  GraphCore
  Cerebras wafer-scale
  Samsung NPU (Neural Processing Unit)
  IBM RaPiD
Summary and Conclusions

## Slide 100: Tensor Streaming Processor: TSP
Conventional Mesh of PEs
Reorganized into sliced vector lanes
Vectorlane
https://dl.acm.org/doi/10.1109/ISCA45697.2020.00023

## Slide 101: Tensor Streaming Processor: TSP
Vertical slices contain 20 units

## Slide 102: Tensor Streaming Processor: TSP
14nm
220 MiBytes SRAM

## Slide 103: GraphCore MK1
The other extreme….
MIMD with 1216 Processors
  256 Kbyte/PE
  no cache
  PE interconnect
  Inter-chip interconnect
MK2 version, see
  https://www.graphcore.ai/products/ipu
  1472 PEs
  900 MB memory
  47.5 TByte/s memory bandwith

## Slide 104: Cerebras Wafer-Scale Integration
Cluster scale DL in a single system
Huge, Not for embedded systems !!!
  23 kW
  850.000 cores
  40 Gbytes on-chip SRAM
  20 petaBytes/s emmory bandwidth
  220 petaBits/s interconnect bandwidth

## Slide 105: Samsung NPU

## Slide 106: Samsung NPU
Exploit input FM sparsity
Weight stationary
Adder trees for inner products
Reconfigurable MAC array
  INT8/INT16 support

## Slide 107: IBM RaPiD
7nm chip with 4 cores:
  25.6 Tflops (FP8)
  102.5 TOPS (INT4)
Per core
  Fused MAC, supporting
    FP16/FP8/INT4/INT2
Supporting:
  range of activation functions
  pooling
  data shuffles
Sparsity-aware dynamic power management

## Slide 108: IBM RaPiD core

## Slide 109
Memory  Energy problem
  how to get DL at the Edge, Everywhere?
Data-reuse is key to achieve very high Energy Efficiency
  Reduce Data Reuse Distance
  Keep data/weights stationary if possible, inside local PE registers
Efficient schedules are needed for Deep Learning Networks
  => Advanced Loop transformations: tiling, interchange, fusion, etc.
Accelerator supporting for these schedules
  CIM: Computing in Memory
  TPU: Systolic (2D) computing, and others
  ASIPs: New class of architecture where HW and SW design are blended!
Hardware capability and Mapping techniques play major role in performance, Energy Efficiency, and Flexibility for DNN accelerators
Many open research questions: check our PARSE website: parse.ele.tue.nl

## Slide 110: Further reading
Recent survey on accelerator design: https://dl.acm.org/doi/pdf/10.1145/3520127